## Slide 1: Liquid Scintillator Purification for Solar Neutrinos
Frank Calaprice
Princeton University

## Slide 2: Low-Background Strategy
Water, Buffers(2) and Scintillator Self-Shielding
  Designed to suppress external backgrounds
  Scintillator and vessel radioactivity are left as the main background sources.
Scintillator Containment Vessel
  Nylon balloon with small mass and low radioactivity.
  Built in low-radon cleanroom to avoid dust and 210Pb (22 yr)
  Expect ~ 1cpd 210Pb due to radon exposure during construction.
  Two nylon vessels motivated by CTF results.
Purification of liquid scintillator
  Pseudocumene (PC) + 1.5 g/l PPO
  Distillation, water extraction, and N2 gas stripping.
  Precision cleaning methods.

## Slide 3
Shielding Against External Background.
  Water: 2.25m
  Buffer zones: 2.5 m
  Outer scintillator zone: 1.25 m

## Slide 4: Special Backgrounds
Radioactive isotopes made by cosmic ray interactions in liquid scintillator:
  12C + m -> 11C +n + m’
  11C -> 11B + e+ + n (t1/2 ~20 min, KE ~1 MeV)
  Ultimate solution: a deeper laboratory such as SNO Lab
  Cuts for positrons and muon produced events.
Mobile radioactivity on liquid scintillator vessel.
  Movement by diffusion or convection of radon and its daughters from scintillator vessel into the fiducial volume.
  210Pb (b, 22 y) -> 210Bi(b, 5 d) -> 210Po (a, 138d)
  Requires clean fabrication of vessel in radon-free cleanroom.

## Slide 5: Radial Distribution of External Background in Stainless Steel Sphere

## Slide 6: Radial Distribution of External Background in Inner Vessel (0.2-0.8 MeV)

## Slide 7: Ideal Purification System
High efficiency to remove impurities.
All parts accessible to “precision cleaning” without dead-ends.
  Mechanical and electro-polished stainless steel minimizes surface area and makes it easier to remove contaminants.
  Turbulent flow and spray balls remove surface contamination well.
  Well-planned cleaning procedure.
Self-cleaning during purification operation removes impurities.
Maintains chemical composition of scintillator
  Solvent, wave-length shifter, other components(?)
A “counting test facility” is very useful measure effectiveness of operations.

## Slide 8: Borexino Scintillator Purification
Distillation
  Separate distillation plants for pseudocumene and PPO.
  Systems are design to reject components with boiling point higher than scintillator. Impurities are left in bottom of the evaporator continuously wasted.
Water Extraction
  transfer of impurities from scintillator to water when two components are mixed thoroughly in a column. Works best to remove polar molecules from scintillator, but works also for less polar species.
  Water and scintillator are immiscible and separate after mixing.
  Water is more dense and flows down column while scintillator flows up.
  Structured packing inside column assures good contact between two fluids.
Nitrogen Stripping
  High purity nitrogen is used in separate volatile components from scintillator. This includes water, and rare gasses, especially 85Kr and 222Rn.

## Slide 9: Scintillator Purification System Distillation, N2 Stripping, Water Extraction @ ~1 ton/hr Precision Cleaned. Assembled in Low-radon Clean Room
4-story tall skid

## Slide 10: Pseudocumene Purification During Filling Operations.

## Slide 11: Solar Neutrino Spectra
Neutrino Energy Spectrum
Neutrino-Electron Elastic Scattering Energy Spectrum
X2 for keV

## Slide 12: Borexino First Spectrum 2007
Note high rate of 210Po a’s: ~ 8000 cpd/100t Note low 210Bi rate: ~15 cpd/100t
The last decays of 222Rn decay chain: 210Pb (22 yr) -> 210Bi (5 d) -> 210Po (138 d) -> 206Pb
How did secular equilibrium get broken so badly? Purification removed 210Pb but not 210Po.
7Be neutrino

## Slide 13: Phase I spectrum with backgrounds
11C
210Po
210Bi
85Kr
CNO

## Slide 14: Phase II
Scintillator Re-purification 2010-2011
  Water extraction
  N2 stripping
Data acquisition 2011-2014.
First direct measurement of pp- neutrinos

## Slide 15: Borexino Re-Purification Systems Water Extraction or Distillation followed by N2 Stripping

## Slide 16: Performance of Scintillator Purification
Distillation system
  Achieved low radioactivity after first purification
    Low level of 210Pb ~ 15 cpd/100t
    ✗ Poor for 210Po: ~ 8000 cpd/100t (Why? From groundwater?)
N2 stripping
  Removed 85Kr during scintillator re-purification.
Water extraction (Re-purification)
  Reduced 238U and 232Th upper chain.
  Moderate reduction of 210Pb
  ✕ Poor removal of 210Po (volatile 210Po in groundwater?)

## Slide 17: Results of Re-purification by Water Extraction
85Kr: 30 cpd/100t → < 5 cpd/100t
238U (226Ra): [(530 ± 50) → < 8 x 10-20 gU/g
214Bi-214Po Reduction factor > 77 (< 0.8 count/100t/yr).
232Th: [(3.8 ± 0.8 → < 1.0] x 10-18 gTh/g
212Bi-212Po Reduction factor > 3. ( < 0.8 count./100t/yr)
210Bi: 70 cpd/100t → 20 ± 5 cpd/100t
210Po: Essentially not reduced!! Volatile 210Po?
Rates before purifcation are based on 153.6 ton-yr exposure taken in 740.7 d between May 16, 2007 and May 8, 2010.

## Slide 18: Borexino Measurements
  ✓ 7Be 46.0 cpd/100t ± 5%. PRL 2011
  8B (> 3 MeV) 0.22 cpd/100t ± 19% PRD 2010
  pep 3.1 cpd/100t ± 22% PRL 2012
  CNO limit: < 7.9 cpd/100t PRL 2012
  pp 144 cpd/100t ± 16% Nature 2014

## Slide 19: 210Bi after Re-purification & CNO
The CNO spectrum is obscured by 210Bi beta decay in scintillator.
  210Bi beta decay = 1.16 MeV
  15O solar n-e max = 1.51 MeV
Strategies to reduce 210Bi:
Measure 210Bi rate from 210Po by secular equilibrium. ✓
  Pule shape discrimination gives clean signal for 210Po alphas.
  Secular equilibrium requires stable detector temperature, to avoid motion of 210Po by convection.
Reduce 210Bi background by scintillator re-purification. ✓

## Slide 20: What’s Next? On-going Efforts with Borexino
Data Analysis:
  4 years of data since scintillator re-purification
  Improve all measurements: pp, 7Be, pep, 8B neutrinos.
  Refine MSW vacuum-to-matter oscillation transition
Detector hardware upgrades for CNO:
  Added thermal insulation to water tank.
    Stabilize temperature to prevent convection currents that move 210Po from vessel surface into fiducial volume.
    The should achieve secular equilibrium in 210Pb-210Bi-210Po sequence.
  Upgrade scintillator re-purification systems.
    Remove 210Bi by water extraction/distillation.

## Slide 21: Science Motivation Borexino Phase III: Precision Solar Neutrino Measurements
Solar Metallicity Problem and CNO
Comparing neutrino and radiant luminosities.
Neutrino physics beyond standard model.

## Slide 22: Temperature & 210Po instabilities
210Po is moved from vessel surface by convection
currents driven by temperature changes. This breaks
secular relationship between 210Bi and 210Po.
210Po non-exponential decay
Seasonal Temperature variations

## Slide 23: Thermal Insulation Rockwool: 20 cm thickness k = 0.03 W/m/K
Before Insulation
During Insulation

## Slide 24: Temperatures 1. Thermal insulation partially complete 2. Water circulation in External Tank turned off
Insulated
Uninsulated
17 C
13 C
15 C
11 C
Water reciculation off
To Rock @ 8 C

## Slide 25: Temperature Profiles Insulation completed early December 2015 Data up to January 2016
Temperatures are continuing to stabilize- Data in analysis, results 2016?

## Slide 26: Upgrade of Water Purification System Reducing 210Pb/210Po from Scintillator
Recent studies show that ground water purified by ion exchange methods has trace concentrations of 210Pb. This can be removed with distillation.
Studies also show that even distillation may not remove 210Po, due to a biological process of micro-organisms in groundwater that produce dimethyl polonium, a volatile compound (B.P. ~ 130 C)
New fractional distillation columns were added to water purification systems.
  More effective removal of 210Pb
  Designed to remove dimethyl polonium (210Po)

## Slide 27: Borexino Water Extraction Systems Original & upgraded systems with 2 new fractional distillation columns Avoiding ground water is also being considered.
Make-up water
system not shown.
Proposed
System
Present
System
Make-up water
system not shown.
Upgraded
System
Original
System

## Slide 28: Summary
Borexino is a unique liquid scintillator detector that achieved an extremely low background and high sensitivity to rare solar neutrino events.
Liquid scintillator purification was a key factor for low background.
Results:
  First direct spectroscopic measurements of all four solar neutrinos in pp fusion reactions, confirming Bethe’s theory of energy production in stars.
  Confirmation of MSW theory of neutrino oscillations.
Strong scientific motivation motivates on-going effort to reduce background for CNO measurement.
Meanwhile, lessons from Borexino inform future experiments on solar neutrinos to search for new neutrino physics and to study the Sun.
Notes: Too many details.
Shorten and highlight future possibilities.

## Slide 29: The End

## Slide 30: Science Motivation Precision Phase of Solar Neutrino Measurements
Solar Metallicity Problem and CNO
  All elements heavier than 4He in the Sun were made before the Sun formed. Their concentrations should be uniformly distributed in Sun, contrary to data that implies lower metallicity in photosphere compared to core.
    CNO rate differs by 30% for high and low metallicity
    An accurate measurement of CNO can clarify the metallicity problem.
Comparison neutrino and radiant luminosities.
    Stability of Sun’s energy output, sterile neutrinos.
    Improve measurement of pp neutrinos to few %.
      Liquid scintillator with low 14C; Liquid xenon dark matter detector (LZ)
Neutrino physics beyond standard model.
  Mapping out vacuum to matter-effect transition, etc.
  See, M. Maltoni and A. Smirnov, “Solar Neutrinos and Neutrino Physics”, arXiv: 1507, 11 Aug. 2015

## Slide 31: The 238U and 232Th Decay Chains
Radon deposits 210Pb (22 yr) which later contaminates scintillator with 210Bi (1 MeV b) and 210Po (5 MeV a).