## Slide 1: European Spallation Source Safety and Licensing Aspects
Peter Jacobsson
Head of Environment, Safety & Health
DOE Workshop on Accelerator Safety Order
Fermi Lab, 2016-09-20--22
www.europeanspallationsource.se
17 September 2016

## Slide 2: Spallation
Spallation: A nuclear process in which a high energy proton excites a neutron rich nucleus which decays sending out neutrons (and other particles such as protons, muons, pions, neutrionos)

## Slide 3: Neutrons are special
Charge neutral
Deeply penetrating
Li motion in fuel cells
Help build electric cars
Nuclear scattering
Sensitive to light elements and isotopes
Actives sites in proteins
Better drugs
S=1/2 spin
probe directly magnetism
Solve the puzzle of High-Tc
superconductivity
Efficient high speed trains

## Slide 4: ESS long pulse potential
Possibilities of pulse shaping
time (ms)
Brightness (n/cm2/s/ster/Å)
7
5
x1014
UK TS1
128 kW
UK TS2
32 kW
US
1.4 MW
Japan
300 kW
ILL 57 MW
ESS 5 MW
2015 design
thermal moderator
0
1
2
3
3
4
1
2
6
λ=1.5 Å
ESS 5 MW
2012 design (TDR)
4
8

## Slide 6: The ESS Site

## Slide 7: Journey to deliver the world’s leading facility for research using neutrons
2014
Construction Starts on Green Field Site
2009
Decision to Site ESS in Lund
2025
ESS Construction Phase Complete
2003
European Design of ESS Completed
2012
ESS Design Update Phase Complete
2019
Machine Ready for
1st Beam on Target
2023
ESS Starts
User Program

## Slide 8: Partner institutions delivering the design & construction of ESS
Institute for Energy Research (IFE)
Institut Laue-Langevin (ILL)
Rutherford-Appleton Laboratory, Oxford(ISIS)
Copenhagen University
Laboratoire Léon Brilouin (LLB)
Lodz University of Technology
Lund University
Nuclear Physics Institute of the ASCR
Oslo University
Paul Sherrer Institute
Roskilde University
Tallinn Technical University
Technical University of Chemnitz
Technical University of Denmark
Technical University Munich
Science and Technology Facilities Council
University of Tartu
Uppsala University
WIGNER Research Centre for Physics
Wroclaw University of Technology
Warsaw University of Technology
Zurich University of Applied Sciences (ZHAW)
Aarhus University
Atomki - Institute for Nuclear Research
Agder University
Bergen University
CEA Saclay, Paris
Centre for Energy Research, Budapest
Centre for Nuclear Research, Poland, (NCBJ)
CERN, Geneva
CNR, Rome
CNRS Orsay, Paris
Cockcroft Institute, Daresbury
DESY, Hamburg
Delft University of Technology
Edinburgh University
Elettra – Sincrotrone Trieste
ESS Bilbao
Forschungszentrum Jülich
Helmholtz-Zentrum Geesthacht
Huddersfield Univesrity
IFJ PAN, Krakow
INFN, Catania
INFN, Legnaro
INFN, Milan

## Slide 9: Accelerator Division – Scope Accelerator Technical performances
Design Drivers:
High Average Beam Power 5 MW
High Peak Beam Power 125 MW
High Availability
Key parameters:
    -2.86 ms pulses
    -2 GeV
    -62.5 mA peak
    -14 Hz
    -Protons (H+)
    -Low losses
    -Minimize energy use
    -Flexible design for mitigation and future upgrades
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz
RF sources for HB part is the scope contingency for accelerator
First beam at 572 MeV in June 2019
5 MW capacity for 2023

## Slide 10: Accelerator Collaboration - Accelerator
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz

## Slide 11: Target Project Scope
Generate neutrons via the spallation process using protons produced by the accelerator
Slow the neutrons to speeds useful for neutron scattering
Direct neutrons to neutron scattering instruments
Safe, reliable operation with high availability
Proton Beam Transport Hall
Target Monolith
Utilities
High Bay
Active Cells

## Slide 12: Target
Target Material; Tungsten (W)
Rotating wheel, He cooled
Pre-Moderator; H2O
Moderator; H2 (l)
Reflector; Be
Proton Beam Window; Al

## Slide 13: Target Components in Monolith
Proton beam instrumentation plug
Proton beam window
Moderator and reflector plug
Target wheel
Neutron beam extraction
Target monitoring plug
Target drive housing
Safety valve
Neutron beam window
Shutter
Protons
Neutrons

## Slide 14: Legal Aspects and Permits
Environmental Code
  Permissibility for construction & operation; 2014-06-12
Radiation Safety Protection Act
  Permit for Construction (step 1), 2014-07-17, revised 2015-07-01
  Permit for Installation (step 2)
  Permit for Commissioning (step 3)
    Permits given for different levels of beam power and production of neutrons.
  Permit for permanent operation (step 4)
  Permit for Decommissioning (step 5)
Planning & Building Act
  Detailed Plan, 2013
  Building Permit, 2014 and onwards
    Permits to be given as a graded approach, building by building
Civil Protection Act
  Working group with the The Regional County Board and the Local Fire Brigade, continuous work
National Heritage Act
  Field archeological investigation finalized 2013

## Slide 15: Graded approach SSM - Schedule
General and conceptual information, enabling SSM to set the requirements
Permit and conditions for building a spallation source
Permit for installation of equiipment and first commissioning of LINAC
Permit for test operation
Permit for permanent operation
Permit for De-commissioning
Reports and analyses showing that ESS is expected to fulfill the requirements
Experience from test operation and maintenance incorporated in verifying analyses
Reports and analyses verifying that ESS fulfills the requirements
Experience from operation incorporated in the de-commissioning plan
1
2
3
4
5
ESS
SSM
Phase
2014
PSAR 2016-05-01
PSAR 2012 + amendments
SAR 2018
Ground break
Installation of Equipment
Neutron production
Operation
2025 - 2065
Decom
2065-2070
FSAR
2017
2019
SAR-Decom
2025
2065

## Slide 16: Reference values for ESS
Event Class | Frequency (/y) | Public Dose (mSv) SSM | Public Dose (mSv) ESS GSO
H1 | > 1 | 0,1 (/y) | 0,05 (/y)
H2 | 1 – 10-2 | 0,1 | 0,1
H3 | 10-2 – 10-4 | 1 | 1
H4 | 10-4 – 10-6 | 20 | 20
H5 | 10-6 – 10-7 | 100 | 100

## Slide 17: Application #2
ESS apply for the step “installation” (for equipment that can generate ionisation radiation) and “commissioning” of the accelerator for an energy up to 75 MeV (warm LINAC).
The application consists of:
  Preliminary Safety Analysis Report, PSAR (350 pages)
  Reference documents to the PSAR (300 documents)
  Status Report
  Self Assessment Report (incl. app.)
In all, the paper versions cover roughly 20 binders

## Slide 18: ESS Schedule - Permit
Complement Information expected
Machine ready for first beam on Target
Application #3
Application #2
Accelerator Readiness Review
First installations on-site (Accelerator)
First commissioning of Accelerator
Permit #2
Permit #3
Q3 2016
Q4 2016
Q1 2017
Q2 2017
Q3 2017
Q4
2017
Q1
2018
Q2 2018
Q3
2018
Q4
2018
Q1
2019
Q2
2019
Q3
2019
Q4
2019
Q1
2020

## Slide 19: Accelerator Safety - Specific
Shielding/Berm Thickness
  Prompt radiation/Skyshine
  1 W/m beam loss
  Accident scenarios
Fire Safety
  Potential fire in the accelerator tunnel – Emergency exists
  Ventilation strategy
ODH
  Simulations of He2 release in the tunnel
Electrical hazards

## Slide 20: Safety Challenges
ESS is a true green-field project. There is not a host Laboratory able to supply the project with services
Design
  Specific requirements for civil construction (external loads) have been challenging for the construction team
  The specific target design is new technology
An aggressive time schedule
Installation
  A large number of in-kind partners will be at site for installation at the same time as the construction company. Parallel activities will occur.
Commissioning of the machine
Starting a scientific operation (gives ESS money)

## Slide 21: Positive factors - Safety
We are a green-field project.
  We do not have any luggage with us
  Everyone at ESS has the same goal
  Large Enthusiasm
Good communication with the authorities
  SSM
  Fire Brigade/Lund Municipality
  Local County Board
Extremely positive response from the science facility network in Europe, US and Japan.

## Slide 22
Civil construction groundbreaking
September 2014

## Slide 23: Progress in 18 months…
August
March 2016