## Slide 1
EBS project at the ESRF: safety challenges
Paul Berkvens
2016 DOE Accelerator Safety Workshop
Fermilab, 20 – 22 September 2016

## Slide 2: Ebs project at the esrf: safety challenges
Contents
Short introduction to the ESRF
EBS project
Decommissioning of existing storage ring
EBS project: general safety challenges
EBS project: radiation protection challenges

## Slide 3: ESRF: short introduction
A research facility unique worldwide
6,500 scientific visitors every year including 4,000 users
2,000 proposals per year: 900 accepted, 1,550 experimental sessions
30% of the research involves industrial developments
Scientific excellence recognised worldwide
N ◦ 1 in scientific output
N ◦ 2 in number of users
N ◦ 1 in reliability & quality
4 Nobel prize-winners among the ESRF users
25,166 reference articles during the period 1994-2014
̴ 30 articles in Nature and Science per year
Nearly 2,000 publications per year: ̴ 5 every day
European Synchrotron Radiation Facility
3rd generation high energy synchrotron radiation facility
6 GeV storage ring
31 public beamlines
12 CRG beamlines

## Slide 4: ESRF: short introduction
13 Member states:
France 27,5 %
Germany 24 %
Italy 13,2 %
United Kingdom 10,5 %
Russia 6 %
Benesync 5,8 %
(Belgium, The Netherlands)
Nordsync 5 %
(Denmark, Finland, Norway, Sweden)
Spain 4 %
Switzerland 4 %
8 Associate countries:
Israel 1,5 %
Austria 1,3 %
Centralsync 1,05 %
(Czech Republic, Hungary, Slovakia)
Poland 1 %
Portugal 1 %
South Africa 0,3 %
Contribution to the budget in %
21 partner nations
Annual budget: 100 million euros
Members of staff: 630 of 40 different nationalities
Legal status: Private civil company subject to French law

## Slide 5: ESRF Radiation PROTECTION POLICY
ALARA principle: nobody at ESRF should be considered as exposed worker.
 In all accessible areas during operation: guarantee non-exposure limit (1 mSv/y)
Guaranteed by:
  Shielding
  Personnel Safety Systems
  Interlocked radiation monitors:
    64 neutron monitors on storage ring roof
    1 ionisation chamber per optics hutch

## Slide 6: ESRF UPGRADE: EXTREMELY BRILLIANT SOURCE PROJECT
Parameter | Existing Lattice | New Lattice
Energy, E [GeV] | 6.04 | 6.04
Circumference, C [m] | 844 | 844
RF frequency, fRF [MHz] | 352 | 352
Beam current [mA] | 200 | 200
Horizontal Emittance [pm ·rad] | 4000 | 150
Vertical Emittance [pm ·rad] | 4 | 3
Beta at ID center, βx , βy [m] | 37.6 , 3.0 (high β) 0.35 , 3.0 (low β) | 3.6 , 3.6
Beam size at ID center, σx , σy [μm] | 413 , 3.9 (high β) 50 , 3.9 (low β) | 24 , 3.3
Beam div. at ID center, σx’ , σy’ [μrad] | 10 , 1.3 (high β) 107, 1.3 (low β) | 6.4 , 0.91

## Slide 7: ESRF UPGRADE: EXTREMELY BRILLIANT SOURCE PROJECT
now

## Slide 8: Decommissioning of the existing storage ring
magnets | 511,360 kg iron |  |  | cables | 186 km | 
 | 82,240 kg copper |  |  |  |  | 
 |  |  |  | cable trays | 9 km | 
vacuum vessels | 9,600 kg stainless steel |  |  |  |  | 
 | 800 kg aluminum |  |  | 160 supports |  | 

## Slide 9: Decommissioning of the existing storage ring
q
Decommissioning of the existing storage ring has to be done within the French legal framework: absence of clearance levels.
Revised technical study sent to ASN, March 2016
Proposed criteria for radiological classification of accelerator components
Detailed activation calculations of standard cell
Measurement protocols for different components
Reply from ASN expected mid 2017

## Slide 10: Decommissioning of the existing storage ring
Monte Carlo simulations:
FLUKA
Process knowledge:
Beam loss distributions
Injected charge history

## Slide 11: Decommissioning of the existing storage ring
Bq/g
Total specific activity (all isotopes), integrated over all z
Cooling down time = 1 month
sum
Sum specific activity/EU clearance level, integrated over z = [890 cm, 900 cm]

## Slide 12: Decommissioning of the existing storage ring
Proposed classification criterion
Indistinguishable from background
(Compliance with the clearance levels defined in the Council Directive 2013/59/EURATOM)
0
y*
3.1·u(y0)
y#
3.1·u(y#)
b = a = 1·10-3
net count rate
count rate distributions
NF ISO 11929 standard, May 2010
Detector:
Exploranium Gr-130 miniSPEC
(1.5” × 1.5”× 2” NaI(Tl) scintillator)
Decision threshold: 2.7 nSv/h
Detection limit: 4.5 nSv/h
(for 30 nSv/h background)

## Slide 13: Decommissioning of the existing storage ring
Equivalence between classification criterion and compliance with the clearance levels defined in the Council Directive 2013/59/EURATOM
Surface dose measurements (indistinguishable form background)
guaranteed for 1 cm3 hotspots.

## Slide 14: Decommissioning of the existing storage ring
Proposed criterion
Only a few vacuum vessels should be considered as activated.
Σi(ASi/SEi)
100 % local losses

## Slide 15: Decommissioning of the existing storage ring

## Slide 16: General safety challenges related to EBS project
Intensive handling activities:
  Removing existing storage ring with 6 T overhead cranes.
    Securing crane operators when storage ring tunnel roof open.
  Installation of new storage ring:
    12 T preassembled girders require specific transport / lifting tools.
    Smaller items installed using 6 T overhead cranes.
Confined space inside storage ring tunnel
Tight schedule
  Dismantling planned in two 8 hours shifts / day
  Intensive use of contractors on site
Since beginning 2016:
  Weekly installation meetings to define:
    Detailed planning,
    Safe work methods.
  Participation of Safety Group to weekly meetings.

## Slide 17: EBS project: radiation protection framework
1st discussions with ASN:
  Upgrade should not be considered as new facility but as a modification of an existing facility.
  Authorisation request to be submitted to ASN mid 2017
  Radiation exposure should be as low as for present facility
   Aim ESRF: - Dose constraint: 1 mSv/y  800 mSv/y (2 mSv/4 h  1.6 mSv/4 h)
- Commissioning period: maintain non-exposure status
          Limit access to experimental hall to staff and long-term contractors
          Guarantee monthly non-exposure limits
Compliance with Council Directive 2013/59/EURATOM

## Slide 18: EBS project: shielding assessment
Purpose: assessment of "normal exposure” and verify compliance with dose constraint.
2013/59/EURATOM : "normal exposure” means exposure expected to occur under the normal operating conditions of a facility or activity (including maintenance, inspection, decommissioning), including minor incidents that can be kept under control, i.e. during normal operation and anticipated operational occurrences.
Major challenge:
  maximum beam losses × 10 use existing bulk shielding
   install few beam loss collimators + local shielding
 |  | Lifetime (h) |  | Beam losses (e/s) | 
Beam mode | Stored current (mA) | Present lattice | EBS lattice | Present lattice | EBS lattice
Multi-bunch | 200 | 45 | 19.3 | 2.2 107 | 5.1 107
16 bunch | 92 | 16 | 1.8 | 2.8 107 | 2.5 108
4 bunch | 40 | 9 | 1.2 | 2.2 107 | 1.6 108

## Slide 19: ebs project: shielding assessment
FLUKA model of EBS storage ring
FLUKA model of optics hutch
Shielding study: need for
  realistic geometry
  realistic beam losses

## Slide 20: Electron Beam loss distribution
beam loss distribution along storage ring
beam loss per unit cell (% of total losses)
unit cell number
collimator location:
between QF4E and SD1E
Matlab Accelerator Toolbox
 Module developed for Touschek losses:
6 dimensional phase space distribution of lost electrons

## Slide 21: Electron Beam loss distribution: example unit cell number 10
y (m)
y' (rad)
x (m)
x' (rad)
beam loss distribution within unit cell
cumulative beam losses within unit cell
for each unit cell: 6 dimensional phase space distribution of lost electrons

## Slide 22: Beam loss collimator: principle design
thickness [cm]
# neutrons × energy [GeV/e-]
10-1
10-2
10-3
40
30
20
10
0
thickness [cm]
# photons × energy [GeV/e-]
photons
neutrons
101
100
10-2
10-3
10-4
10-6
40
30
20
10
0
10-1
10-5

## Slide 23: Collimator shielding tungsten collimator
mSv/h
0.4
effective dose rate (mSv/h)
cm
total
neutrons
0.4 mSv/h

## Slide 24: Collimator shielding 50 cm steel local shielding
mSv/h
0.4
effective dose rate (mSv/h)
0.4 mSv/h
cm
total
neutrons

## Slide 25: Beam loss collimator
Engineering design of collimator is being finalised.
Next steps:
  Modeling collimator in FLUKA
  Design local shielding
  Activation calculations

## Slide 26: Shielding assessment
2013/59/EURATOM : "normal exposure” means exposure expected to occur under the normal operating conditions of a facility or activity (including maintenance, inspection, decommissioning), including minor incidents that can be kept under control, i.e. during normal operation and anticipated operational occurrences.
Normal losses
  Verify that effective dose rates are << 0.4 mSv/h (1.6 mSv / 4h)
Minor incidents
  Stored beam losses: estimate probability, assess dose
  Injected beam losses
    Assess integrated dose per 5 nC booster pulse (6 GeV, 5 mA, 1 ms)
    Verify doses are kept under control via interlocked radiation monitors
      Dose / booster pulse < 1.6 mSv
      Validate number / location of interlocked dose monitors

## Slide 27: Normal beam losses: 92 mA, 1.8 h lifetime – 1 % local loss per cell
mSv/h
0.4 mSv/h
beam height
above roof
total effective dose rate (mSv/h)
cm

## Slide 28: STORED BEAM incident: 200 mA lost on closing gate valve
mSv
total dose
neutrons
1.6 mSv
cm
total effective dose (mSv)

## Slide 29: Injected beam incidents: 5 nC injected on closed gate valve
mSv
beam height
above roof
cm
total effective dose (mSv)

## Slide 30: Injected beam incidents: 5 nC injected with DQ1B magnet off
mSv
beam height
above roof
cm
total effective dose (mSv)

## Slide 31: Storage ring Vacuum conditioning - 1 A.h – 200 mA
mbar
mm
cm
mSv/h
beam height
0.4 mSv/h
average pressure @ 200 mA: 7.5×10-7 mbar
Initial vacuum conditioning of storage ring
After 1 A.h of conditioning:
  Total dose rate outside walls: 0.7 mSv/h
  Total dose rate above roof: 1 mSv/h
   Radiation protection will not be an issue for the storage ring commissioning
total effective dose rate (mSv/h)

## Slide 32: Beamline commissioning - 1000 A.h – 200 mA
mbar
mm
cm
mSv/h
beam height
0.4 mSv/h
average pressure @ 200 mA: 4×10-9 mbar
Beamline commissioning
After 1000 A.h of conditioning:
  Outside ID optics hutch: 0.75 mSv/h
  Outside BM optics hutch: 0.025 mSv/h
   Vacuum conditioning needs to be reassessed.
effective dose rate (mSv/h)

## Slide 33: Many thanks for your attention