## Slide 1
Karie Badgley
53rd Annual Users Meeting
August 12, 2020
Applied Physics and Superconducting Technology Division
M. Murphy
http://td.fnal.gov

## Slide 2: APS-TD Mission
Pursue highly innovative R&D program in superconducting magnets and SRF for accelerators and quantum technology to advance the lab’s scientific mission and to help in defining the lab’s future direction
Operate accelerator test facilities to maximize the lab’s scientific productivity and impact
Develop and build next generation accelerators and detectors using cutting-edge technologies
Educate and train the next generation of physicists and engineers
Wilson
APS-TD
Machine Shop

## Slide 3: Departments and Projects
Programs and Projects
PIP II
LCLS-II
High Luminosity LHC Accelerator Upgrade Project (HiLumi AUP)
Mu2e
SRF Program
Magnet Development Program
Accelerator Support
R&D
Superconducting RF R&D
Superconducting Magnet R&D
Quantum Technologies
Departments
SRF Department
Magnet Systems
Cryogenics
Machine shop
Test & Instrumentation
Quality & Materials
Talk by Lidija Kokoska
Talk by Farah Fahim
Talk by Manolis Kargiantoulakis
Talk by Sarah Demers
Talk by Sarah Demers

## Slide 4: Departments and Projects
Programs and Projects
PIP II
LCLS-II
High Luminosity LHC Accelerator Upgrade Project (HiLumi AUP)
Mu2e
SRF Program
Magnet Development Program
Accelerator Support
R&D
Superconducting RF R&D
Superconducting Magnet R&D
Quantum Technologies
Departments
SRF Department
Magnet Systems
Cryogenics
Machine shop
Test & Instrumentation
Quality & Materials

## Slide 5: Decadal SRF and Magnet R&D Roadmaps
In last few years, US magnet and RF communities have developed “roadmaps” to carefully evaluate R&D directions for the next decade
Goal is to continue to provide frontier accelerator-based physics for years to come

## Slide 6: Superconducting RF Cavities R&D
FNAL R&D – benefits range of initiatives from Energy Frontier to Intensity Frontier to Basic Energy Science and to Quantum Information Science
Frontier projects which build upon our SRF facilities + experience include the following: PIP-II, LCLS-II, LCLS-II HE, HL-LHC AUP
Highlights from FY20 R&D:
  First ever Nb3Sn-coated 9-cell cavity – key technical demonstration for accelerators for industry, universities, and beyond
  Breakthrough in understanding oxygen diffusion mechanism in Nb for reaching very high gradients – impact to all high gradient cavity applications
Nb3Sn 9-cell cavity: world record accelerating gradient for a non-niobium multicell cavity!
HEP + BES

## Slide 7: LCLS-II and LCLS-II-HE
LCLS-II work at Fermilab is nearing completion
  Finishing testing with a schedule to ship remaining 3.9 and 1.3 GHz cryomodules to SLAC by Feb 2021
  A 3.9 GHz CM is going through extended testing to gain experience with its low level RF control system
LCLS-II-HE Fermilab scope has building 10+ 1.3 GHz CMs including designing and building an SRF gun for the second injector line
  Successful transfer of protocols to industry with four vendor cavities completed and others under testing
  The corresponding verification cryomodule on schedule for fabrication and testing in FY21.
HEP + BES
Upgrade of the Linear Coherent Light Source at SLAC
https://lcls-ii.fnal.gov/

## Slide 8: Research towards an ILC
SRF R&D for ILC focused on achieving high gradient (40-50 MV/m) and quality factor (Q > 1010)
A FNAL cavity was sent around the world (KEK, JLab, DESY, Cornell) for cross-verification of its performance
Work is ongoing for preparation of a > 40 MV/m cryomodule demonstration at FNAL
JLab, Cornell, KEK, Saclay, DESY, TRIUMF will join this effort with in-kind contributions
ILC Spec
f=1.3GHz
T=2K

## Slide 9: Magnet R&D: 15 T Dipole (MDPCT1) (A. Zlobin, I. Novitski et al.)
MDPCT1 design features:
60 mm aperture, 1 m long graded 4-layer Nb3Sn dipole coil
600 mm diameter innovative support structure
Towards the limit of the Nb3Sn accelerator magnet technology
Magnet Dipole Prototype Cos-Theta type 1

## Slide 10: Magnet R&D: 15 T Dipole Test (A. Zlobin, I. Novitski et al.)
1. 1st test – May-July 2019
Test target: Bmax=14 T
Bmax =14.1 T @4.5K – the world record field for accelerator magnets!
2. August 2019-February 2020
magnet re-assembly with improved coil axial support and higher pre-stress
3. 2nd test – May-July 2020
Reached the conductor limit
Bmax=14.5 T @1.9K – the new world record field for accelerator magnets!
The world record field for accelerator magnets is now at Fermilab!

## Slide 11: R&D: Quench Current-boosting Device (QCD)
Has the potential to accelerate training by “skipping” intermediate current quenches
Capacitor based device with 0.4 F banks (upgradable)
Boost the quench current through SC magnet to higher levels at quench detection
To be tested on a single coil (“mirror magnet”) first
(simulations)
CIs: Maria Baldini, Sandor Feher
Expert support: Matt Kufer, Howie Pfeffer,Chris Jensen
Stoyan Stoynev
Status
Started in April 2019
Component optimization work on the device completed, components ordered but long lead times
Preparations for mirror magnet assembly started
Main components purchased and work on individual parts done, assembly toward the end of the year

## Slide 12: R&D: Quench Antenna (QA)
Use intersection of determined quench angle/x-position from each of the two panels to locate quench
Stoyan Stoynev, Joe DiMarco
Induction loop quench antennas
Design and fabricate sheet-like flexible multi-channel devices - senseSkins
Grid-like and “pixelized” (point-like QA sensors) versions
Fit for “warm” and “cold” bore operations specifically for VMTF
  becoming part of this FNAL testing facility
Coil-specific versions in addition

## Slide 13: Nb3Sn Composite R&D Goals and Progress
Correlate Conductor Properties with Magnet Performance
Identify signatures for quench Initial
Quantify Energy Release events in real loading conditions
Develop Techniques for enabling different classes of magnet impregnation systems
Use the above to develop insulation systems that reduce or eliminate magnet training
  Build quiet magnets, eliminate training
Energy Spectrum during sample testing: Use this to target quench mitigation actions
Load and acoustic data: Enabling quantification and measurement of behavior in magnet like configuration
Sample demonstrating techniques for enabling highly viscous resins
Thermal Shock sample demonstrating poor thermal shock resistance
New Resins have been demonstrated to have twice the shear strength with respect to baseline and substantially better thermal shock performance
K. Badgley | 53rd Annual Users Meeting | APS-TD

## Slide 14: Nb3Sn - Superconductor R&D: X. Xu et al.
Accelerator magnets for Future Circular Collider (FCC)-hh: will be based on Nb3Sn conductors
A grand technical challenge for FCC-hh: critical current density (Jc) of state-of-the-art Nb3Sn has plateaued for ~2 decades, but 50% below FCC specification
R&D in Fermilab: developing new-generation Nb3Sn using artificial pinning center (APC) technology
Current Status: achieved new record Jc, surpassed the FCC specification!
Other R&D on Nb3Sn conductors: enhance specific heat for stability
Supported by X. Xu Early Career Award
X. Xu et al., Patent # 9916919, 2018

## Slide 15: U.S. HL-LHC AUP
APS-TD plays a key role in the fabrication and test of:
MQXF Nb3Sn low β quadrupoles
RFD Crab Cavity
U.S. High-Luminosity LHC (HL-LHC) Accelerator Upgrade Project (AUP)

## Slide 16: Nb3Sn low β quadrupoles (MQXFA): status
Rutherford cable
HL-LHC AUP Coil Fabrication at FNAL
Efficient coil production ramping up
 (out 49) Coils completed or in production
Target: 132.6 T/m
- 150mm aperture, 11.4T Bpeak
Q1/Q3 (by AUP)
2 magnets MQXFA with 4.2m
  Series:20 magnets
Q2a/Q2b (by CERN)
1 magnet MQXFB with 7.15m
  Series:10 magnets

## Slide 17: AUP Cold Mass Production
New expansion, ICBA, to host cold mass and cryostating for AUP
Production will last ~ 4 years
Tool Crib
Production Floor
Lift Fixture

## Slide 18: Mu2e Solenoids
Testing and assembly of Transport solenoids in HAB
  12 of 14 units at FNAL!
  Cold testing complete on TSU
Production and Detector Solenoid being fabricated at General Atomics
  2 of 3 PS solenoids wound, starting the last winding
  3 of 11 DS solenoids wound
Winding PS2
DS 10 Shell
TS Assembly in HAB
PS
DS
TSD
TSU
https://mu2e.fnal.gov/

## Slide 19: Cryogenic Capabilities
APS-TD supports the laboratory helium cryogenic engineering and operational requirements
4.5 K Facilities
  Physics experiments
  Test facilities for project support
2 K Facilities
  Accelerator test beams
  Test facilities for project support
  Future PIP-II superconducting linac
mK Facilities
  Quantum computing
  Astrophysics
  Detector development

## Slide 20: Cryogenic Capabilities
APS-TD supports the laboratory helium cryogenic engineering and operational requirements
4.5 K Facilities
Engineering and operational experience developed with the groundbreaking 20 kW Tevatron cryogenic system which operated for over 25 years
  Earned the ASME International Historic Mechanical Engineering Landmark
Muon Campus
  Muon g-2
  Mu2e
Current systems have capabilities up to 2,500 W refrigeration and 350 liter/hour liquefaction
Distribution box Mu2e
Feedbox Mu2e

## Slide 21: Cryogenic Capabilities
APS-TD supports the laboratory helium cryogenic engineering and operational requirements
2 K Facilities
  Supports superconducting magnet and RF cavity development and application
mK Facilities
  Supports astrophysics experiments, quantum computing and quantum detector development
Future PIP-II Cryoplant
  2,500 W at 2 K
LHC high luminosity magnet test stand
Quantum Computing Lab
SuperCDMS

## Slide 22: Machine Shop
Serving FNAL experiments
and operations along with other Labs
Provides high tolerance rapid prototype
and small run machined parts along with
radioactive (Class 1) work
Certified welding processes
  SMAC – (Arc)
  GMAW – (Mig)
  FCAW – (Flux-Core)
  GTAW – (Tig)
  PAW – (Plasma Arc)
  And others
Niobium Cavity Machining
Cavity Undressing

## Slide 23: Concluding Remarks
SRF and Magnet R&D
  World record accelerating gradient for a non-niobium multicell cavity
  World record field for accelerator magnets
  World record Jc for Nb3Sn superconductor
LCLSII work nearing completion
HL-LHC AUP quadrupoles in production ~20 of 49 complete
Mu2e Solenoids making progress, DS/PS in production, 12 of 14 TS Units at FNAL
Apologies to the numerous activities in APS-TD not covered
Thank you to all who provided material for this talk!

## Slide 25: RFD crab cavities: status
RFD-LARP-001 has been successfully tested at FNAL, after undergoing full processing at APS-TD and ANL facilities
Rotational BCP tool for RFD cavity
RFD HPR and Cleanroom Assembly
RFD cavity 600 C and 120 C heat treatments
RFD-LARP-001 Q vs Vt, exceeding requirement for HL-LHC
(Nominal: 3.4 MV, Acceptance: 4.1 MV)
Processing and Facilities validation is complete
  New rotational Bulk & Light BCP
  600 C degassing and 120 C bake
  HPR and clean assembly
  VTS test