Therapy & ThorEA,
FFAG & RCS:
Common Challenges
Steve Peggs, BNL & ESS-Scandinavia
With special thanks (and no further attribution) to:
R. Barlow, M. Blaskiewicz, J. Escalier, J. Flanz, Y. Kadi, E. Keil, T. Linnecar,
M. Lindroos, S. Machida, B. Parker, K. Peach, D. Trbojevic, A. Zaltsman.

---
Therapy accelerators
LOW power LOW energy

---
Swept frequency cyclotrons
1980's	Design studies confirm 1/B3 scaling of SC cyclotrons, but leave synchrocyclotrons (swept RF frequency) out of reach.
ACCEL Superconducting	COMET (below): 80 tons, 3 m dia.
250 MeV protons with markedly better extraction efficiency

---
Rapid Cycling Medical Synchrotron
Racetrack design
2 super-periods
Strong focusing minimizes the beam size
FODO/combined function mags with edge focusing
2x7.6m straight sections, zero dispersion, tune quads
Working tunes: 3.38, 3.36
Compact footprint
Circumference: 27.8 m
Area: 37 sq m

---
Required rep rates?
What rates do current “point-and-shoot” slow extraction facilities deliver?
PSI	50 Hz	(Med. Phys. 31 (11) Nov 2004)
20 to 4,500 ml per treatment volume
1 to 4 fields per plan
200 to 45,000 Bragg peaks per field
3,000 Bragg peaks per minute
few seconds to 20 minutes per field
MDACC ~70 Hz	(PTCOG 42, Al Smith, 2005)
10x10x10 cm tumor treated in 71 seconds
22 layers, 5,000 voxels

---
Clinical requirements
Easy to operate
– environment is very different from a national lab
Overall reliability of 95%
– accelerator reliability greater than 99%
Penetration depth
– 250 MeV protons penetrate 38 cm in water
– carbon equivalent is 410 MeV/u - 2.6 times the rigidity
Dose rate
– deliver daily dose of 2 Grays (J/kg) in 1 or 2 minutes
– 1 liter tumor needs (only) ~ 0.02 W very low power!
– need x10 or x100 with degraders & passive scattering

---
Thorium Energy Amplifiers
ThorEA!

---
Global interest

---
Energy amplifier basics
Protons injected into a target generate neutrons into a subcritical core which “burns”, creating heat & electricity.
Power generation ceases quickly when the beam stops
Inherent safety at the cost of ultra-high reliability!
Neutron multiplication
factor typically k = 0.98
Accelerator
Neutrons
Protons
Reactor core
Spallation target
Grid
Energy
extraction

---
Sustainable
Known Thorium reserves are more than sufficient for centuries of significant power production.
More will be found – Thorium has been of little interest.
India, Australia, Canada, U.S., Norway have lots.
Strong interest/activity in Australia, China, EU, India, Norway-UK.
Exploding global interest will soon include North America?
World Thorium Resources
Country
Australia
India
USA
Norway
Canada
South Africa
Brazil
Other countries
World total
Reserve Base (tons)
340,000
300,000
300,000
180,000
100,000
39,000
18,000
100,000
1,400,000
Source: U.S. Geological Survey, Mineral Commodity Summaries, January 2008

---
ThorEA
Thorium Energy Amplifiers (possibly) enable a method of nuclear power generation that avoids the problems of:
Critical accidents. Not possible (AND) turn beam off.
Long-lived waste. The modest amount of “true waste” has only to be stored for some 300 years, not millions.
Plutonium stockpiles. Transmutation of conventional reactor waste includes plutonium - “negative waste”.
Fuel inventory. Re-fueling only every 5 to 10 years enables easy central management & monitoring of many reactors.
Proliferation. The fuel mixture cannot be used for nuclear weapons – neither unburnt nor after the burn cycle.

---
http://www.thorea.org
“The need to avert climate change through reducing our use of fossil fuels is now acknowledged to be of paramount importance. Nuclear power is a zero carbon energy source, but the Uranium-Plutonium fuel cycle in current use suffers from problems around safety, waste disposal, and weapons proliferation. Problems of public acceptance persist.”
“Thorium-fueled subcritical reactors driven by accelerators (Thorium Energy Amplifiers) do not have the drawbacks of conventional nuclear power, and can provide safe, clean, carbon-free power that will satisfy the world’s energy needs for tens of thousands of years without the danger of weapons proliferation, or the need to dispose of long-lived waste. Thorium EAs have the additional benefit that they can use the waste from other reactors as fuel.”

---
ThorEA accelerators
HIGH power LOW energy

---
What beam energy?
Above ~1 GeV neutron flux is proportional to beam power
(Depends somewhat on the target & moderator design)

---
What beam power?
Full scale electricity plant needs (eg) 1 GW thermal
– if criticality factor k = 0.985, then gain G = 200
– required beam power = 5 MW
Medium scale demonstrator only needs (eg)
– k = 0.94, G = 50,
– thermal power = 10 MW, beam power = 200 kW

---
Demonstration – SBVR75 submarine reactor?

---
4 accelerator technologies
Some truths seem self-evident ..... ??
SRF linac cost estimate > $1B or 1 B Euro !!
SNS reliability is 80% : multiply by availability!

---
FFAGs
KURRI
“Study neutron production”
3 stage FFAG, 120Hz
0.1 – 2.5 MeV
2.5 – 20 MeV
20 – 150 MeV (?)
Current ~1 nA
Beam power ~0.15 W
Therapy?
EMMA & PAMELA

---
Synchrotron space charge
Laslett space charge tune shift parameter
Injection energy: maximize, eg DTL: ~200 MeV
Extraction energy: 1 GeV or more
Rep rate! Want ~kHz
Space charge limits injected intensity, output beam power
Rapid Cycling (RCS) technology has been with us for more than 40 years – before “real” control systems.
FNAL 15 Hz, Cornell 60 Hz, DESY 50 Hz, KEK 50 Hz, RAL 50 Hz, (transformers 50/60 Hz), ...

---
How to answer the critics?
Critics claim that accelerators:
– are not reliable enough
– don't have the performance at a reasonable cost
Very likely they are wrong.
– How to prove it without making extravagant promises?
What accelerator R&D?
What demonstration stages?

---
Common RF challenges:
Therapy OR Thorium

---
Fast RF challenges
FFAGs & RCSs face a similar need for fast RF with
~1 kHZ rep rates, especially (but not only) with
~1 GeV high power thorEA implementations:
~ 10 times more RF volts
~ 10 times faster df/dt
7 MeV to 250 MeV:	factor of 5.1 freq swing
100 MeV to 1 GeV:	factor of 2.0
200 MeV to 1 GeV:	factor of 1.5
FFAGs frequency swing somewhat ameliorated?

---
Voltage requirement
700 kV solution not yet demonstrated … !
… but plausible given enough space(?)

---
Biased ferrite (RCMS)
RCMS cavity design is ready for early prototyping
Ferrites procured and tested for large frequency swing
  - 1.3-6.6 MHz
  - 60 Hz is aggressive but feasible
60 Hz requires two cavities
  - Expected voltage limit is about 6-7 kV/cavity

---
Barrier buckets (AGS)

---
”Wave packet” (SPS)
Linnecar: “Our cavities are about 16 m long and can work in fixed frequency operation for a beta swing of about 10%.”
“Reducing the length, and .... voltage (at the moment .... 2 MV), by a factor 10 should allow the beta or frequency swing to reach ~ 1.5.”
“For a 1 GeV top kinetic energy [and] 200 MeV injection the swing is 1.54 and for 100 MeV it’s 2.04.”
“So .... [wave packet] operation is not excluded!”
“Traditional ferrite tuners can also do this readily – but can they be persuaded to do it at 600 Hz?”

---
Very Rapid Cycling Synchrotrons

---
Bipolar injection + “Wilsons” magnet
Cornell synchrotron (60 Hz) & FNAL booster (15 Hz) use the same combined function magnet, with “no” beam pipe.
Wilson magnet 8.5 x 11 inches
Bi-polar injection gives redundancy & doubles the frequency

---
Multiple redundancy
Eg, use 3 or 4 accelerators per reactor core?
1st is down for maintenance, 2nd fails, 3rd & 4th keep on ...
Need inexpensive unit cost
Single points of failure?
PS Booster: 1.4 GeV, ~1 Hz
1.6 kJ per cycle per ring!
Factor of 4 in rep rate!?

---
Eddy currents
As well as RF, a VRCS also must worry about
   1. eddy currents: beam pipe, magnet iron & copper
   2. high voltages in driving magnets that fast.
Four 60 Hz “Wilson” magnet rings with bipolar injection and extraction take the rep rate up to
4 x 2 x 60 Hz = 480 Hz
Beyond 1 kHz: direct-wind iron-free bent active shielding SC combined function magnets?

---
Direct wind iron-free magnets
ALPHA octupole for anti-proton cooling experiment at CERN.
Very fast turn on (half-cycle?)!
ILC prototype IR quadrupole QD0, with concentric corrector layers.

---
Combined Function 3.5 T direct wind magnet
 for a Carbon gantry

---
What next?

---
Upcoming ThorEA events
May 4–6, Vienna:	IAEA meeting, with reps from China & India.
Sept, Chicago area:	FNAL & ANL joint workshop on ADS. Some involvement of the BNL non-proliferation folk?
Sept++, DC area:	DoE Nuclear Engineering ThorEA workshop.
October, DC area:	DoE Science workshop (2, phased). What does it mean, “OHEP is the steward of accelerator R&D"?
ThorEA stakeholders:	DoE Science, DoE NE, NE departments, NE industry, National labs, Universities, AR+D, .....

---
DOE & ARPA-E
Chu ... plans to appoint a blue ribbon panel to develop a comprehensive plan to deal with nuclear waste ... DOE will begin a “vigorous research and development program” to determine how to reduce the proliferation risk associated with the recycling of nuclear waste. Chu [said that] "We are trying to ... restart the American nuclear industry again."
AIP Bulletin of Science Policy News, Number 50: April 29 2009
“ARPA-E applicants are required to submit a concept paper as the first step ... Only after notification from ARPA-E on the concept paper will the applicant be permitted to submit a full application.”
“Submission of concept papers begins May 12, 2009 [until] 2 June 2009.”
“... funding for the FFRDC [eg BNL, FNAL] portion of the work will not be included in the ARPA-E award, and instead will have to come through the “DOE field work proposal system.”

---
ThorEA (accelerator) stages
0)	Develop a loosely co-ordinated global plan, in broad agreement with ThorEA (target/moderator/core) & therapy folk.
1)	Early hardware prototyping without beam, eg fast RF & magnets
2)	Low power acceleration, with minimum complexity.
3)	Demonstrate & develop reliability. Increase power.
4)	Medium power integrated tests (eg SBVR75)
5)	Full power electricity production ....

---
Summary

---
ThorEA: more haste, less speed
Fusion promised too much too soon! Don't!
A prominent early failure would cause lasting harm
Aim low, succeed with ease, look good, move on!

---
Summary: Accelerator R&D
1) FFAGs &/or VRCSs may eventually provide excellent low and high power proton performance – power, reliability & availability at reasonable cost – for Therapy, ThorEA, HEP, .....
2) Fundamental accelerator R&D topics are fast magnets (eg VRCS) and fast RF (eg FFAG & VRCS).
3) Collaborate with ThorEA, first with zero or low power demonstrations, only then with medium power prototyping.
4) Leave GW electricity production until later.
5) Don't promise too much too soon!

---
There is only one boat!
Easily said:
No destructive war between competing designs
Share R&D on common challenges, eg RF