## Slide 1: The ARRA ANI Network Testbed Project September 29, 2009
Brian L. Tierney
bltierney@es.net

## Slide 2: Overview
Project Start Date: September, 2009
Funded by ARRA for 3 years
  Hopefully will continue beyond ARRA
Designed, built, and operated by ESnet staff
1 of 3 ARRA “Advanced Network Initiative” (ANI) projects in the DOE
  ANI 100G Prototype
  ANI Testbed
  4 ANI research projects

## Slide 3: ARRA/ANI Testbed Goals
Enable network, middleware and application end-to-end R&D at 100G
Configurable
Breakable
  Isolated from the production network
Reservable
Easy to reset to known state
A community network R&D resource
  open to researchers and industry to conduct experiments

## Slide 4: Multi-Layer Architecture Capability Planes

## Slide 5: Testbed Requirement: Support Network Research
Support research on:
  Data Plane
  Control Plane
  Management Plane
  AA Plane
  Service Plane
Ability to do multi-domain hybrid networking
  Support R&D on multi-layer and multi-domain control and signaling at layers 1-3
Ability to reserve and manage each components
Support protection and recovery research
Support interoperability testing of multi-vendor 100G network components
Provide access to all available monitoring data

## Slide 6: Testbed Requirement: Support Middleware/Application Research
Ability to support end-to end experiments at 100 Gbps
  Connect to Magellan systems at NERSC and ALCF
Ability to reserve and manage components
  End hosts / storage as well as network
Use virtual machine technology to support protocol and middleware research

## Slide 7: ANI 100G Prototype Network
The “100G Prototype” network will connect NERSC, ALCF, OLCF, and MANLAN at 100Gbps
  Not for production ESnet traffic
Testbed will use 100G waves from the prototype network
Testbed will use 100G routers from the prototype network

## Slide 8: Nationwide 100G Prototype Network
Sunnyvale
NYC
Nashville
Chicago
OLCF / ORNL
100 G
ALCF / ANL
NERSC
Magellan
Magellan

## Slide 9: ANI Testbed “Nodes”
Each testbed node will consist of:
  DWDM device (Layer 0-1)
    e.g.: Infinera, Ciena, Adva, etc.
    GMPLS-enabled
  Ethernet Services Router (layer 2-3)
    e.g.: OSCARS compatible Juniper, Cisco, etc.
    MPLS-enabled
  Test and measurement hosts
    Virtual Machine based test environment
    10G test hosts initially
      Eventually 100G from Acadia 100G NIC project

## Slide 10: Phased Approach
Phase 1:
  4 nodes in a lab at LBL
  Multiple10G waves between each node (> 40)
    Combination of Ethernet and SONET
  Full mesh connectivity
  Ability to simulate multiple domains
  MPLS enabled routers
  Secure access via a gateway node from anywhere
  Scheduled via simple calendar

## Slide 11: Phase 1: Tabletop Testbed in Lab
N1
N2
N3
N4
Notes:
Can configured in multiple ways, including example above with 3 possible paths from N1 to N4
Can be used to simulate multiple domains

## Slide 12: Phased Approach
Phase 2:
  Nodes are deployed on the WAN
  1 or more 10/100G Ethernet circuits between each node
    Will upgrade segments to 100G as hardware becomes available
  Partial physical mesh connectivity
    Logical full mesh possible via VLANs
  Ability to simulate multiple domains
  MPLS enabled routers
  Scheduled using OSCARS-like system

## Slide 13: Phase 2 Deployment Assumptions
The following architecture assumes the following comes out of the ESnet ANI RFPs:
  “Dim fiber” between Sunnyvale and NERSC
  “Dim fiber” between Chicago and ANL
  A single 100G service between Sunnyvale, Chicago, Nashville, and New York
Dark fiber ring in Long Island connecting AofA to BNL
Note that the ANI architecture presented here will change if these assumptions are not true

## Slide 14: ANI Prototype Network – current plan

## Slide 15: Testbed Access
Testbed will be accessible to anyone:
  DOE researchers
  Other government agencies
  Industry
Must submit a short proposal to the testbed review committee
  Committee will be made up of members from the R&E community and industry

## Slide 16: Timeline: Phase 1
Project Start
Hardware selection
Milestone
Oct 2009
Jan 2010
Apr 2010
Jul 2010
Oct 2010
Jan 2011
Initial Hardware Ordered
Testbed installed and configured
Simple management software developed
Initial ‘table top’ node hardware setup at LBL
Review committee established
Testbed available to DOE-funded researchers
Hold Testbed Workshop
Start accepting Testbed proposals

## Slide 17: Timeline: Phase 2
WAN deployment planning based on ANI Prototype awards
Milestone
Oct 2010
Jan 2011
Apr 2011
Jul 2011
Oct 2011
Jan 2012
Connect Testbed to Magellan
100G WAN Testbed Available to researchers
Testbed available to 1st group of non-DOE researchers
Accept 2nd round of Testbed Proposals
Refine Testbed Management Software
2nd round Testbed users get access
OSCARS-like interface to schedule resources deployed

## Slide 18: Testbed to support DOE ARRA-funded Research Projects
Climate 100 (LLNL, LBL, ANL)
  Project Goal: Scaling the ESG to 100G
  Testbed role: provide interconnect between “Magellan project” resources at ANL and NERSC
Advanced Network and Distributed Storage Laboratory (OSG: U Wisc, FNAL, etc)
  Project Goal: enhance Virtual Data Toolkit (VDT) data management tools to effectively utilize 100G networks
  Testbed role: provide interconnect between “Magellan project” resources at ANL and NERSC
100G NIC (Acadia and Univ New Mexico)
  Project Goal: produce a host NIC capable of 100 Gbps
  Testbed role: Provide test environment for this device
100G FTP (BNL/Stony Brook University)
  Project Goal: design 100G transport protocols and tools to enable 100G FTP server to client data transfer
  Testbed role: Provide a 100G test environment

## Slide 19: Testbed to support DOE Network Research Projects
“Resource optimization in hybrid core networks with 100G links” (Univ Virginia)
  Project Goal: Develop methods for automatic identification and tagging of flows that should be moved from the IP network to a dynamic virtual circuit
  Testbed role: Provide a test environment for validating these these methods
“Integrating Storage Resource Management with Dynamic Network Provisioning for Automated Data Transfer” (BNL, LBL)
  Project Goal: Integration of dynamic virtual circuits into BestMAN (Berkeley Storage Manager / SRM v2.2)
  Testbed role: Provide a 100G test environment for verifying this work
“Provisioning Terascale Science Apps using 100G Systems” (UC Davis)
  Project Goal: Advanced path computation algorithms for efficiency and resiliency
  Testbed role: Provide a control plane test environment for these algorithms using OSCARS

## Slide 20: Testbed to support DOE Network Research Projects (cont.)
Virtualized Network Control (ISI, ESnet, Univ New Mexico)
  Project Goal: multi-layer, multi-technology dynamic network virtualization
  Testbed role: provide a control plane test environment for experiments using hybrid networking
“Sampling Approaches for Multi-domain Internet Performance Measurement Infrastructures to Better Serve Network Control and Management” (Ohio State Univ)
  Project Goal: Develop new network measurement sampling techniques and policies
  Testbed role: Provide a network environment for initial deployment

## Slide 21: For More Information
Contact: bltierney@es.net

## Slide 22: EXTRA SLIDES

## Slide 23: Objectives
Provide a easily re-configurable high-performance network research environment to enable researchers to accelerate the development and deployment of 100G networking through prototyping, testing, and validation of advanced networking concepts.
Provide experimental network environments for vendors, IPSs, and carriers to perform inter-operability tests necessary to implement end-to-end heterogeneous 100G networks.
Provide support for prototyping middleware and software stacks to enable the development and testing of 100G science applications.
Notes: This text from Thomas Ndousse

## Slide 24: Relation to the Magellan Project
High-speed storage resources for the ANI Testbed will be provided by the ARRA-funded Magellan Project
  DOE computing project funded at $33M
  Goal is 100G end-to-end
Magellan is:
  a research and development effort to establish a nationwide scientific mid-range distributed computing and data analysis testbed.
  Consists of two sites
    NERSC / LBNL
    ALCF / ANL
  Will provide multiple 10’s of teraflops and multiple petabytes of storage, as well as appropriate cloud software tuned for moderate concurrency.