## Slide 1
6-D Cooling
Tom Roberts
Muons, Inc.
Muon Accelerator Program Review
Fermilab, August 24, 2010

## Slide 2: Outline
Why Cooling is Needed
How Ionization Cooling Works
Simulation Programs
Overview of the Cooling Subsystem
6-D Cooling
  Guggenheim
  Helical Cooling Channel
  Helical FOFO Snake
  Comparison of Techniques
Down Selection (FY12)
Design and Simulation – Level 2 Cooling Tasks
Milestones
Cooling R&D Issues
Why We Believe We Will be Successful

## Slide 3: Why Cooling is Needed
The muon beam is a tertiary beam generated by the decays of secondary pions.
The initial muon beam is huge: enormous transverse emittances and a very large momentum spread.
It is infeasible to accelerate such a large beam to TeV.
To obtain adequate luminosity, the normalized 6-D emittance must be reduced by roughly 106.
We call this reduction in emittance “cooling”; it is directly analogous to thermodynamic cooling.

## Slide 4: How Ionization Cooling Works Basics
By alternating absorbers with acceleration, the p⊥ of each particle can be reduced:
This is inherently a 2-D process in {x’,y’} (={dx/dz,dy/dz}); it operates in the 4-D transverse phase space.
Energy loss with re-acceleration cools the beam, multiple scattering heats it − need low-Z absorber (H2, LiH, …).

## Slide 5: How Ionization Cooling Works Basics
Liouville’s theorem is not violated: the electrons in the absorber are heated (but they aren’t part of the beam).
It takes many cooling cells to achieve the 106 emittance reduction required.
The channel must be designed to partition the emittance reduction into all 6 dimensions {x,x’,y,y’,dt,dp/p}.

## Slide 6: How Ionization Cooling Works Partitioning the Cooling
Re-partitioning the cooling in the transverse dimensions merely requires a change in focusing of the beam.
Partitioning cooling to the longitudinal dimension requires emittance exchange:
Straggling and the variation of dE/dx with energy contribute to longitudinal heating of the beam.
Reduced Longitudinal emittance, increased transverse emittance.
Dispersion is arranged so higher momentum particles have a longer
path in the absorber.

## Slide 7: How Ionization Cooling Works Summary
The 6-D cooling channels below differ in how they arrange the dispersion, absorbers, and focusing to re-partition the cooling among the 6 dimensions.
All use a helical path, as that is the best way to maintain transverse focusing and to provide the dispersion necessary for the emittance exchange.

## Slide 8: Simulation Programs
Muon cooling requires tracking particles through matter, which standard accelerator design codes do not support.
We have developed two simulation programs that do:
  ICOOL
    Primary author: Rick Fernow
    Fortran, with portions from Geant3
    https://pubweb.bnl.gov/~fernow/icool/
  G4beamline
    Primary author: Tom Roberts
    C++, based on Geant4
    http://g4beamline.muonsinc.com
As muon cooling is new technology, our plans include maintaining both programs and using them to evaluate our designs.
Other programs may be used as appropriate.

## Slide 9: Overview of the Cooling Subsystem – Current Baseline
From Front End
6-D Cool A
6-D Cool A
Bunch Merge
Bunch Merge
6-D Cool B
6-D Cool B
Charge Recombination
Charge Separation
Final Cooling
To Accel.
Negatives
Positives

## Slide 10: Overview of the Cooling Subsystem – Current Baseline
From Front End
6-D Cool A
6-D Cool A
Bunch Merge
Bunch Merge
6-D Cool B
6-D Cool B
Charge Recombination
Charge Separation
Negatives
Positives
This Talk
Bob Palmer’s Talk
Final Cooling
To Accel.

## Slide 11: Overview of the Cooling Subsystem
END
Figure credit: R. Palmer
Final Cooling
40-50 T Solenoids
BEGINNING:
From Front End

## Slide 12: 6-D Cooling Guggenheim
Basically a cooling ring stretched out vertically to simplify extraction and injection; also reduces heating power in absorbers (from multiple turns).
Lumped liquid hydrogen absorbers (pink), or LiH
Vacuum RF cavities (dark red)
Solenoid magnets, inclined to force the beam to follow the helix (yellow)
A short section of a
Guggenheim cooling
channel.

## Slide 13: 6-D Cooling Guggenheim
ICOOL simulations of a tapered Guggenheim cooling channel.
Overall transmission is 32%.
Figure credit: R. Palmer

## Slide 14: 6-D Cooling Helical Cooling Channel
Continuous high-pressure hydrogen gas absorber
Short solenoids (green) in “helical solenoid” configuration give solenoid, helical dipole, and helical quadrupole fields
Integrated high-pressure RF cavities (orange)
Pressure windows only at beginning and end
A short section
of a Helical Cooling Channel;
outer solenoid not shown.

## Slide 15: 6-D Cooling Helical Cooling Channel
G4beamline simulation of three tapered helical cooling channels.
Overall transmission is 60%.
Figure credit: K. Yonehara
and T. Roberts
λ=1.0–0.8 m
λ=0.8–0.3 m
λ=0.3 m
73%
63%
60%

## Slide 16: 6-D Cooling Helical FOFO Snake
Basically a linear channel with tilted solenoids to give a shallow helix
Lumped liquid hydrogen absorbers
Vacuum RF cavities
Can cool both positives and negatives
A short section of a Helical FOFO Snake.

## Slide 17: 6-D Cooling Helical FOFO Snake
Simulation results for the helical FOFO snake.
Transmission after 100 meters is about 60%.
Figure credit: Y. Alexahin
 (cm)
|| (cm)
z (m)
z (m)
Transverse Emittance
Longitudinal Emittance
-
-
+
+
Initial
Mismatch
Initial
Mismatch

## Slide 18: 6-D Cooling Comparison of Techniques
 | Guggenheim | Helical Cooling Channel | Helical FOFO Snake
Absorber | Lumped liquid H2 or LiH wedge | Continuous high-pressure gas H2 | Lumped liquid H2
RF Cavities | Vacuum with Be Windows | High-pressure gas, Be Windows | Vacuum with Be Windows
Magnets | Tilted Solenoids | Helical Solenoid | Tilted Solenoids
Helix ratio: radius / period | Large, >>1, almost a ring | Moderate, ~0.2 | Small, <<1, almost straight
Can achieve low emittance to feed into final cooling | Yes | Yes | No
Can cool both charges | No | No | Yes
Have initial simulations | Yes | Yes | Yes

## Slide 19: Down Selection (FY12)
At present we have three viable 6-D cooling techniques.
In FY12 we will have enough information to “down-select” and determine the actual cooling subsystem to be used in the Design Feasibility Study Report.
Our current task is to evaluate the possibilities and collect all necessary information to make an informed choice.
We expect the selection to be of a complete cooling configuration; multiple techniques may be involved.

## Slide 20: Down Selection (FY12)
Indeed, even the overall block diagram is subject to selection:
  At present, it seem likely that a helical FOFO snake will come first, before the charge separation.
  That may or may not be sufficient to go directly into the bunch merge.
  The choice for Final Cooling might require the charge recombination to come after final cooling.
The selection for cooling can be affected by similar down-selections in the Front End and in Technology Development (RF).

## Slide 21: Design and Simulation Level 2 Cooling Tasks
Develop approach for comparing, assessing, and selecting cooling techniques
6D Cooling
Final Cooling
Auxiliary Components (charge separation, bunch merging, charge recombination)
Simulation Code Development (ICOOL, G4beamline, ...)
Target-to-accelerator simulation of Front End and Cooling
RF Systems Simulations
DFS Report preparation

## Slide 22: Milestones
Date | Milestone | Deliverable
FY12 | specify cooling initial configuration | MAP Review, Design Report
FY14 | finish D&S for Interim MC DFS report finish D&S for Final IDS-NF RDR report | Formal Report Formal Report
FY15 | provide specifications & parts count for MC costing | Design Report
FY16 | provide description of remaining MC R&D items finish D&S for Final MC DFS report | Design Report Formal Report

## Slide 23: Cooling R&D Issues
Simulation Issues
  Match the different sections, with acceptable emittance growth and losses.
  Evaluate space charge effects (primarily final cooling).
  Analyze, understand, and evaluate collective effects in the absorbers (primarily final cooling).
    Plasma effects (ionization electrons)
    Dielectric polarization effects
    Effect on space charge, macro-particle interactions, etc.
Design Issues
  High RF gradients (See Alan Bross talk)
  High-field magnets (See Alan Bross talk)
  High beam heat load in absorbers (needs engineering)
  High beam loading in RF cavities (needs engineering)

## Slide 24: Why We Believe We Will be Successful
We already have considerable experience in designing cooling channels:
  We have multiple techniques for both 6-D and final cooling, and at least one for each of the auxiliary components.
  We have initial simulations of each technique, indicating they can be put together as shown.
We have a team of experts already involved.
The primary developers of the simulation tools we are using are already part of the team.
MAP is the culmination of more than 15 years of effort – we are motivated to succeed!