## Slide 1: Proton Beam for PRISM
Keith Gollwitzer
Accelerator Division
Fermilab
5th Workshop Project X Physics – Muons
November 8, 2010

## Slide 2: Outline
Review of Project X beam
PRISM beam requirements
Changing bunch structure
Issues

## Slide 3: Project X Beam Review
3GeV beam energy out of CW Linac
325MHz bunches (3.1ns spacing)
  RF splitter doubles spacing
  50ps bunch width
1.9x108 particles/bunch (10mA for < 1μsec)
Linac average beam current 1mA (>1 μsec)
  3MW out of Linac possible
H- beam out of Linac
  Preference to convert beam to protons before 3 way RF splitter

## Slide 4: PRISM Beam Requirements
1MW of proton beam power
  Already asking for more beam power
    More beam current (towards 4MW)
    Increase CW Linac energy
Repetition rate of ~1kHz
  Believed to be limit of injection/extraction kickers of muon storage ring
    2x1012 protons every 1ms
Bunch width of 10ns
  A narrower width is desirable

## Slide 5: Changing Bunch Structure (1)
Need to accumulate beam
  Change 162.5MHz beam out of RF splitter to 1kHz beam onto target
  Requires H- beam out of RF splitter
  Accumulation Ring will have stripping system and dump
    To accept unconverted beam (H- and Ho)
  Requires programmable Linac front end to populate appropriate Linac bunches such that the appropriate Accumulation Ring RF bunch(s) are filled
    Leave kicker gap using barrier RF system
    Set initial bunch length before RF manipulations

## Slide 6: Change Bunch Structure (2)
Final bunch length requires RF manipulation
  After accumulation, beam transferred to second ring: Buncher
  Buncher will perform final RF bunch rotation to achieve short bunch length
Accumulation
Ring
Buncher
Ring
RF Splitter
Linac
H- beam
Proton
Bunch to
Target

## Slide 7: Issues (1)
Injection/Extraction Kickers
  1kHz kickers are the same technological issue as for PRISM Muon Storage Ring
    Repetition rate
    Rise time or fall time
Beam Dynamics
  Space Charge?
  Beam size in dipoles at final bunch length
RF
  How much required to perform manipulations at required rate?

## Slide 8: Issues (2)
H- beam out of RF splitter
  Requires lower field in downstream Lambertson to avoid Lorentz stripping of H- beam
    Affects layout of switchyard area
    Each area will need own stripping system
Stripping system and beam dump
  Quantum mechanics of stripping systems
    >95% easy but leaves tens of kW beam power

## Slide 9: Summary
Project X can provide the amount of proton beam necessary for PRISM
Work will be needed to convert bunch structure