## Slide 1: Remote Office Revitalization
ORAU - ISD

## Slide 2: Remote Offices Present Status
Servers are aging - scheduled for Tech Refresh
Wide Area Network technology is same as we installed 10 years ago – T1 – 1.5mbps
Traffic over the WAN has changed. More traffic is remote, local traffic is less
T1s are over utilized – 40ms is now 400ms
Each office (except 1) has a local ISP connection, only used for backup/VPN connectivity – underutilized.

## Slide 3: Proposed
Migrate from Point-to-Point T1s to MPLS Wide Area Network
Utilize inexpensive broadband Internet for backup connections
Utilize broadband Internet for local use (proxy server)
ESX server – providing Internet Proxy, File/Print, AD/DNS, SCCM, Backup

## Slide 4: Provides
Network
  More resilient network – connection into MPLS network is local, a few miles instead of thousands
  Cheaper local broadband ISP can be used for backup, downtime is less
  MPLS network is a mesh routed network
  Secure – encrypted connections between ORAU offices through MPLS network
Server is smaller, cooler, less power requirements, and easily expandable and manageable

## Slide 5: Costs
MPLS Network
  Current monthly WAN costs - $5,000
  Proposed WAN network - $13,750 per month
  An increase of $8,750 per month
  Provides 6 to 20 times the bandwidth in that same cost of nxT1s - cost of 4xT1 (6mbit) is same as 10mbit MPLS
  Speed upgrades through a service change request.
  Equipment for all locations - $70,000 – lifetime of 5-7 years
Servers
  ESX Servers - $15,000 per office
    one server replaces four

## Slide 6: Remote Office
The proposed solution becomes a Remote Office in a box solution
Open a new Remote office, the same equipment ships
One item that is variable is amount of disk space for file shares

## Slide 7: “Office in a Box”
Network
  Juniper J4350 router
  AT&T MPLS connection - >= 10mbps
  Brocade FGS648P network switch – 48 ports
Power
  Liebert GXT3-2000 UPS
  Liebert EMComm – Environmental monitoring

## Slide 8: “Office in a Box” – cont’d
Server
  IBM Server
    ESX
    Proxy Server – Internet access
    Windows Active Directory Domain controller / DNS
    Windows File/Print
    Windows SCCM – monitoring and management
    IBM TSM - backup

## Slide 9
Arvada
Oak Ridge
Belcamp
DC
Stafford
Comcast /
Broadband
Internet
T1
T1
1xT1
2xT1
100 VPN
1G
Current

## Slide 10
MPLS
Network
Arvada
Oak Ridge
Belcamp
DC
Stafford
Broadband
Internet
DR connectivity has not been define
45
45
45
45
100
1G

## Slide 11
FGS
SRX
J-4350
Routed
Network
Broadband
SRX
J-6350
LAN
OR Net
Oak Ridge
Remote Office