## Slide 1: DICE Diagnostic Service
Joe Metzger
metzger@es.net
Joint Techs Measurement Working Group
January 27 2011

## Slide 2: Background
Each of the DICE collaborators are defining and delivering services to their users. A subset of these services will be a lot more useful for everyone if all of the DICE participants deploy them in an interoperable fashion.
A decision was made last winter to add more rigor or structure to our collaborative efforts and focus on a small set of services.
  Network Diagnostic Service
  Dynamic Circuit Provisioning Service
  End user performance portal service

## Slide 3: DICE Network Diagnostic Service
The DICE Network Diagnostic service is an agreement between Internet2, ESnet, GEANT, Canarie & USLHCnet to deploy, support and use a interoperable subset of perfSONAR network measurement tools across our backbones to simplify diagnosing inter-domain network performance problems.
The target user community for these services is the network engineers in our respective NOCs, and the engineers at around a dozen other transit networks selected from European NRENs (coordinated by GEANT) and Gigapops or Regionals (coordinated by Internet2)
The measurement services included in the DICE service are intended to be the minimal useful interoperable subset of the measurement services that each domain is offering to their community.
Notes: Note, it is intended to be an inclusive service. But

## Slide 4: The Diagnostic Service Includes
Definitions of the Service
    Active latency & bandwidth measurement points
    Historical latency and bandwidth measurement archives
    Recommended measurement schedules, parameters & limits
Service Level Specifications
    Incident, problem, change management
    Reporting details
Operational Level Agreements
    Dealing with target availability goals, outage notification, etc
    AA (very lightweight.)
Agreements about Jointly Operated Service Elements

## Slide 5: What are we actually ‘deploying’?
Bandwidth measurement services
  10G* capable measurement points near network borders
  Regularly scheduled TCP tests between domains
    4 tests per day
    TCP
    Using Cubic, BIC or another aggressive TCP stack
    Long enough to get out of slow start (20-30 seconds)
    Large TCP windows
    Best effort QOS tags
  Results will be archived & published via perfSONAR
Notes: This is the target. The agreement includes weasel words so that 10G is not a hard requirement.

## Slide 6: What are we actually ‘deploying’?
Latency measurement services
  Measurement points near domain borders
  Active one-way tests between domains at 10 pps
  Archives of historical results
  Target accuracy of clocks for 1-way tests is better than 1ms.
Lookup Service
  Provides a mechanism to find services
Looking Glass Service
  Standard looking glass to look at current info from routers

## Slide 7: And, all business processes to support the services…
Provide user interfaces and training to our NOC engineers so they can effectively use these services for diagnosing performance problems
Monitoring the services, coordinating outages, responding to failures, supporting users, and all of the other things involved with running a production service.

## Slide 8: Primary changes of the deployed ESnet measurement infrastructure to support the DICE Diagnostic Service
Change TCP stack used for scheduled bandwidth tests from Reno to a more aggressive stack like BIC or Cubic
Configure inter-domain bandwidth tests to use best effort instead of scavenger DSCP
Expand the metadata bandwidth measurement points register with the lookup service to include info like TCP stack, interface speed, version numbers, etc.
Support invoking bandwidth & latency tests via the XML perfSONAR protocol in addition to the bwctl & owamp protocols used today
Deploy a router looking glass

## Slide 9: Additional Slides about the DICE Services for ESCC talk.

## Slide 10: DICE Dynamic Circuit Service
The goal of the dynamic circuit service is to support automatic provisioning of dynamic circuits across multiple domains
  Primary participants are ESnet, Internet2, GEANT & USLHCnet
    5-6 European NRENs participation will be coordinated by GEANT
    4-6 Regionals or Gigapops participation will be coordinated by Internet2
  Initially using OSCARS & AutoBahn & version 1.1 of the IDC protocol
  Dynamic circuits will transport VLAN tagged frames
  Will support monitoring of dynamic circuits
  The target users of the pilot service will be the NOC engineers in the participating domains.

## Slide 11: DICE End User Performance Portal
The goals of the performance portal are to educate end users by:
Explaining basic concepts about network performance
Help them determine if what they want to do is feasible
Demonstrating what the network is capable of doing
Help them distinguish between good and bad network performance
Provide guidance on where to go for help
The target community is the non-technical end users. (ie humanities professors, not high energy physicists!)