## Slide 1: SNS/ProjectX Commissioning/Infrastructure
Willem Blokland
(SNS/RAD)

## Slide 2: WorkGroup Controls, Instr.& Protection
What are the requirements for ProjectX?
  Identify technical issues for Controls & Instrumentation (and high level applications)
  Establish goals and mile stones
  Collaboration and R&D

## Slide 3: SNS Commissioning Experience
Loss tuning and measurement
Flexibility of cavities
Hardware (HVCM) reliability -> Shake out period
Dual Source for reliability -> Risk management
Errant beam control -> Diagnostics performance
Robust Intelligent Control system
What are the (uptime) requirements by the customer?
(K. Jones)

## Slide 4: SNS Research Accelerator Division
Responsibilities are separated (to a degree) to avoid priority conflicts
Optimizing, setup, theory, design
Accelerator applications (XAL)
Simulations
Real-time/offline models
Operations
Day to day operations
Console Applications (GUI, Alarm, Tune-up)
Physics
Controls
Infra-structure: network, consoles, PLC, PPS, MPS, CSS, Timing….
EPICS, PLC, VME, VxWorks,…
Instrumentation
Beam measurements
  Detectors, Electronics, Instrumentation Platform
Support and use their own infra-structure on top of Controls’
See also previous ProjectX talk on SNS Console Overview, Sept. 2010

## Slide 5: Physicist Control System Interface Perspective (SNS)
Physicists wrote high level programs
  Some more, some none
High level programming/script interface
  Java, python, matlab, …
  Use modern tools for gui, plots, math, …
Simple interface to “physical” quantities
  Hide control system connection details
  E.g. getAverageHorizontalPosition()
J. Galambos

## Slide 6: Hierarchical Control System
Planning
Execution
Supervisory
Coordination
Control
Group Control. For Example: Laserwire Transfer line
Implementation
NAD
NAD
Server
Plant-wide data collection and optimization
Data-acquisition and processing:
PLCs, NADs
Operations
Management
Run Coordinator
Applications
Network
(Private) Network
Wires
Sensor/Actuator
Operation of the plant, executing
the plan, e.g run beam to 50mA
Long term planning of the accelerator, e.g.CD4 goal
Examples
Accelerator
Toroids, BMP plates, Harp, etc

## Slide 7: ProjectX Infrastructure
What is required for ProjectX from a top-down perspective? If you don’t do a top-down design and rely on a bottom-up approach only, you can end up with a best guess implementation by people who might not fully understand the difference between the old and the new system.
Oh, you wanted wheels with that!
Photo credit: Kevin P. Coughlin

## Slide 8: ProjectX Infrastructure
Discussion:
  What do you envision for the ProjectX Control Room Environment?
    Console screens-> graphics, alarms
    Physics applications
      programming environment
      Rapid development
      Who develops in what programming language
    What data is needed and at what rates
    Archiving and retrieval
    Network requirements