## Slide 1: Cavities, Cryomodules, and Cryogenics Working Group 2 Summary Report
Mark Champion, Sang-ho Kim
Project X Collaboration Meeting
April 12-14, 2011

## Slide 2: Acknowledgments and Disclaimers
The presenters were well-prepared and gave very nice talks
  Thank you !
There is a lot of good work going on in support of Project X
The following slides represent my view with input from Sang-ho

## Slide 3: 15 Presentations
325 MHz Cryomodule Development at Fermilab Tom Nicol
Project X 650 MHz Cryomodules Tom Peterson
Cavity and Cryomodule Progress at RRCAT Satish Joshi
Status of the SPL cryo-module design Vittorio Parma
Reliability of SNS Superconducting Linac Jeff Saunders
SNS Cryomodules Matthew Howell
SNS Cryo System Operational Experience Fabio Casagrande
Operating Temperature Analysis Arkadiy Klebaner
SNS SCL Experiences Sang-ho Kim
Experience with SNS HOM Couplers Marc Doleans
HOM Couplers for Project X: Are they needed? Slava Yakovlev
HOM coupler requirements for SPL/SNS/ESS Frank Gerigk
Project X Superconducting Cavities Status Report Mark Champion
650 MHz Beta = 0.61 Cavity Design, Fabrication and Testing Bob Rimmer
Active Stabilization of the SRF Resonance Frequency Yuriy Pischalnikov

## Slide 4: Highlights (1)
325 MHz cryomodule conceptual design (Nicol)
  Cryogenic load dominated by conduction cooled solenoid current leads
  Concept for segmentation of SSR0 cryomodule into 3 parts with cold interconnects was presented
650 MHz cryomodule conceptual design (Peterson)
  Baseline configuration is Tesla-type with 300 mm pipe used as cavity strongback; “closed” helium vessels with separate 2-phase helium pipe
RRCAT Activities (Joshi)
  Much progress in cavity fabrication at 1.3 GHz and 650 MHz
  Major SRF infrastructure construction is underway
  Collaborating on 650 MHz cryomodule design

## Slide 5: Highlights (2)
SPL cryomodule status (Parma)
  4-cavity prototype cryomodule, 704 MHz, 5-cell, beta=1 cavities
  Interesting design concepts, especially cavity support system
  Schedule calls for cryomodule testing end of 2013
SNS Linac reliability (Saunders)
  Failures include: pressure transducers, cold cathode gauges, tuners, HOMs, vacuum leaks, and loose rf cables
  Numerous repairs effected, in-tunnel and out-of-tunnel, to maintain performance of the Linac
  All tuner components can be repaired or replaced in-tunnel
SNS cryomodules (Howell)
  Vacuum vessel and end cans are code-stamped and meet pressure vessel requirements (unique approach)
  Spare high-beta cryomodule under construction
  PUP cryomodules will be plug compatible with original cryomodules

## Slide 6: Highlights (3)
SNS cryogenic system operational experience (Casagrande)
  Cryo plant has been in operation since 2004 with very little downtime
  Operation of heaters to balance heat load provides for stable operation
  One week to warm up, repair tuner, and cool down cryomodule
Operating temperature analysis (Klebaner)
  Practical range is 1.8K to 2.17K – rather flat optimization curves
  Real issue is to minimize cavity dissipation. This is the primary cost driver for the cryogenic plant.
  Plant coefficient of performance: how low can it go?
SNS SCL experience (Kim)
  A wealth of experience
  Collective effects of field emission limit cavity maximum operating points
  Current operating parameters are providing very stable operation

## Slide 7: Highlights (4)
SNS HOM experience (Doleans)
  Nice explanation of how SNS HOM analysis was performed
  SNS HOMs were included not for beam dynamics reasons, but only to prevent additional rf dissipation in cavities
  No HOM couplers on PUP cavities
Project X 650 MHz cavity HOM analysis (Yakovlev)
  Project X and SNS applications similar in terms of average HOM power per cavity
  Many details, but clear conclusion: HOM couplers not needed for Project X
  No dissenters
HOM coupler requirements for SPL/SNS/ESS (Gerigk)
  Plan to include flanged HOM ports on SPL cavities (SPL beam parameters are subject to change)
  ESS: frequency comparison between 704 and 1300 MHz
    Lower frequency favorable with respect to HOMs

## Slide 8: Highlights (5)
Project X cavities status report (Champion)
  650 MHz single-cell prototypes in fabrication
  Nearly ready to procure SSR0 and five-cell 650 MHz prototypes
650 MHz beta=0.61 cavity status (Rimmer)
  Two single-cell prototypes complete
  Test results expected soon
Active stabilization of cavity frequency (Pischalnikov)
  Demonstrated very effective compensation of Lorentz force detuning and detuning from helium bath pressure variations (dF/dP) and mechanical vibrations on 325 and 1300 MHz cavities
  Pulsed and continuous wave applications
  Extremely narrow cavity bandwidths (few Hz to tens of Hz)

## Slide 9: Issues / Decision Points
What cavities will be used in the 2.5 – 10 MeV range?
  325 MHz SSR0 or 162.5 MHz half-wave cavities
  Meanwhile, do we build prototype SSR0 cavities?
Need to formalize decision to omit HOM couplers on 650 MHz cavities
How and when to proceed with SSR2 development given finite funds?
Need to complete requirements documents for many technical systems and components
Need to decide if beam tests are necessary and feasible for the SSR four-cavity prototype cryomodule
Consider increasing loaded bandwidths to mitigate control complexity and total reliance on piezoelectric tuners
Cryogenic plant capacity is highly dependent on cavity performance

## Slide 10: What will be reported at the next collaboration meeting?
Cavity deliveries
Cavity test results
  650 MHz single-cell cavities
  325 MHz SSR1 cavities
Prototype cavity fabrication will be in progress
  325 MHz SSR0 cavities
  650 MHz five-cell cavities
Installation and commissioning of VTS2 at Fermilab
Progress in 650 MHz electro-polishing facility development
Cryomodule designs transitioning from conceptual to detailed design
Progress on the 2K conversion of the Fermilab spoke cavity test cryostat
Progress in microphonics compensation
And more…