## Slide 1: Foil Injection for RDR and Long Pulse Operations
David Johnson
Project X Collaboration Meeting
April 13, 2011

## Slide 2: Foil Issues
Foil Temperature
  What is an acceptable maximum temperature?
    SNS initial camera system designed to measure temps down to 1500-1600oK but never got a good measurement. A new system is planned…. Best guess for 1.4MW is in the 1500-1600oK range (M. Plum)
    JPARC reported on initial tests of measurement system of phototransistor and photodiode. Large errors in photodiode output. Focusing on pulsed measurement. Estimate safe carbon or diamond foil temp around 1600oK (A. Takagi)
Secondary Electrons
  Shape and magnitude of magnetic field – trajectory of electrons – beam normal to B
  Resistivity of injection foil ( build up of static charge – lesson learned SNS)
Minimizing secondary hits by circulating protons
  Ring lattice functions ( symmetric insertion, a=0 at foil)
  Foil size and orientation (matched to injection beam size)
  Painting algorithm
Losses due to
  H0 excited states (location of foil in rising field of HBC3 only n=1 not captured into circulating beam - 0.7% 2.2 kW will go to injection dump)
  Nuclear collision in 500 mg/cm2 foil
    -> probability 8.3E-6 -> Power=n hits*int/sec*NCP*E*C -> for 30 hits loss approaches 84 W
  Large angle coulomb scattering -> previously estimated for 30 hits est. 81 W
  H- missing the foil (utilize beam shaping to safely remove large amplitude)

## Slide 3
Type | Advantage | Disadvantage
Correlated | Paint over halo Square profile | Singular density Coupling emittance growth
Anti-Correlated | Immune to coupling Circular Profile | Halo Growth due to space charge Extra 50% aperture
H-V Coupled | Paint over halo Diamond Profile | Extra Aperture
Paint (H)/ Steer(V) | Similar to anti-correlated Fewer Kicker | Foil Support Difficult Susceptible operation error
Paint V/ Steer H | Similar to Anti-correlated. Fewer Kicker e- collection on mid-plane | Vertical injection Susceptible to operation error
Oscil. Bump (sin/cos) | Paint over halo Circular profile | Fast PS Switch Extra 50% Aperture
Transverse Painting Schemes

## Slide 4: Recycler Injection
HBC1
HBC2
HBC3
HBC4
75 to 100 mm
8.941 m
0.606 m
1.068 m
Stripping foil
H-
H0
H+ to inj. absorber
Thick foil H0->H+
Circulating protons
KEK (anti-correlated) H paint V steer
Foil orientation (corner foil used in present simulation)
Hor. Strip foil (matched to size of beam)
6-8mm
12mm
14mm
18mm
+3.5669 kG
-0.4656 kG
-11 kG
11 kG

## Slide 5: Distributions during painting
Uniform distribution in X and Y
Circulating beam hits on foil

## Slide 6
Transverse painting is designed to:
  Minimize the number of secondary passages and foil heating
  To make correlated x-y painting (K-V distribution) with radius increase for each next pulse
Injected beam does not move on foil
Closed orbit describes almost a quarter of circle (forward and back)

## Slide 7
The hit densities, N, from the STRUCT simulation for each injection are used to calculate the peak temperature as a function of time with
Peak foil temperature for five linac current pulse length combinations utilizing the
H paint/V steer painting algorithm.
Hit Density for Corner Foil (1ms)
Foil Temperature

## Slide 8
case | I | II | III | IVS | VII | S/c
linac current[mA] | 4 | 2 | 1 | 2 | 1 | 1
pulse length[ms] | 1.08 | 2.16 | 4.28 | 2 | 25.72 | 4.3
#turns/inj | 97 | 194 | 385 | 194 | 2310 | 385
#turns total | 582 | 1164 | 2310 | 1164 | 2310 | 2310
hmin | 13.5 | 27.0 | 53.7 | 27.0 | 53.7 | 53.7
<#hits> sim | 32.6 | 60 | 118 | 38.7 | 118 | 35
hit densitymax [E12] | 34 | 68 | 134 | 64 | 515 | ?
Peak temp | 1090 | 1480 | 2050 | 1420 | 2320 | 1400
loss (inelastic) W | 93 | 171 | 336 | 110 | 336 | 100
loss (nuclear coll.) W | 65 | 119 | 234 | 77 | 234 | 69
Summary of Painting
An analytical expression has been developed [10] for the minimum number of foil traversals, hmin, by a circulating beam as

## Slide 9: Foil for Long Pulse Injection
SBIR Proposal Submitted:
  H- Stripping Innovations (Muon’s Inc.)
Concept for rotating foil
  Spread beam heating
  Doesn’t address loss due to parasitic hits
  Simulation of moving foil to investigate interaction with circulating beam and hit density - STRUCT
Argonne Center for Nano Technology
  UNCD Fabrication Facility

## Slide 10
2 micron UNCD film
(surface structure may be required
Si substrate
Copper
34 mm
42 mm
5 mm
5 mm
H- beam
t = 30 ms
w = 12,600 rpm (disk Drive speed)
w
The Si substrate and UNCD film are
sandwiched between two copper disks
Rotating Diamond Foil Assembly
for H- Stripping

## Slide 11: Next Steps for Long Pulse
Simulate rotating foil in tracking to determine number of interactions with circulating beam to estimate power lost.
Initiate effort to develop a mechanical and thermal model for rotating foil (if SBIR awarded work with Muon’s Inc.).
If results of mechanical/thermal model are encouraging initiate collaboration with Argonne’s Center for Nano Technology to investigate the design of a prototype foil.
Investigate other foil configurations