## Slide 1: Fermilab 650 MHz Cavity and Cryomodule Status Report
Mark Champion, Fermilab
Project X Collaboration Meeting
October 25-27, 2011

## Slide 2: 650 MHz Cavity Prototypes and Readiness for Processing & Testing
Orders placed for a mix of single-cell and five-cell cavities (next slide)
Vertical test stand ready for testing 650 MHz cavities
  Single-cell b=0.6 cavity to be tested soon
    Facility shakedown & comparison with measurements at JLab
Infrastructure ready for preparation of single-cell cavities
  Tooling design in progress for handling five-cell cavities
Electro-polishing tool at ANL nearly ready
Optical inspection system ready

## Slide 3: Cavity Procurements
Beta | Type | Quantity | Provider | Due Date
0.9 | 1-cell | 6 | AES | First two by end of CY2011
0.9 | 5-cell | 2 (option +2) | AES | June 2012
0.6 | 1-cell (FNAL) | 3 | RI | June 2012
0.6 | 1-cell (JLab) | 3 | RI | June 2012
0.6 | 1-cell (JLab) | 2 | JLab | Complete

## Slide 4: b=0.9 five-cell cavity prototype design
Ti helium vessel
4 mm Nb wall thickness
Nb-Ti flanges
Nb-Ti transition
No HOM couplers

## Slide 5: Cavity without helium vessel (this is what we ordered)

## Slide 6: And here’s how it will look when ready for horizontal tests

## Slide 7: 650 MHz Cryomodule Design Status
Conceptual design work and 3D modeling is in progress
  Frequent working meetings with collaborators
Plan to transition to detailed design work at end of FY2012
Basic configuration settled, but many details to be addressed

## Slide 8: Cryomodule requirements - major components
Eight (8) dressed RF cavities
Eight RF power input couplers
One intermediate temperature thermal shield
Cryogenic valves
  2.0 K liquid level control valve
  Cool-down/warm-up valve
  5 K thermal intercept flow control valve
Pipe and cavity support structure
Instrumentation -- RF, pressure, temperature, etc.
Heat exchanger for 4.5 K to 2.2 K precooling of the liquid supply flow
Bayonet connections for helium supply and return

## Slide 9: 650 MHz, b=0.9, conceptual cryomodule design

## Slide 15: Conclusion and Acknowledgments
Prototype cavities on order; first deliveries expected late this calendar year.
Plan to conduct first 650 MHz cavity test at FNAL in next month.
Infrastructure for processing & testing of 650 MHz cavities is nearly complete and will be available as cavities begin arriving.
Cryomodule conceptual design is progressing and will transition to detailed design near end of fiscal year.
Thanks to Tom Peterson, Chuck Grimm, and Youri Orlov for contributions to this presentation.