## Slide 1: SSR1 cavity EM and Mechanical design
Leonardo Ristori
I. Gonin, M. Hassan, D. Passarelli
PX Collaboration Meeting – 26 Oct 2011

## Slide 2
Main Parameters | 
Frequency | 325 MHz
βG | 0.215
Aperture | 30 mm
Cavity diameter | 492 mm
Bandwidth | ~ 90 Hz
Gain/Cavity, nominal | 2 MeV
Max Surface Magnetic Field, nominal | 60 mT
Max Surface Electric Field, nominal | 39 mV/m
Power/Coupler, nominal | 4 kW (1 mA)
He temp, pressure | 1.8-2.1 K, 20 torr
Q0 at Eacc | > 1.1x1010
df/dP (jacketed) | <25 Hz/mbar
1st prototype
By Zanon (Italy)
SSR1 overview
1st prototype
Jacketed at FNAL
Single Spoke Resonators have been developed at Fermilab in the last few years
2 bare prototypes tested in VTS and 1 jacketed prototype tested in HTS
We are receiving an order of 10 resonators from US vendors, 8 needed for the PXIE cryomodule
VTS
Spoke Cavity Test Cryostat

## Slide 3: RF design of SSR1
The dimensions were varied in MWS to optimize the RF design.
Surface electric (left) and magnetic (right) fields in SSR1.
The field strength increases as the color changes from green to yellow to red.
RF design parameters | 
Epeak/Eacc | 3.84
Bpeak/Eacc | 5.81 mT/(MV/m)
Leff (2*βλ/2) | 198.5 mm
G | 84 Ω
R/Q | 242 Ω

## Slide 4: SSR1 Mechanical design
Requirements:
Pressure rating 2 bar
Pressure sensitivity df/dP < 25 Hz/mbar
Tuning range ±130 kHz without yield
Facts:
Cavity material: 3.1 mm
Helium Vessel made of 316L
Transitions are Cu-Brazed (ANL)
Flanges are Conflat (3-3/8” & 6”)
All stiffeners are made of RRR40 Nb
Tuning
forces

## Slide 5: Pressure sensitivity – Vessel optimization
Circle Shape
R1
Tk
D
Various geometrical parameters of the helium vessel have been studied to meet the requirements for df/dP.
There are infinite solutions (e.g. the star on the plot).
Other considerations will define the design (ease of fabrication, tunability etc..)
The plot shows one of the studies for the ring diameter and vessel dome diameter.
Chart: df/dp (Hz/torr) vs. Vessel thickness (mm)
| 2 | 6 | 10
Ring125_D170 | 18.74 | 21.658 | 23.84
Ring125_D180 | -6.24 | 11.06 | 18.935
Ring125_D190 | -32.148 | 2.469 | 14.262
Ring125_D200 | -57.88 | -6.95 | 9.06
Ring133_D170 | 27.71 | 28.42 | 29.362
Ring133_D180 | 4.266 | 20.112 | 25
Ring133_D190 | -21.09 | 12.36 | 20.958
Ring133_D200 | -42.78 | 5.31 | 15.722
D170 | 24.35 | 31.74 | 33.528
D180 | -0.76 | 26.35 | 33.6
D190 | -20.9 | 19.83 | 26.285
D200 | -39.04 | 13.44 | 21.612
R1 = 125 mm, D = 200 mm, T = 7 mm
For example a solution is:

## Slide 6: Pressure sensitivity - analyses
Comsol multiphysics
df/dp ~ 4.9 Hz/Torr
Ansys multiphysics
df/dp ~ -1 Hz/Torr
Ansys mechanical (explained in next slide)
df/dp ~ 2.6 Hz/Torr
Figure shows deformations (enhanced x500) for a cavity under vacuum and Helium at 1 atm
Beam pipes deform only ~ 6 μm inward
df/dP < 10 Hz/torr
Deformations in high E and B regions balance out resulting in a small frequency shift
Comparison between analysis tools
High E
High B

## Slide 7
d4
d2
d3
d1
The cavity is constrained to the helium vessel in several locations (e.g. d1, d2, d3, d4,..)
After a first series of RF-mechanical coupled analyses, we can perform mechanical only analysis to predict df/dP.
The computation time is reduced considerably
In the specific case of SSR1, only 3 RF simulations (3 points of the plane) are needed to define the mathematical relation to have an estimation of df/dp function of the displacements on Rings (d3, d4) and beam pipes (d1, d2)
Mechanical analyses for df/dP estimation

## Slide 8: SSR1 Fabrication (Niowave-Roark, USA)
Power Coupler
port
Beam Pipe port
SST
Cu
Nb
Spoke with collars
10 resonators ordered, 2 received. Balance expected by end of 2011.
ANL development
Completed resonator

## Slide 9: Plan for the 10 resonators
Bulk BCP at ANL (1st already in process)
Hydrogen degassing at FNAL (10h at 600 C)
Light BCP at ANL
Vertical tests at FNAL (1st expected in January 2012)
Jacketing operations to start in March 2012
Jacketed tests in cryostat to start in June 2012