## Slide 1
LHC Crab Cavity Engineering Meeting
FNAL, May 30, 2013
LHC Crab Cryomodule
DOE-HEP SBIR Phase II
Terry Grimm

## Slide 2: SBIR Phase II
DOE-HEP Phase II SBIR
  1 million dollars over 2 years
Schedule
  Contract Start April 2013
  Year 1 progress report due Feb 2014
  Year 2 final report due March 2015
Start transition to Phase III in late 2014

## Slide 3: Crab Cavities for the LHC
Niowave became involved with crab cavities for the LHC first through DOE in collaboration with ODU, and later with the other designing groups.
4-rod Crab (Daresbury – Graeme Burt)
ODU/SLAC RF Dipole (ODU – Jean Delayen)
Quarter-Wave Crab (BNL – Ilan Ben-Zvi)

## Slide 4: Horizontal Cryomodule Assembly (500 MHz Multi-spoke)
He vessel with superinsulation
LN2 thermal shield
mu metal magnetic shield
insulating vacuum vessel
cavity high-pressure rinse
final cavity preparation in clean room

## Slide 5: LHC Crab Cryomodule Conceptual Design
Liquid He fill tube and exhaust
Nb cavity
Liquid He vessel
2K magnetic shield
Liquid N2 thermal shield
Mu-metal magnetic shield
Vacuum vessel
Power coupler
Three HOM couplers or pick-up antennas
Frequency tuner

## Slide 6: Cryomodule Critical Dimensions
The crabbing cavity shown in the drawings is the DOE-HEP SBIR funded prototype that has been built and room-temperature tested at Niowave in March 2012.
Once a new cavity with smaller diameter is developed, the cryomodule design will be changed accordingly.
beam-to-beam separation (194 mm)

## Slide 7: 3D Cryomodule View
beam tubes
cavity tuner
niobium cavity
RF power coupler

## Slide 8: In-Line Double Cavity Cryomodule Concept
Cryomodule concept can be extended for multiple cavities – shown here with two cavities in-line: separate He vessels and fill, separate low-temperature magnetic shield, but combined thermal shield and insulating vacuum.

## Slide 9: Room Temperature Measurements of the LHC Crab Cavity
Mode spectrum for the cavity measured before and after final welds
Room-temperature cavity Q confirms geometry factor within ~10%
Vacuum frequency shift measured (~300 kHz)

## Slide 10: 750 MHz Crab Cavity Vertical Dewar Cryotest Setup
Similar crab cavity geometry developed with ODU for an electron-ion collider
DOE-NP STTR project
Approximately half the size of the LHC cavity

## Slide 11: 750 MHz Crab Cavity Test Results
Chart: integrated voltage (MV)
| 0.10235990914076748 | 6.3845441087912E-2 | 4.9559839554378739E-2 | 0.15492799186891698 | 0.22653217339514642 | 0.2455443196347174 | 0.33123017321845477 | 0.37164636697274217 | 0.41699408221769635 | 0.43664640785843389 | 0.44170253496597955 | 0.43664640785843389 | 0.44170253496597955 | 0.45722491907244267 | 0.46251933410932772 | 0.47877326564101697 | 0.4927536974043325 | 0.50133715449626537 | 0.54029368527278732 | 0.54529296119056836 | 0.57561206952582944 | 0.6458473645269257
 | 246191017.492 | 264299572.0978 | 221981243.6813 | 257903284.0492 | 240816576.9426 | 235729423.3086 | 221981243.6813 | 210141475.9584 | 203123938.1907 | 182828734.8853 | 161871800.2211 | 145601613.5713 | 134696397.4494 | 119007924.4732 | 119597681.771 | 121445327.471 | 123080819.651 | 124106956.881 | 128987646.8218 | 129641917.3682 | 133756575.0295 | 144371283.3667
 | 0.0625 | 0.4 | 0.9625 | 1.2 | 1.425 | 2 | 2.5 | 3.75 | 10 | 12.5 | 100
The 750 MHz crab cavity reached an estimated maximum deflecting voltage >0.6 MV (radiation limited – no cavity quench).
multipacting barrier
pulsed conditioning progress
Notes: 11

## Slide 12: Next steps
HOM coupler design
Detailing of mechanical design
  Pressure-code compliance
  Fast and slow tuners
Field stability requirements
Assembly plan