## Slide 1: Target enclosures: pro & cons of various solution
M. Calviani (CERN)
With major contributions from: J. Hylen (FNAL), T. Ishida & T2K team (KEK/J-PARC), H. Vincke, C. Strabel, P. Vojtyla (CERN)
Brainstorming session
5th High Power Target Workshop
https://indico.fnal.gov/conferenceDisplay.py?confId=7870

## Slide 2: Disclaimer
This is not going to be a review of possible solutions, but a starting point for further discussions
Limited to few installations (sorry)
Complex matter, involving:
  Physics optimisation
  Engineering requirements
  Radiation protection & environmental protection (site dependent)
  Ventilation system design
  Material studies and R&D
  Project “strategic” decisions
  Installation/laboratory configuration

## Slide 3: Target installation types
Neutrino facilities
  Usually constituted either by long tunnels or shallow/deep trenches/chase
  Large volumes w/o shielding
Spallation sources
  Usually inside pits or enclosed in shielding blocks with ports for neutron beams
Radioactive beams sources
  Usually inside bunkers/halls as requires several “active” equipment around

## Slide 4: What do we mean by enclosure?
Area where target and other associated beam equipment are located during beam operation
In general the enclosure needs to be equipped and relatively accessible in case of equipment exchange
Primary line
Target
Beam focusing (if any)
Dump/absorber
~5/10 meters
~5/20 meters
Opening cover

## Slide 5: Enclosure atmosphere
Air
Easiest solution in terms of handling
Activation levels penalizing (high mass spallation)
Helium
Radiation only produces 3H (+ impurities-driven spallation products)
Complex handling and operation – specialized devices needed
Vacuum
Best for activation and corrosion
NOx formation/humid environment  radiation-accelerated corrosion
Optimal corrosion resistance
Cumbersome for operation and higher costs for the vessel
A priori...

## Slide 6: T2K experience
T2K chose to use a huge He-vessel to enclose all beam elements
Air-to-He environment is achieved by pumping down the whole volume to 50 Pa
Quite large mechanical constraints, but very successful operation with lots of lessons learnt

## Slide 7: Helium Vessel Enclosure at J-PARC Neutrino Beamline
Target Station(TS), Decay Volume(DV) & Beam Dump(BD) in a gigantic vacuum/helium vessel, made of carbon steel plates (water-cooled).
  Effective to prevent nitrogen oxide (NOx) production / oxidization, thus damages to the apparatus inside.
    We succeeded to use 1st apparatus for ~5 years without fatal troubles
  He gas filling after evacuation
    The entire structure was rigidly built with thick plates (100mm for TS / 16mm + anchors for DV / 200mm for BD) / welding with deep grooves.
  He circulation at TS: 1,300m3/h, inlet plays role as horn stripline cooling duct. No forced circulation for DV/BD so far (piping at BD for future use)
Decay Volume
Target Station
Beam Dump
Vessel filled w 1atm. He gas
L=~110m,V=1,300m3
OA2o
OA2.5o
Beam Transport
From RCS to MLF
6m-thick concrete wall
OA3o
Ishida-san & co. (JPARC)

## Slide 8: Helium Vessel Construction
Upstream DV
Oct.05’07
DV
Support anchors
Embedded in concrete wall
TS
BD
Top lids
(3 pieces of 120mm-thick Aluminum )
Graphite
blocks

## Slide 9: Evacuation / He-filling procedure
<100 Pa reached in a ~a week after vessel closure
Leakage in the vessel creates ~10-2-10-1 Pa*m3/s = 1~10 ppm O2/day
  Solved by keeping the He-vessel in overpressure
O2 contamination <100 ppm for entire beam period

## Slide 10: Vessel opening and issues
After operation, He is vented and filled with air – raise of HTO up to ~1 Bq/cm3
  In order to fix this dry air is blown from TS to absorber – it takes about 1 month to dry up inside – i.e. delay before access
T2K will try to fix it by performing an online dehumidification of the He gas
For more info, see NBI2012 presentation: (link)

## Slide 11: NuMI experience
NuMI target pile cooled with air
Kept at under pressure by sucking air via a passageway lateral to the DP
  To protect utility rooms and open shaft
  NuMI target hall deep, but “ran it an effectively shallow”
This method allows reduction of releases of short lived isotopes (but not enough for 41Ar)
See J. Hylen talk, this workshop

## Slide 12: NuMI experience
During NuMI lifetime several access to the target area are/have been required

## Slide 13
J. Hylen, NBI2012 (link)

## Slide 14: LBNE studies
Target pile NuMI-style with air recirculation, but DP with static He
  Short-lived isotopes strongly suppressed by using NuMI facilities as a huge “buffer tank”
  41Ar emissions evaluated by means of scaling up NuMI releases
    Uncertainty in extrapolation due to thermal neutrons
Extraction of air through a drier area (mitigation of tritium issue)

## Slide 15
J. Hylen

## Slide 16
J. Hylen

## Slide 17: CERN’s experience
CNGS – long tunnel, deep underground installation
  Tritium production has been a constant problem, which have been dealt with:
    Avoid “clean” water contact with tritiated air
    Modification of the ventilation system
      Access tunnel in overpressure rather than controlled leakage
From beam stop to access ~O(10 hours)
  No issues with short lived isotopes
Lessons learnt: in complex tunnel systems, the actual air-flow may be difficult to predict
  See H. Vincke NBI2012 presentation (link)

## Slide 18
Air releases of short lived isotopes not a problem, minimal impact by Ar41

## Slide 19: Comments from CERN point of view
Control of air path for new installations should follow the ISO17873:2004 with appropriate DP control
The use interconnected tunnels passing from different installation w/o pressure control would be difficult to accept
  Huge volume for the required DP
  Wet areas/sumps an issue

## Slide 20: TOF spallation target
Target installed in a vertical pit, no specific atmosphere control (i.e. air)
Extensive oxidation stains observed
Future upgrades will consider dehumidification/recirculation or Helium enclosure

## Slide 21: CERN studies
For both CENF and SHIP (and future projects) a He-vessel is sought:
  Shallow installation
    RP/environmental consideration
    Hydrogeological situation above the water acquifier
  Equipment protection and reliability
General situation for CERN’s releases
  We cannot add much more respecting the internally imposed limit of 10 mSv/y to the public (all installations!)
However (true for all installation): helium do not solve 3H problems (if present)!

## Slide 22: CERN studies
However (contrary to T2K) no vacuum vessel is presently considered:
  Collaboration with external company to study a system that would perform an online purification (goal ~few days) down to 0.1% air
    Seems to be possible with membrane and cryo traps
  Reduce costs and structural requirements
  No problem with expansion/shrinkage of vessel (i.e. structural alignment)

## Slide 23: Summary
Every facility has his own specific requirements and external conditions imposed by law or laboratory rules
Air allows operational flexibility that He (or vac) enclosure could not provide
He allows reducing issues associated with light spallation products (11C, 13N, 14,15O, 41Ar)
  Independently of the air treatment
  3H still produced, but less “radiological relevant” if released in air
QA always important, but particularly for He enclosures where He leakage would potentially create operational difficulties

## Slide 24: Discussion!