## Slide 1: Handling ESH Issues of a Water-cooled Proton Beam-on-Liquid Lithium Stripper Film Experiment
Claude Reed1, Jerry Nolen2,3, Yoichi Momozaki1, James Specht2,3, Dave Chojnowski1, Felix Marti3
1 Argonne National Laboratory, Nuclear Engineering Division
2 Argonne National Laboratory, Physics Division
3 Michigan State University, Facility for Rare Isotope Beams
5th High Power Targetry Workshop
Presented at
Fermi National Accelerator Laboratory
May 23rd 2014

## Slide 2: Outline
Background
Lithium and water hazard
LEDA source reconditioning and beam line design
Mating LEDA source to Li system
Proton beam-on-film experiment
Summary

## Slide 3: Background
3
20 kW beam on
  Stable operation under 20 kW load or ~5 MW/cm3 at the peak in 2003(1).
  Stable formation of ~50m/s, ~10 µm thick Li jet in 2011(2),(3).
High speed, thin Li jet in vacuum
Further demonstration of the liquid lithium stripper under a high thermal loading by a proton beam.
Next step
Liquid Li appears as an attractive option for high power beam applications.
Rev. Sci. Instrum. 76, 73501 (2005); http://dx.doi.org/10.1063/1.1942530
(2) JINST 4 P04005 doi:10.1088/1748-0221/4/04/P04005
(3) ANL/NE-11/01 (2011)

## Slide 4: Background
4
Use a beam from the Low Energy Demonstration Accelerator (LEDA) ion source (75 kA, 110 mA) for the beam-on-film test.
+
Many water-cooled components!

## Slide 5: Lithium and water hazard
ANL, USA, Lithium spill and fire, Lithium Processing Test Loop, 1979
  due to incompatible material and stress cracking from cold working.
Sandia National Lab. (SNL), USA, Lithium fire, LIquid Metal Integrated Test System (LIMITS), 2005?
  due to incompatible material.
SNL, USA, Lithium-water explosion, Plasma Materials Test Facility (PMTF), 2011
  due to use of brittle, non-Li compatible material as a water pressure boundary.
Status Report on Sandia Plasma Materials Test Facility (PMTF) and Actions after Li Fire on 26 Aug 2011, PFC Group Annual Meeting, 20-22 June 2012 - PPPL
ORPS: NA-SS-SNL-1000-2011-0007
Not limited to, but all Li/H2O boundaries must retain integrity under all conditions.
Broken flange!
Personal communication

## Slide 6: Lithium and water hazard
In LEDA + Li system:
  Hot liquid lithium in the vacuum chamber
  Water cooled plasma chamber
  Water cooled injector
  Water cooled turbo pumps
  Water cooled LEBT solenoids
  Water cooled apertures

## Slide 7: LEDA source re-conditioning and beam line design
Reconditioning, shake-down, new beam line design at MSU-FRIB.
7
LEDA source at MSU
First proton beam at 14 mA
Beam at aperture
Beam profile

## Slide 8: LEDA source re-conditioning and beam line design
8
Could image up to 4-5 mA @ 65 kV to 3-mm base-base spot size.
Final focusing using an Einzel lens for no-water near Li.

## Slide 9: Mating LEDA source to Li system
Overall layout in ALEX, Bldg. 370 at ANL.
9
LEDA source
Beam line
Li system
C-2: All metal containment designed for alkali metal experiments.
Top view
3.00 m
2.95 m
3.63 m

## Slide 10: Mating LEDA source to Li system
Extensive safety analysis for Li + water hazard.
10

## Slide 11: Mating LEDA source to Li system
Extensive safety analysis.
11
Note: all pressure ratings based on the assumed operating temperature of 93 C.
Plasma chamber body
  56.6 bar
Turbo pump
Flange
  56.6 bar
4 mm aperture
  49.1 bar
5 mm aperture
  49.1 bar
Plasma chamber solenoids
  56.6 bar
LEBT solenoid
  169 bar
Single wall isolation
Plasma chamber flange
  6420 bar
Injector mount
  277 bar (internal)
  13.2 bar (external)
Double wall isolation
Triple wall isolation

## Slide 12: Mating LEDA source to Li system
Reentrant shroud prevents external water leak Into C-2.
12

## Slide 13: Mating LEDA source to Li system
Additional safety features
  Apertures minimize Li ingress and potential water ingress in case of leakage.
  Gate valve closes if source side pressure increases due to potential water leakage to protect Li from water.
13
4 mm aperture
5 mm aperture
Pneumatic gate valve

## Slide 14: Mating LEDA source to Li system
Some pictures and beam profile.
14
Beam line without shroud
Li system in C-2
LEDA source
Beam profile
Achieved 3-mm base-base beam width at 4-5 mA, 65 keV at ANL; space charge effects at higher currents.

## Slide 15: Proton beam-on-film experiment
Lithium thin film stays intact with proton beam.
15
April 5;
front view (left),
back view (right)
Proton beam (65 kV, 4.6 mA, σ = 0.7 mm) on the liquid lithium film, ~ 10 μm thick, at 50 m/s.
Focusing variation via the Einzel lens. Film width ~15 mm.
Beam viewing via neon gas additive; ~5E-6 Torr total pressure.

## Slide 16: Proton beam-on-film experiment
16
Beam dump
Beam
Li valve position,
green line (closed)
Li valve position,
green line (open)
1
2
3
4
5
6
7
8
9
Beam dump zero point
Beam zero point
Beam on without Li flow 5:22
beam off while establishing Li flow 5:22-5:49
Li valve opened 5:37
Beam on with Li flow 5:49-
Beam manipulation
Lost beam 10:18-10:24
Beam on with Li flow
Li valve closed 11:01
Beam on without Li flow
Beam current data measured at beam dump.
Li film completely stopped beam!!

## Slide 17: Proton beam-on-film experiment
17
Movie
http://www.youtube.com/watch?v=qPwdYQbp3Bg&t=2m26s
Additional movie (evolution of the Li film)
http://www.youtube.com/watch?v=iOv1D5LaId8

## Slide 18: Proton beam-on-film experiment
18
Results
 | FRIB | Experiment | Ratio (Exp/FRIB)
Beam power (W) | 700 | 299 | 0.43
Beam σ (mm) | 0.62 | 0.70 | 1.17
Beam power/σ (W/mm) | 1129 | 427 | 0.38 (151 kW)
Linear power density ~38 % of the maximum power density at FRIB with a 400 kW of U at 200 MeV/u.
65 keV protons only penetrate 1.5 μm in the 10 μm thick Li film. The net effect would be a power density higher than FRIB by a factor 2 (~0.43 x 0.62/0.7 x 10/1.5).
Uncertainties: Faraday cup correction factor, beam fluorescence profile, effect of short range of protons.
Beam power: 4.6 mA x 65 keV = 299 W

## Slide 19: Summary
19
First time that a thin liquid lithium film (~ 10 μm) was successfully used to stop an ion beam with a high power deposition.
The 65 keV protons stopped in the first 2 μm depositing ~300 W on a beam spot with σ = 0.7 mm.
For FRIB we expect 700 W in full thickness (~10 μm) on a beam spot with σ = 0.62 mm.
This was the most important validation of the choice of liquid lithium as the charge stripper medium.

## Slide 20
20