## Slide 1: High Power Targets and Performance Optimization versus Costs or How much shall one pay for a useful neutron?
F. X. Gallmeier
5th High Power Targetry Workshop
May 20, 2014

## Slide 2: Outline
Illustration of neutron path
Neutron accounting
Improvement options
Second target station - an opportunity

## Slide 3: Path of Useful Neutron from Birth to Death
Proton
Detector
Sketch of CNCS

## Slide 4: Neutron Economy at SNS
1.4 MW SNS produces: 2 ×1017 n/s
Thermal neutrons at beamline start: 2×1012 n/s
Neutrons at sample position (white): 2×1011 n/s
Neutrons at sample (chopped): 2×1010 n/s
Neutrons scattered: 2×108 n/s
Neutrons counted: 5×107 n/s
Neutron counted/Neutrons produced: 3×10-10

## Slide 5: Costs Analysis
SNS construction cost: $ 1.4×109
Yearly SNS budget: $1.7×108
SNS expected life: 40 yrs
Yearly hours of operations: 5000h
Yearly counted neutrons: 9×1014 n/yr
Neutrons per dollar: 4×106 n/$

## Slide 6: Handles to Improve #neutrons/$
Beam power increase
Target/Moderator/Reflector optimization
Neutron optics optimization
Detector coverage
Background reduction
New instrument concept

## Slide 7: SNS Source Improvement
Next-generation IRP:
  Cadmium poison for decoupled moderators (increases IRP life from 6MWyr to 8 Mwyr)
  Coupled hydrogen moderator enlargement (increases flux output by 50%)
Enforce full para-hydrogen conversion in coupled moderator
Replacing of IRP light-water by heavy water (10-20% flux increases)
Increase power within two years to promised 1.4 MW
A factor 2 can be envisioned
Curtesy: Harada/JPARC

## Slide 8: Neutron optics improvements
Recent developments
  High m-value mirrors (m ≥ 7 today)
  True curved guides – elliptical, parabolic
  Guides may not be the answer – curved single mirrors (HFIR IMAGINE: 15 x 18 mm2  2x3mm2 with uniform divergence. Solution: 2 bandpass mirrors + 2 elliptical focusing mirrors)
Strategy
  Match new technologies to instrument requirements
  Test devices with collaborators (e.g. Wolter optics, K-B mirrors, novel combinations of guide shapes, adaptive optics)
CG1 measured and simulated guide exit
Compact SANS employing Wolter optic tested at HFIR
Notes: Structure in CG1 is real and largely expected based on simulation model. Specifics of installation and alignment, however, make prediction of detailed performance extremely difficult. - one of the reasons for in situ alignment and adjustment needed – (guide is 11 mm wide by 15 cm tall).

## Slide 9
Curtesy: Phil Bentley/ESS

## Slide 10: Working on Background Reduction
Elastic scattering
from Vanadium
Inelastic feature from
Vanadium
Spallation
Event every
16.7 ms
(1/60 Hz)
HYSPEC: Background tail ends about 3.5 ms beyond spallation event

## Slide 11
Before
Now
Wrap-around

## Slide 12
Elastic peak
inelastic signal
“Time-constant” Background
First indication of delayed neutron contribution in neutron scattering instrument
Also a photo-neutron based background is expected
curtesy: M. Harada/JPARC

## Slide 13: Second Target Station – a chance to do it better
A second target station uses the same accelerator frontend
A second target station allows to copy positive experience from first target station, and solve incidents of negative experience
A second target station can be complementary in instrumentation to a first target station
ISIS has demonstrated how this is done
SNS thinks heavily about STS
JPARC also has ideas of a second target station

## Slide 14: FTS+STS Baseline Parameters
Parameter | STS Short-Pulse | FTS Short-pulse
Power (kW) | 467 | 2000
Repetition Rate (Hz) | 10 | 50
Pulse Length (ms) | <1e-3 | <1e-3
Assumptions based on accelerator build-out to 2.8 MW power at 1.3 GeV proton energy according to PUP.

## Slide 15: What are the drivers for moderator performance?
Choice of target material: tantalum-clad tungsten (high atomic mass, high density, suppressed fission)
Compact proton beam footprint: 30 cm2
Intermediate energy proton beam:1.3 GeV proton will result in neutron yield of about 33
Bright compact neutron source: 10 cm x 10 cm high luminosity

## Slide 16: Choices of Moderator materials
Hydrogeneous materials for fast neutron slowing down and moderation
Liquids for heat extraction
Radiation resistance
Para-hydrogen moderator T=20 K
Ambient water as pre-moderator and ambient temperature moderator
Carbo-hydrates, ammonia?
ortho
para

## Slide 17: Coupled Moderator Parameter Space
x-z y-x z-y
Fixed parameters:
Viewed area: VIEWW x VIEWH
Proton beam area: PBW x PBH = 30 cm2
Moderator height: MBH = VIEWH
VIEWHxVIEWW Configurations: 10x10, 7x7, 5x5, 3x3, 2x2 cm
TZO
2*MBR
PBH
PMB
PMR
VIEWH
PMT
VIEWW

## Slide 18: Short Pulse Coupled Hydrogen Moderator Studies

## Slide 19: Coupled Moderator Performance
Gains in time-integrated and peak brightness of a factor of 5 are possible for SP-STS compared to FTS on a per unit power basis for moderators with 10x10cm viewed area
Another factor of 3.2 can be gained in brightness by reducing the viewed area to 2x2cm.

## Slide 20: Crossing new thresholds in instrument capabilities requires total optimization
> x100 Performance Gains
Source Parameters
Beam Transport
Sample
Detectors
Data Acquisition/Data Reduction
Data Analysis
Repetition Rate
Target
Moderators
Small Moderators to Small Samples
Size
Beam Divergence
Sample Environment
Spatial Resolution
Count Rates
Area
$$$
Integrated
Live Results
Computational Sciences
High Performance Computing
Theory
Polarization
Visualization
Curtesy: K. Herwig/ORNL
Notes: Science mission dictates the neutron phase space that is required at the sample position.
Instruments will likely be more narrow in what they can do – but do that much better in order to obtain these types of gains (e.g. smaller samples)

## Slide 21: STS small sample cold spectrometer multiplies gains across elements
Source
1.5
High Brightness Moderator
2.6
Beam Divergence
2
Repetition Rate Multiplication
12
Detector Coverage
3
280x Gain over CNCS (1.4MW)
Curtesy: K. Herwig/ORNL
Notes: Source gain is peak brightness 467 kW STS 10/10 cm2 moderator compared to 2MW FTS coupled moderator.

## Slide 22: Planning Suite of 19 instruments for STS
Instrument | Description | Length (m) | Sample size (cm) | Moderator Type | Moderator Size HxV (cm2) | Beamline
DIFFRACTION |  |  |  |  |  | 
NeSCRY | Magnetic diffraction for small crystal and epitaxial materials | 90 | 2 | Cold, coupled p-H2 | 5x5 | 14
 |  | 40 | 2 | Cold, decoupled p-H2 | 5x5 | 
VERDICT | Long-wavelength neutron diffractometer for magnetic structure determination similar to ISIS-TS2 WISH | 40 | 2 | Cold, coupled p-H2 | 5x53x3 | 13
HiRes | High resolution powder diffractometer | 100 - 120 | 3 | Cold, decoupled p-H2 | 7x7 | 20
EWALD | Macromolecule single crystal diffractometer (1 mg samples) | 90 | <0.1 | Cold, coupled p-H2 | 3x3 | 16
DYPOL | Macromolecule dynamically polarized single crystal diffraction | 90 | <0.1 | Cold, coupled p-H2 | 5X53x3 | 12
REFLECTOMETRY |  |  |  |  |  | 
TLR | Kinetics liquids reflectometer | 15-20 | 2 | Cold, coupled p-H2 | 5x53x6 | 2
mmLR | Small sample liquids reflectometer | 30-40 | 1 | Cold, coupled p-H2 | 3x3 | 4
M-STAR | Polarized neutron reflectometer | 20-30 | 2 | Cold, coupled p-H2 | 3X3 | 7
M-WASABI | Polarized reflectometer combined with GISANS | 20-30 | 2 | Cold, coupled p-H2 | 3x3 | 6
SANS |  |  |  |  |  | 
SWANS | High-resolution small and wide-angle neutron scattering. (Molecular ordering to nanostructures) | 20 | 1 | Cold, coupled p-H2 | 3x3 | 15
FLOODS | Flux Optimized Order-Disorder SANS. Fast kinetics and out-of-equilibrium behavior | 20-30 | 1 | Cold, coupled p-H2 | 3x3 | 5
INELASTIC/QUASI-ELASTIC |  |  |  |  |  | 
superCNCS (SBIS) | Cold neutron chopper spectrometer optimized for high flux on small samples (10 mg) and polarization | 60 – 120 | 1 | Cold, coupled p-H2 | 3x3 | 17
superLET | Cold neutron chopper spectrometer optimized for large single crystals and polarization | 25 | 5 | Cold, coupled p-H2 | 10x105x5 guide at 75 cm | 11
MiBARS | Mica-based very high resolution backscattering spectrometer | 60 | 3 | Cold, decoupled p-H2 | 7x7 | 19
WAVESS | Very broad dynamic range using wide-angle velocity selector as analyzer | 15-17 | 3 | Cold, decoupled p-H2 | 7x7 | 18
JANUS | Hybrid spectrometer (low-Q chopper spectrometer, backscattering analyzer spectrometer) | 50 | 3 | Thermal-Cold, decoupled | 7x7 | 10
CAMEA-type | Extreme environment/inverse geometry | 40-50 | 1 | Thermal-Cold, decoupled | 3x3 | 8
SPHIINX | SPHerical Indirect Inelastic Xtal spectrometer (70 meV elastic, 1% dw/w) | 35-40 | 3 | Thermal-Cold, decoupled | 7x7 | 9
EXTREME CONDITIONS |  |  |  |  |  | 
Zeemans | Versatile instrument designed for studies at the highest magnetic fields | 60 | 2 | Cold, coupled p-H2 | 5x53x6 | 1

## Slide 23: Conclusion
Power is only one of many wheels to improve performance/efficiency of a neutron source

## Slide 24: Backup slides

## Slide 25: ILL vs FRM2
Power:
60 MW vs 20 MW
3:1
Unperturbed thermal Neutron Flux in reflector:
1.5×1015 vs 8×1014
n/cm2/s
2:1