## Slide 1
LHC Hi-Lumi QXF
Options for Value Engineering
M. Anerella, J. Schmalzle, P. Kovach
July 17, 2015

## Slide 2: Motivation
From Ruben Carcagno (see below):
Total US-Hi Lumi Project net cost estimate = $222M
Total DOE funding expectation = $181M
$41M shortfall
QXF is $148M total inc. contingency for 20 cold masses
$7.4M per cold mass (most expensive ever?)
  Only $28M for Nb3Sn; $37M for remaining material ($1.8M / CM)
  $67M for labor ($3.4M / CM)
Production starts Jan 2018
All Value Engineering must be
evaluated ASAP

## Slide 3: Goals
Reduce assembly labor costs / time
Reduce material costs
preserve or improve quality (while achieving goals 1&2)

## Slide 4: Candidates previously proposed (see details in back-up slides)
Coils:
Solid formblock
  reduces assembly labor (cleaning and installation of many EDM blocks)
  likely reduces tooling cost (needs verification)
  improves quality via reduced quantity of parts, fewer tolerances to accumulate
Structure:
Eliminate masters
  reduces material cost due to elimination of machined parts
  reduces assembly labor due to fewer parts to handle at assembly
  improves quality via reduced quantity of parts, fewer tolerances to accumulate

## Slide 5: Other Candidates
Coils:
Eliminate curing of outer layer; install directly into reaction fixture
Employ silver plated bolts in the reaction fixture to eliminate application and cleaning of anti-seize compound (already implemented?)
Utilize commercial die sets to ensure parallel closing of reaction & impregnation fixtures, eliminating the three-step process of closing to a shim, then opening fixture to remove shim, and then closing again
Eliminate inner trace
Eliminate (resist incorporation of?) secondary operation of potting wires into coil extension; utilize mechanical strain relief instead
Structure:
Replace collar bolts with keys (intermittent spaces permit gap msmts)
Eliminate “Fuji film” inspection assembly
If deemed necessary, develop an optimized plan for magnetic shimming (i.e., avoid/minimize cost growth)

## Slide 6: Back-up slides

## Slide 7: QXF Baseline Design

## Slide 8
LHC Hi-Lumi QXF
Proposal for Collar / Yoke Assembly
(updated 7/17/15)
M. Anerella, J. Schmalzle, P. Kovach
July 10, 2015

## Slide 9: Proposed QXF magnet cross section
Masters are eliminated.
Bladders / load keys are between yoke and load pads.
Pads locate to collars at angled surfaces
(as masters did 2x)
Pads key directly to yokes

## Slide 10: Yoke shell sub-assembly
Load pad are pre-assembled in the yoke shell subassembly
Bolts secure load pads in retracted position. Bolts are installed at existing cutouts in shell.

## Slide 11: Collar pack insertion
Collar assembly supported on roller assemblies, roller tracks inserted in yoke holes (more on next slide)
Once collar assembly is in place, screw assemblies used to push pads into position against collars to increase space for bladder installation.
Note: requires holes in table base at bottom screw locations

## Slide 12: Collar pack insertion
Roller supports ready to accept collar pack
Collar pack on supports, ready for insertion.
Collar assembly installation complete

## Slide 13: Alternate tooling concept
Alternative (cheaper) insertion rail concept, simpler support bar sliding on low friction UHMW bar.

## Slide 14: Summary
Shell - yoke subassembly includes the load pads.
Masters eliminated:
  Increases alignment accuracy
  Reduces cost
Insertion of only collared coil assembly.
Requires only minor changes to tooling & procedures
  New yoke preloading beam
  New rollers / slides for collar assembly
  Other?

## Slide 15
LHC Hi-Lumi QXF
Proposal for Coil Impregnation
(updated 7/17/15)
M. Anerella, J. Schmalzle, P. Kovach
June 11, 2015

## Slide 16: Modified Impregnation Fixture Design
Replace top plate and EDM blocks with solid formblocks, ~2 m long sections, machined & honed
(see appendix for details)
0-ring seal to base plate
Mandrel blocks remain unchanged
Commercial die sets provide alignment of formblock to mandrel, ensure parallel closing of fixture

## Slide 17: Impact with respect to existing design
Liner is eliminated
Side bars and screws are eliminated
Pusher bars and screws are eliminated
Top plate is eliminated
* All changes reduce tolerances and/or reduce cost *
Mating surface is maintained to retain compatibility with reaction fixture plate

## Slide 18: Other (updated 7/17/15)
Vendor quote of 2.3 m parts is $52K each using tool steel, ~ $60K each in 304 sst
  Need to compare to existing costs of formblocks + top plate + liner + side bars + pusher bars
  4.6 m quotes in both materials are pending
Existing 4 m EDM formblocks can be recycled for 4.2 m reaction fixtures
Time for cleaning of formblocks between coils is significantly reduced

## Slide 19: Summary
Solid tooling is a well established, proven method for fabricating formblocks (all production RHIC tooling)
Elimination of parts and tighter tolerance capability (R .01 mm vs. .05 mm) can yield improved coil size & L-R asymmetry results
A seamless implementation is possible due to compatibility with existing tooling
Parts reduction should also yield significant cost savings
Labor savings should result due to reduced surfaces to clean and prepare with each coil

## Slide 20: Appendix Tooling Fabrication Steps

## Slide 21: Step 1 – initial milling of tooling halves & drilling holes* * some used for temporary bolting together of halves

## Slide 22: Step 2 – bolt halves together & gun drill to undersized radius

## Slide 23: Step 3 – separate and machine each half to larger undersized radius, accurately machine midplane and machine overall height

## Slide 24: Step 4 – bolt halves together and hone radius to final dimension
Ø ± 0.013 mm