## Slide 1: Beam Line HOM Absorber Design design, tests, concerns
Nikolay Solyak,
LCLS-II CM Interconnect FDR,
July 29, 2015

## Slide 2: Outline
  Motivation
  HOM power
  Beam Line Absorber design
  Tests at FLASH Sept.2008 and 2009
  Thermal simulations and Thermal Connection to 40 K Tube
  Final Remarks
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 3: LCLS-II (SCRF) Baseline Parameters
Parameter | symbol | nominal | range | units
Electron Energy | Ef | 4.0 | 2.0 - 4.14 | GeV
Bunch Charge | Qb | 100 | 10 - 300 | pC
Bunch Repetition Rate in Linac | fb | 0.62 | 0 - 0.93 | MHz
Average e- current in linac | Iavg | 0.062 | 0.0 - 0.3 | mA
Avg. e- beam power at linac end | Pav | 0.25 | 0 - 1.2 | MW
Norm. rms slice emittance at undulator | ge-s | 0.45 | 0.2 - 0.7 | m
Final peak current (at undulator) | Ipk | 1000 | 500 - 1500 | A
Final slice E-spread (rms, w/heater) | Es | 500 | 125 - 1500 | keV
RF frequency | fRF | 1.3 | - | GHz
Avg. CW RF gradient (powered cavities) | Eacc | 16 | - | MV/m
Avg. Cavity Q0 | Q0 | 2.7e10 | 1.5 - 5e10 | -
Photon energy range of SXR (SCRF) | Ephot | - | 0.2 - 1.3 | keV
Photon energy range of HXR (SCRF) | Ephot | - | 1 - 5 | keV
Photon energy range of HXR (Cu-RF) | Ephot | - | 1 - 25 | keV
240kW
0-1.2MW

## Slide 4
Motivation
15%
48%
29%
f [GHz]
1
10
100
1000
8 %
Modes under cut-off,
(R/Q) up to 160Ω /cavity
Propagating modes, (R/Q) up to ~ 5 Ω/cavity
f [GHz]
1
10
100
1000
1.3GHz
HOMs of the LCLS-II and XFEL cavity:
HOM couplers
Beam Line Absorber
CW mode: XFEL beam (200 pC @ 0.1 MHz @ σz = 25 µm): 0.6 W/CM
LCLS-II beam (300 pC @ 1 MHz @ σz = 25 µm): 13.8 W/CM
              (similar power for XFEL2000 parameters)

## Slide 5: HOMs and Wakes in LCLS-II SC Linac: Steady-state losses
In LCLS-II, HOM's generated by the beam will add to the power load, especially in the last linac (L3), where the peak current is highest.
Ceramic absorber (between CMs , tied to 50K)  to absorb propagating HOM power >85%
The HOM power generated by the beam is P~ Q2·frep. The nominal charge Q = 100 pC; however, the combination Q = 300 pC, frep = 1 MHz, will generate the highest HOM power
The beam (Q = 300 pC, frep = 1 MHz) loses 7.7, 10.7, 13.8 W/CM in L1, L2, L3 (except for first two CMs)
=25µm
[V/pC/CM],
(Weiland, Zagorodnov)

## Slide 6: Transient Wakes
For a short bunch passing through a periodic structure, it takes on the order of the catch-up distance, =, to reach the steady-state wake. For L3 taking a = 3.5 cm &= 25 µm, zcu = 25m
When the beam enters the first CM of L3, the first cells loss factor is higher (see LCLS-II TN-13-04). In the first four CMs of L3 losses are: 29.5, 14.5, 13.8, 13.8 W
Direct calculation of the transient wake is difficult to do because of the huge number of mesh points involved. However, G. Stupakov /SLAC has obtained the transient wake with Echo using scaling law.

## Slide 7: Beam Line Absorber
Ceramic Ring: Ø 90mm
Length 50 mm
Thickness 10 mm
Lossy ceramic
Mechanical design
Estimated absorption efficiency for the periodic structure: one BLA/cryomodule is 83% (M. Dohlus)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 8: HOM BLA Design

## Slide 9: Production
BLA with protecting Al-bars after shipment to DESY.
Cu coating inside:
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 10
  Heat conductivity at 40K > 50 W/(m*K)
  DC resistivity(across the cylinder) < 200MΩ at 70K
  Measured absorption properties:
    Ceradyne CA137
    ε<30 @ tgδ> 0.1 for 5 GHz < f < 40 GHz
    Sienna Technologies AlN STL-150D
  ε<30 @ tgδ> 0.4 for 5 GHz < f < 12 GHz
Ohm-meter
Ceramic cylinder
Al discs
Isolator
Production: Spec for the ceramics:
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 11: Lossy Ceramics: Ceradyne Inc.
    Ceradyne CA137
    We used λ=70W/m·K in our modeling,
    Will be redone with actual T dependence
CERADYNE does not produced the rings anymore (Jacek)

## Slide 12: Lossy Ceramics:

## Slide 13: Wakefield power losses in CM models
Ray Tracing (diffusion) model - M. Dohlus
Scattering matrix approach - K. Bane/ G.Stupakov
Simple Analytical Estimation using diffusion approach.(V.Yakovlev / A.Saini)

## Slide 14: Distribution of power losses in CM (diffusion model)
 | Pcav (W) | Pbellow (W) | Pabsorb (W)
Cu bellow | 0.07 | 0.76 | 13.0
SS bellow | 0.03 | 7.6 | 6.2
Distribution of power losses in CM
Power dissipation at 2K ( inside the cavity) is negligible.
Most of HOM power is deposited to absorber in case of copper bellow.
For SS below ~50% of HOM power is absorbed in bellows.
A.Saini
Q: How HOM power generated in transition CM are distributed along the string of CMs? averaged over string.

## Slide 15: S-matrix model (K.Bane, SLAC)
At a number of discrete frequencies, 4, 8, 12, 16, 20 and 40 GHz, we used the field solver to calculate the scattering matrix for each element type (cavity, bellows, drifts and absorber) for all TM0n monopole modes propagating in the beam pipe at each respective frequency
Radial geometries of the cavity, bellows and absorber with field plots (|E| for cavities; |H| for others) from HFSS simulations at 4 GHz and 20 GHz, with TM01 input from the left.
Conclusion: Two complementary approaches provide confidence in the effectiveness of the beamline HOM absorbers. Only a few percent HOM power will be lost at 2K.

## Slide 16: Test Setup at FLASH
  2 Beam Tests in September 2008 and 2009
  Computer modeling for the location of BLA (M. Dohlus):
  15% of the HOM power should be absorbed in the BLA (?)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 17
Chart: Time
  High current run at TTF-II in 2008
  HOM Power in ACC6
  Monitored Temperature
ΔT=1.1K
Braid cross-section (Cu OFH)= 74mm2
Heat conductance of the braid :
Sensor T1
Sensor T2
Sensor T0 tube (40K)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 18: 9 mA run in 2009
Chart: time [h]
  ACC6
  Monitored BLA Temperature
2.5 K
<1.7 W>
  Measured and calculated absorbed power in two tests
 | Sept.08 | Sept.09
Computed Absorbed Power [W] | 0.180 | 0.255
Measured Absorbed Power [W] | 0.143 (-20%) | 0.325 (+27%)
Accuracy of measurements?
Accuracy of simulation?
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 19: Thermal connection Beam Absorber design (XFEL)
With XFEL proposed thermal connection (S ~ 3 cm2) for 3W Tc=59 K when the He tube is at 50 K.
For 30 W (max in 1st CM in L3) dissipated HOM power the highest temperature of the ceramic ring = 230 K  will be improve for LCLS-II CM.
Remaining design issues:
  Larger cross-section of stub? => 4-5 cm2
  Weight = 21 kg. Need support?
.
Thermal connection made of a copper stub, terminated on each end with short braid, eliminating mechanical forces during the cool down and warm up cycles.
Absorbing ceramics ring
(Courtesy of J.Sekutowicz)
50K
59K
XFEL Heat: 3W
Computer modeling by T.Ramm (DESY)

## Slide 20: Thermal simulations
Maximum power dissipation ~30W (1st CM in L3)  Should be ~15 W/CM average ?
Proposed copper stub cross-section ~4-5cm2 will provide T ceramics < 150 K
Thermal stresses analysis (I.Gonin):
  Max stresses at Cu-Ceramic brazing joint, acceptable for P<30W
ΔT=28K
T=70K
Copper RRR=100
Ceramics λ=70W/mK
Ring = Ø90mm
Length=50mm
Thickness=10mm
S=3.6cm2
S=7.5cm2
S=15cm2

## Slide 21: Thermal Connection to 40K Tube
  It is rather complicated due to very limited space between cryomodules.
  Modeling by T. Ramm showed that thermal connection is not a trivial part of the BLA.
2.2 K forward
5 K forward
40 K forward
2-phase tube:
2 K, Gas Return Tube
80 K, Return
8 K, Return
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 22: Supporting HOM Absorber
XFEL proposal for support

## Slide 23: Status of the HOM beamline Absorber
LCLS-II adopted Eu-XFEL HOM Absorber design:
  Capable to absorb up to 100W of HOM power with spectrum > 1THz
  High Absorbing efficiency > 85%.
  R&D program and several design iteration since TESLA era.
  Industrial studies for XFEL, improvements on absorbing materials, brazing, cleaning.
  Tested with beam at FLASH (2008/2009); good agreement with simulation
  - Minor issues (cleaning, support in CM, thermal straps) will be finalized. Work in collaboration with XFEL team.
Procurement (JLAB):
Permission from DESY to use HOM absorber design received
Technical information and quotation from vendor (INS-Swierk in Poland)
  - Drawings, specs, cleaning and QA/QC docs.
- Quotation for 1 and 35 units.
Ready to start procurement for series production (35 units)

## Slide 24: Remarks
HOM Beamline Absorber design for LCLS-II project is based on tested design, developed for a decades and modified for XFEL. Parameters meet LCLS-II requirements.
LCLS-II CW operation produces high cryogenic losses. It requires good thermo-connections to remove heat and keep temperature under control. Thermal simulations in progress to define losses and finalize configuration of the thermal braids and connections.
Design Concerns:
  Ceramics loss tangent was measured up to 40 GHz. No data for higher frequencies, where major HOM power is expected.
  Diameter of ceramic ring is parameter for optimization of efficiency
  Braid cross-section is defined by L3 HOM power level. Can be reduced in L1 and L2, where power level is smaller.
Design Concerns (based on production experience, see Jacek slides in appendix):
  Permeability (µr<1.16)
  Copper plating and adhesion
  Cleaning issues

## Slide 25: Acknowledges
Thanks
Jacek Sekutowicz and Martin Dohlus for provided materials
Fermilab, JLAB and SLAC team
Ivan Gonin, Timergali Khabiboulline, Andrei Lunin, Slava Yakovlev, Arun Saini,
Tug Arkan, Yuri Orlov for help with simulations, design and discussiom

## Slide 26: Slides fro Jacek Sekutowicz presentation at SLAC
Back-up slides

## Slide 27: Production
DESY Experience and concerns
Vacuum
  All BLAs undergo leak test, performed by the vendor. 84 of 85 produced BLAs have passed this acceptance test.
  One would expect that the vacuum oven brazing of ceramic ring to Cu-stub at 950 C and Cu-stub to Stainless Steel at 1050 C
  and the Cu-coated housing heat treatment in 450C (1h) should make BLAs very clean. This is not the case and an additional cleaning is performed at DESY. It is very time consuming and not always successful. There is mainly a problem with masses 40-100. The partial pressures are rather factor of 100 than factor of 1000 smaller than the total pressure.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 28: Production
Experience and concerns
Vacuum, cont.
Disassembly +Visual, Mechanical and Cu-layer inspection
Cleaning of rings:
  Cleaning in an ultrasonic bath (containing organic surfactants ?)
  Rinsing with ultrapure water.
  Drying in 55 C.
  Baking in vacuum, T= 300 – 600 C.
Permeability test of the housing
Cleaning of the housing:
Cleaning in ultrasonic bath
Rinse with ultrapure water
Rinse with isopropanol
Drying in 55 C
Installation of the ring in the housing
…………………...
Mass spectrum test.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 29: Production
Spec for Stainless Steel
  For flanges 316LN SS ESR (1.4429)
  Housing and bellows 316LN (1.4435)
Vacuum spec:
No outgassing from ceramics (accordingly to the material properties description by vendors)
The integral leak rate has to be ≤ 1·10-10 mbar·l·sec-1
To ensure that BLA is hydrocarbons free, two conditions have to be fulfilled for the outgassing:
For a total pressure of 10-7 mbar
The sum of all partial pressures of masses from 45 to 100 must be less than 10-3 of the total pressure.
Permeability spec:
µr ≤ 1.05 later less conservative 1.16
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 30: Production
Experience and concerns, cont.
Permeability
Good adhesion of the Cu-coating requires an interlayer of Nickel.
The 1st delivery had this layer of the order of 3+µm, adhesion was very good but the thick Ni layer made permeability, µr , significantly ≥ 1.05. All with µr > 1.16 have been sent back for re-coating.
DESY requested to keep µr ≤ 1.16 (much less conservative value).
  The thickness of Ni layer was reduced to ca. 1µm.
  These BLAs had still good adhesion and µr ≤ 1.12.
Then the thickness of Ni layer has been reduced second time to 0.3-0.7µm(??). µr dropped below 1.04, but adhesion was poor in convolutions of bellows, peeling off was observed in many BLAs.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 31
Poor adhesion observed at DESY, on January 30th and on April 2nd, 2015
Production
Experience and concerns
  All these BLAs have been sent back to vendor for re-coating.
  These which were sent back to DESY have good adhesion and low µr.
Permeability, cont.

## Slide 32
      In two tests we observed absorption of the high frequency HOMs
      The amount of HOM power was close to the calculated power
      Cleaning is still time consuming
      Issue with adhesion and µr seems to be solved
  Final Remarks

## Slide 33
No CSR here
See PRD:
LCLSII-2.4-PR-0041
Linac RF and Compression
48
48