## Slide 1: Reentrant Cavity for Low Mass Axion Search
Akash Dixit
Microwave Cavity Design for Axion Searches (LLNL)
August 2015

## Slide 2: Outline
Inductive coupling to field generated by axions in external B
Reentrant cavity geometry
Cavity simulation (COMSOL)
  Resonant Frequency
  Field distribution
Prototype Cavity
  Tuning

## Slide 3: Inductive Coupling
P. Sikivie, N. Sullivan, D.B. Tanner (Florida U.). Oct 31, 2013. 5 pp. Phys.Rev.Lett. 112 (2014) 13, 131301
Use inductor to capture the flux generated by
Notes: The electric field term in the Maxwell equation can be neglected since the 1/m_a is larger than the extent of the external B field

## Slide 4: Cavity Geometry
Notes: Cylindrical cavity with this feature size corresponds to 1.5 GHz
Reentrant design: L remains constant, but increase C to lower resonant frequency

## Slide 5: Magnetic Field Distribution
Notes: Fermilab teslatron 4 dimension give 140MHz resonance

## Slide 6: Field Magnitude
Notes: Electric field is concentrated to parallel plate region, falls of rapidly outside.
Inductive and capacitive parts integrated but are spatially separated

## Slide 7: Squashed Cavity Prototype

## Slide 8: Prototype
(Left) Reentrant Cavity open.
(Center) Cap with transmitter and receiver
(Right) Assembled cavity with spectrum analyzer
Notes: R ~ 40mm
r_i ~ 15mm

## Slide 10: Cavity Tuning
Brass tuning rod inserted into cavity
Notes: Use a rod to vary the gap between reentrant region and bottom of cavity

## Slide 11: Cavity Tuning
Q≳200

## Slide 12: Resonant Frequency vs Gap
Simulation
Data

## Slide 13: Conclusions/Future
Exotic axion current produces magnetic field
Flux detected using reentrant cavity
Cavity tuning
  Vary gap by piezoeletrics
Inner plunger