## Slide 1: Technical Design of the Resonant Extraction for the Mu2e experiment
Vladimir Nagaslaev
Technical Design Peer Review
August 25-27, 2015

## Slide 2: Introduction: Motivation
Mu2e Experiment:
  Pulsed beam
  Detector dead time - 700ns
  Detector Live time - 995ns
Slow extraction is important to deliver this time structure

## Slide 3: Introduction: Debuncher Ring
Circumference | 505m
#FODO cells | 57
Max Beta | 15m
Operating point | 9.763 / 9.769
Max Intensity | 3e8 p
Acceptance (unnorm.) | 36 pm
Injection
Extraction to Accumulator
Regular FODO, 60°per cell
Zero Dispersion in SS
Betas optimized for aperture
Rapid 6D stochastic cooling
RF bunch rotation/debunching
Transfer to Accumulator
Debuncher lattice functions

## Slide 4: Implementation of RE in the DR
New injection point
Extraction in SS30
ESS
2 families of Sext.
A family of tune Quads
Magnetic septa
Dynamic orbit control
Abort line
RFKO system
Spill monitoring
Spill regulation
3rd Integer resonance
Qx/Qy=9.650/9.735
SS10-60
SS40-50
SS20-30
RFKO kicker

## Slide 5: Requirements
Parameter | Design | Limit
Length of slow spill period | 54 ms | >20 ms
Average intensity per pulse on target | 31 Mp | <50 Mp
Maximum variation of pulse intensity on target | ±50% | ±50%
Mu2e Proton Beam Requirements (doc-1105)
Extraction efficiency | 98% | 
Unextracted left over | <5% | 
Additional Requirements

## Slide 6: Beam scenario in the Delivery Ring (DR)
Parameter | Value | Units
MI Cycle time | 1.333 | sec
Number of spills per MI cycle | 8 | 
Number of protons per micro-pulse | 3.1×107 | protons
Maximum DR Beam Intensity | 1.0×1012 | protons
Instantaneous spill rate | 18.5×1012 | protons/sec
Average spill rate | 6.0×1012 | protons/sec
Duty Factor (Total Spill Time ÷ MI Cycle Length) | 32 | %
Duration of each spill | 54 | msec
Spill On Time per MI cycle | 497 | msec
Spill Off Time per MI cycle | 836 | msec
Time Gap between spills | 5 | msec

## Slide 7: Technical and operational risks
Technical Risks (extraction specific)
  High losses
    Large effective thickness of ESS planes
    Insufficient kick in the ESS
    Inadequate ESS alignment
    Inadequate orbit control
  High spill variations
    Regulation is not fast enough
    Regulation is not deep enough
    Insufficient RFKO power
  Insufficient aperture
  Magnet strengths are not sufficient
  Magnet ramping capabilities are insufficient
  Insufficient machine diagnostics
  Substantial fraction of the beam not extracted
  Beam instabilities
Operational risks
  Radiation and machine protection

## Slide 8: Path to satisfy the requirements and address risks
Develop the model/design
  Determine the optimal parameter space
  Determine necessary hardware and specifications
  Identify key elements of the design that are necessary to satisfy requirements
  Satisfy machine stability conditions
Verify design: simulations/prototyping/beam-tests
Prepare the Ring (aperture, diagnostics, lattice)
Ensure fabrication/installation satisfy the specs
Address risks:
  Evaluate and reserve back up options when appropriate
  Include in the design or pre-mitigate when necessary

## Slide 9: Physics model of the Resonant Extraction
Theoretical model
Simplified parametric model
Tracking simulations
  Orbit
  Synergia
  MARS
Beam studies
Machine operation issues
  Stability
  Optics design
Physics model of the Resonant Extraction

## Slide 10: Theoretical model of Resonant Extraction
Hamiltonian:
Separatix conditions:
with:
L.Michelotti: “Preliminaries toward studying resonant extraction from the Debuncher”, 2010
For optimal orientation f0=-p/6:
and

## Slide 11: Parametric model of the RE, application
V.Nagaslaev, L.Michelotti: “Parameter Space Optimization For The Third Integer Resonant Extraction.”, 2012
Current x-position X1 and x-position after 3 turns, X2 as functions of parameter r.
Semi-analytical extension of the model:
Geometrical losses vs beta-function at ESS
Geometrical losses vs machine acceptance

## Slide 12: Synergia tracking simulations
We adopted Synergia package for the tracking simulations:
  RF fields; RFKO fields
  DEX bump with ramping
  Tune ramping; full spill tracking
  Aperture definition
  Substantial speed up
Main results include:
  Full spill simulations
  Ramping curves
  Extracted beam samples at ESS
  DEX bump optimization
  RFKO heating rates
Extracted beam footprint, DEX bump off
Extracted beam footprint, DEX bump on
  Performance benchmarked with earlier ORBIT results
  No known physics observed to impact performance.

## Slide 13: Tracking simulations with MARS
Tracking extracted beam with MARS code:
  Tracking particles in media and DC fields
  Radiation levels, Residual activation, Energy deposition, etc
  Essential for beam loss calculations and geometry optimization
Plot:
Total beam losses
Narrow angle spread beam
Losses vs beam misalignment

## Slide 14: Machine operation issues: Space Charge (SC)
Laslett tune shift:
 0.01
With dispersive effects QSC  0.007
Not an issue if approaching the resonance from below

## Slide 15: Machine operation issues: Instabilities
DR intensity increases ~105
Instabilities?
  TMCI
  Weak head-tail
  Electron cloud
  Microwave
  IBS
Considered in much more challenging version of Mu2e with 24kW beam power. Not nearly an issue for the 8kW
[ A.Burov , BeamStability_Mu2e.pdf ]

## Slide 16: Machine operation issues: Optics redesign
Optics redesign
  Smoothing optics
  Increasing bX at ESS1
Existing optics
“Smoothed” optics
Beta-bump optics
Difficulties with implementing a large beta-bump
Currently we consider only smoothed optics design with possibly a modest beta-bump, not a part of the project baseline.

## Slide 17: Magnet specifications and definition
Magnets and Power Supplies
Tune ramping quads
Sextupole magnets
Dynamic (DEX) bump dipoles

## Slide 18: Magnets: Tune ramping quads
Locations:
0-harmonic circuit: 3 quads in the middle of each SS. Not the only possible choice.
Strengths:
Ramps:
The tune ramp curve was calculated from the linear spill tune curve defined in Synergia.
Magnet and PS Specs:
Field distortions <1%
Stability <0.5%
Ripple <0.05%

## Slide 19: Magnets: Tune ramping quads
Choice of magnet types:
CQA type, available in storage. Air cooled.
Power supplies:
PS design is an extension of the existing
Booster PS design. Low risk.
Magnet tests performed:
Magnet performs very well on the ramp.
Field delay of ~0.1ms detected with SS beam pipe

## Slide 20: Magnets: Sextupoles
Strengths
B”L=80 T/m
Would like to have 2 orthogonal families of magnets
FODO cell PA 60° is ideal for adding up
Choice of locations available in SS50 and SS10-60
Noticeable difference Left-Right
Best choice: 10R+50L
SS 10: Left and Right
SS 50: Left and Right
SS 60: Left and Right

## Slide 21: Magnets: Sextupoles
Ramps: There is practically no cost difference between DC and AC options. It may be useful to reserve ramping capability, e.g. to adjust separatrix orientation instead of orbit control
Magnet choice: Existing design of ISA magnets is suitable, but no spares – will have to build them.
Water cooling is required.
Power supplies: PS design is an extension of the existing Booster PS design. Low risk.
Magnet and PS Specs:
Field distortions < 1%
Stability < 0.5%
Ripple < 1%

## Slide 22: Magnets: DEX bump
Locations: Very tight space in SS30 limits the choice of trim locations. Substantial orbit shifts, in particular, at Q205 is a concern.
Kick:
Strengths: BLMax=0.014Tm
Ramps: Calculated to keep the orbit angle at ESS1 constant.
2Q10
2Q7
2Q5
3Q0
3Q3
3Q5
H210
H206
H301
H305
1cm
0.4mR

## Slide 23: Magnets: DEX bump
Magnet choice: Debuncher style NDB. Air cooling is sufficient.
Power supplies: Only 7A , but needs lots of voltage to drive the fast ramp. Splitting 2 coils in parallel, augmenting the PS with the 350V regulation.
Magnet testing: FEA analysis show that magnet should perform well in the AC mode. However in the case of distorted lamination issues may appear, therefore testing was recommended. Tests are in progress now.
Magnet and PS Specs:
Field distortions < 1%
Stability < 1%
Ripple < 1%

## Slide 24: Transverse RF Knock-Out (RFKO)
Transverse RF Knock-Out (RFKO)
Overview
Theory and simulations
Measurements

## Slide 25: RF Knock-Out – Overview
Transverse RFKO- fast betatron beam heating
We will use transverse RFKO for the regulation of fast spill rate ripples.
Simulations show that 1uR kick at max power is sufficient for fast spill regulation. (!?)
Calculations of the emittance growth rate (EGR) are consistent with simulations and beam measurements.
The kicker waveform has to be FM-modulated with the BW covering the beam tune spread.
Spill regulation is made through regulating the RFKO power.
We will use the old Tevatron damper kicker. It’s already installed and tested with beam.

## Slide 26: RF Knock-Out – Theory and simulations
Two types of modulation were studied in tracking simulations: linear chirp and random “colored” noise. Performance is very similar.
Emittance growth rate (EGR) is the most essential characteristic of the RFKO heating.
Beam tune spread and EGR in narrow DQ bins
Tune distribution and emittance growth rates in narrow BW:
proportional to occupancy
close performance
V.Nagaslaev et al., FERMILAB-CONF-11-475-A

## Slide 27: RF Knock-Out – Theory and simulations
Beam tune spread and EGR in wide DQ bins
Tune distribution and emittance growth rates with wide BW:
~1/width
What if the tune width is dominated by the Space Charge?
Tune width due to the SC alone does not provide any mixing, so EGR=0

## Slide 28: RF Knock-Out – Theory and simulations
Cx=2; SC is off Phase space after 1000 turns
Cx=0; SC is on Phase space after EACH of 1000 turns

## Slide 29: RF Knock-Out – Comparing with measurements
EGR(Orbit)=33p mm-mr/sec
60p mm-mr/sec
@ 25W+25W
Orbit
FM width, kHz
EGR, p m/sec
EGR measurement in the Debuncher ring:
Difficult measurements
Final results consistent with calculations

## Slide 30: RFKO Summary
RFKO emittance growth is inversely proportional to the beam tune spread
RFKO needs non-zero chromaticity and chromatic tune spread
Chromatic tune spread should be large enough to ensure fast mixing
Calculated emittance growth rates are consistent with simulations and beam measurements

## Slide 31: Spill Control
Spill Control
Simulations
Regulation logic
Spill Monitoring

## Slide 32: Spill Control system
Required: spill uniformity at the level of ±50%
On average spill is controlled by the tune ramping quad circuit
We plan to regulate fast spill variations with the RFKO kicker
RFKO is fast and proved to be very effective in slow extraction for medical applications
We are cautiously optimistic about use of.
Early simulations of the RFKO regulation with ORBIT:
  No regulation when spill rate is high
  Large variations
  High statistical noise

## Slide 33: Spill Control system
RFKO regulation simulations with Synergia:
  Regulation responds to 10% increase in the reference spill rate
  Large variations
  High statistical noise
Proportional regulation seems to do the job, but it produces large oscillations due to the beam response latency and overregulation

## Slide 34: Spill Control system: overregulation
Oscillations in the spill rate appear as a result of beam response latency and overregulation with proportional loop P
This can be alleviated by using the derivative regulation loop D
Or a combination of P and D
Derivative loop has a “prediction” power
and therefore has a potential to smoothen
oscillations. Problem of tracking simulations is that D signal is intrinsically very noisy. Same problem may occur if the SM sensitivity is limited.

## Slide 35: Spill Control system: noise-free simulations
For practical purposes of the electronics FB simulations we developed a simplified NOISE-FREE semi-analytical model of RE:
Beam distribution is assumed to have a Gaussian shape limited by the separatrix size A(t):
On each step recalculate:
  New eX
  New A(t)
  New part of beam outside of the separatrix
  New extracted beam
  Spill Monitor response
  Spill error signal
  Regulation gain
  RFKO power
The model is now employed for the hardware optimizations

## Slide 36: Spill Control system: regulation topology
Learning function filter
(feedforward)
+
+
PID filter
(feedback)
Spill Mon
Ideal Spill
-
+
e
Spill Mon
AM Signal
External Generator
FM Signal
Done in uP
And FPGA
Tune Quads
Very flexible and adaptive system
Based on past experience with MI SE

## Slide 37: Spill Monitoring
Dedicated WCM device for SM
  Enhanced sensitivity
  Beam tested
  Ready for use
Will use DR DCCT for additional I-loop input
Will need additional instrument for the D-loop input. Plan to use the Extinction Monitor output.

## Slide 38: Electrostatic Septum Design
Electrostatic Septum Design
Design considerations
Beam losses budget
Prototyping
Full scale prototype

## Slide 39: ESS design considerations: foils
MARS:
  100u dia wires; 50u foils
  Conservative case
  Narrow angle spread beam
  No significant advantage
Red- 100m wires; Green- 50m foils
Total losses vs beam angle.
Foils or wires?
Would the foils stay flat?
Would a wire be destroyed by a single spark?
The choice does not appear to be obvious, but at this point we prefer foils as a more mechanically stable option

## Slide 40: ESS design considerations: pre-scattering
Losses predominantly occur for those particles that pass through the septum plane at low angle
These particles can be deflected to a small angle by the diffuser plane in front of the septum plane
Works best with low density materials (e.g. Carbon)
Mo foil plane can also be effective with foil spacing of 20mm
50u foils, 2.6mm spacing:
Green– with diffuser; Red – without diffuser
Total losses vs beam angle.
Optimal geometry for the diffuser
We reserve 0.5m of frame length in front of the foil plane of ESS1 for the diffuser.
Do we need a diffuser?

## Slide 41: ESS design considerations: septa lengths
  Losses are most significant in ESS1
  Losses grow with ESS1 length due to the beam angle spread
  Performance can be improved by making L1 < L2
ESS1/ESS2 length ratio:
Purple-0.5m/2.5m; Blue-0.7m/2.3m; Green-1m/2m; Red-1.5m/1.5m
MARS:
Total losses vs beam angle.
Practical choice: L1=1.25m (+0.5m diffuser)
and L2=1.75m leads to equal total vessel lengths. This makes design of two septa fully interchangeable.
What’s the optimum ESS length ratio?

## Slide 42: ESS alignment and flatness
Optimal ESS alignment angle
Losses sensitive to misalignment or wide angle spread
Flatness is most important in first part of ESS1
Small positive bend acceptable in the end of ESS1
Design should allow flipping the frames
It might be beneficial to introduce a small positive bend in the end of ESS1
Motion control better than 50u

## Slide 43: ESS design considerations: ions
Clearing electrodes required (up to 10kV)
Allowed spacing = 2.6 mm center-center
It is believed that if ions created in residual gas are pulled into the strong field gap, they assist spark generation. Field penetration from the ESS gap into the area of high density proton beam should be avoided even if there is a broken foil.
How to minimize effect of ions?

## Slide 44: ESS Design studies overview
Foil strength, yield
Attaching foils: crimping, brazing
Foil stretching, removal, assembly
Foil flatness
High voltage studies
Need to do the engineering studies:

## Slide 45: ESS prototyping
Foil attachment
Stretching
Test flatness
Completed
“Prototype-I”

## Slide 46: ESS prototyping
Stretching prototype
Foil attachment
Foil assembly techniques
Test flatness
In progress
See presentation of M.Alvarez

## Slide 47: ESS prototyping
HV Prototype
Vacuum facility- NWA

## Slide 48: ESS prototyping
HV Prototype
Foil breaking limit
Cathode material, handling
Feedthrough
Foil materials
Conditioning techniques
Period of extremely hard conditions
Lots of interesting observations
In progress
See presentation of M.Alvarez
R=3.5u
R=26u

## Slide 49: ESS prototyping
Large scale prototype
Working towards the full scale prototype
Test design solutions in real scale
Satisfy ESS specifications
Preproduction prototype
May reuse parts in production
See presentation of D.Tinsley’s

## Slide 50: Conclusions

## Slide 51: Conclusions
The physics model of slow extraction has been developed to determine the key system parameters and hardware specs
We have a plan of building the new hardware and a plan to ensure the performance parameters will be met.
Material and design studies for the ESS with the foil plane are in progress and we proceed with the full scale preproduction prototype.
Technical and operational risks are being addressed and in most cases mitigated.

## Slide 52: Supplemental slides

## Slide 53: Extraction channel
ESS1
ESS2
Q203
Q204
Q205
LAM
C-Mag
Extraction line
Delivery Ring
Extraction channel

## Slide 54: Extracting from multiple separatices

## Slide 55: Approaching resonance with SC

## Slide 56: Special Topics
Special Topics
Instrumentation
Technical risks
Radiation protection
Machine protection

## Slide 57: Instrumentation: BPMs
Debuncher BPMs can only see 53MHz and will be upgraded to Echotech standard with 2.5MHz electronics.
  Repurpose Tevatron BPM crates
  Repurpose Recycler BPM electronics
Tunnel hardware will be repurposed.
BPMs will have sub-millimeter resolution.
  Closed orbit and TBT available.
Delivery Ring BPM system is off-project on the Delivery Ring AIP.
Courtesy B.Drendel

## Slide 58: Instrumentation: DCCT
Delivery Ring DCCT hardware repurposed.
Analog conditioning and VME electronics modified for Mu2e operation.
The system has an accuracy of one part in 105 over the range of 1 x 1010 to 2 x 1012 particles with a noise floor of 2 x 109.
The Accumulator unit will become a working spare.
Courtesy B.Drendel

## Slide 59: Instrumentation: Schottky
Repurpose Tevatron 21.4MHz Schottky which has an acceptable aperture.
Down convert from 36th/37th harmonics to 1st harmonic (0 to 590 KHz)
Use 24-bit ADC to sample signal
  2 to 4 MHz sampling
  100 db dynamic range
Use digital signal processing to produce tunes
  Tunes to ±0.001 at 590 Hz
  Tunes to ± 0.0001 with averaging over many spills
Courtesy B.Drendel

## Slide 60: Instrumentation: BLMs
The M4 Line Beam Loss Monitor (BLM) system has been designed to measure a 0.2% localized loss with microsecond integration.
This will allow seeing losses develop inside of an individual slow spill.
30 BLMs will be placed at key locations along the 245m beam line.
This system design is identical to the existing Main Injector, P1, P2, M1 and M3 line BLM systems.
There is not a sufficient pool of spare hardware and electronics so new parts will need to be purchased and constructed to build the system.
Courtesy B.Drendel

## Slide 61: Technical risks
Technical Risks (extraction specific)
  High losses
    Large effective thickness of ESS planes
    Insufficient kick in the ESS
    Inadequate ESS alignment
    Inadequate orbit control
  High spill variations
    Regulation is not fast enough
    Regulation is not deep enough
    Insufficient RFKO power
  Insufficient aperture
  Magnet strengths are not sufficient
  Magnet ramping capabilities are insufficient
  Insufficient machine diagnostics
  Substantial fraction of the beam not extracted
  Beam instabilities

## Slide 62: Radiation protection
Extraction channel- Elevation view
Beam
In-tunnel shielding
Beam enclosure has been designed for 13W 8GeV operations
Mu2e: 8kW 8GeV beam
In-tunnel shielding above extraction channel
Concrete shielding in the isle
Additional shielding if needed

## Slide 63: Radiation protection
Shield wall
Protection of people downstream (not in RE scope)
M4 line enclosure protected by shielding wall during installation
Mu2e PS hall protected by shielding wall during commissioning and g-2 operation
G-2 protected by shielding wall during Mu2e operation

## Slide 64: Machine protection
Accident case scenarios
DR abort system is not capable to abort beam during the spill, we can only abort in the end of the spill and inhibit next one.
Worst case scenario: loss or extraction of the whole spill intensity in a single pulse
Beam permit system can inhibit the next spill:
  On BLM trip
  On Spill Monitor threshold
  On Detector diagnostics
  On regulation system abort signal
Single bunch is not destructive for:
  Septum foils
  Production target
  Detector systems

## Slide 65
Beam loss – local and global budget

## Slide 66: Beam loss – local and global budget
Phase space of circulating beam
Phase space of extracted beam
Total losses in the ring
Total losses in DS Beam line
Losses downstream
Local losses defined as missing beam DS of C-mag
DS losses calculated as beam scattered outside of the 20 p-mm-mrad area
Total losses = Local + DS losses (nearly twice local)
“Anything scattered is lost” ?
Tolerance on effective thickness of the foil plane <50u

## Slide 67: Beam loss – local and global budget
Localized losses in the ring
Synergia tracking:
87% lost in first turn
99.7% lost in first 3 turns
40% lost before the first arc
16% in the first arc
33% in the known narrow elements
Tracking assumes idealized apertures, this breakdown just gives a general idea.

## Slide 68: Beam losses and related extinction issues
Scattered beam tracking
Scattered beam integration
All scattered particles are expected to be lost very quickly, so they should not contribute to out of time beam contamination.