## Slide 1: Design Concepts of the Mu2e Electrostatic Septa - Large Scale Prototype
David Tinsley
Mu2e Resonant Extraction Technical Review
August 25, 2015

## Slide 2: Extraction Channel Layout (Plan View)
Beam direction is left to right
Electrostatic Septum: ESS1, ESS2 – Total horizontal kick 2 mR, Inward
LAM, C-MAG – vertical kick 110 mR, Up
Have septa as close as possible to the quad (Q203)
Need quick access because of radiological concerns (DS flange if made of SS can reach 700mR/hr on contact after 100 days irradiation and 7 days cooling)
Beam direction
Extracted beam
Circulating beam

## Slide 3: Views of Septa in the Beamline
Q203
ESS2
ESS1
Elevation view
Plan Section View
Beam Direction
Upstream
Downstream
Vacuum bellows before
and after both septa.
Q203
ESS1
ESS2

## Slide 4: Shielding around Septa
D-30 Straight Layout
ESS1
Q203
ESS2
Q202
Q204
Steel Shielding
Above Septa
And Quads
Beam Direction
Upstream
Downstream

## Slide 5: Main Electrostatic Septa Specifications
Number of septum modules | 2
ESS1 cathode length | 1.18 m
ESS2 cathode length | 1.79 m
Total kick | 2 mrad
Cathode material | Ti (or SS304)
Septum plane | W/Re (or Mo) foils
Foil thickness | 25 m
Foil spacing (center-center) | 2.54 mm
Foil width | 1.0 mm
Total number of extraction foils (total) | 1196
Diffuser length (ESS1 only) | 0.509 m
*The full specification document is provided in the review page

## Slide 6: Main Deviations from the Existing Design
 | MI Slow Extraction | Mu2e Slow Extraction
Proton Beam (GeV) | 120 | 8
Avg. Beam Power (kW) | 2.6 | 8
Septum Anode Plane | 50m 75%W/25%Re Wire | 25m W/Re Foil
Operating HV (kV) | 100 | >100
Frame Length (inches) | 144 | 72
Cathode Gap (mm) | 14 | 10 to 25 (12 nominal)
Cathode Material | 304 SS | Titanium

## Slide 7: The full scale prototype of the septum
Test design solutions in real scale
Started with the small scale prototypes for dedicated studies
Working towards the full scale prototype
Satisfy ESS specifications document

## Slide 8: Cross Section of the Electrostatic Extraction Septum
Baffle
HV Feed-thru
cable
Clearing
Electrode
Clearing Electrode
Feed-thru
Frame
Cathode
Termination
Resistor
HV Feed-thru
Port
Ceramic
Insulator

## Slide 9: Overview of Design Details Index Page Numbers
Frame – 10 & 11
Foils - 11
Clearing Electrode – 11, 12, 25 & 26
Diffuser - 13
Baffles - 14
Cathode – 19, 20 & 23
Cathode Standoff – 20, 21, 26 & 27
Vacuum Vessel - 22
Feed-thru – 26 & 28
Vacuum - 29
Assembly Procedures – 30
Quick Disconnect Flanges - 31

## Slide 10: Frame Final Machining
The frame is machined from 7075-T6 aluminum.
The top of both the frame rails that contact the foils
will be finished with a 25m dip on that surface
so the foil will be flat down the length of the frame
after the foils are installed.
The frame is symmetrical both top to bottom
and end to end.
Frame
Rails
The frame can be installed with either end
inserted first depending on the straightness.

## Slide 11: Frame Assembly Procedure
After the correct shape to the frame rails have been achieved
the frame is cleaned and the assembly can begin.
The clearing electrodes are installed.
The spring pins are installed.
The retraction springs and foils are then pulled
evenly and hooked onto the spring pins.
Clearing Electrodes
Spring Pins
Retraction
Spring
Foil
Frame
ESS1 will have 478 extraction foils and
21 diffuser foils installed.
ESS2 will have 718 extraction foils installed.
Frame straightness will be checked again.
Only one foil assembly is shown for clarity.

## Slide 12: Clearing electrodes helps pull ions out of the recirculating beam area which reduces the sparks on the cathode.
Frame
Extracted
Beam
Area
Cathode
Foil
Recirculating
Beam Area
Clearing
Electrodes

## Slide 13: Diffuser
On ESS1 the first .509m of the frame have foils mounted on 25.4mm centers.
These 21 Molybdenum foils act as a diffuser.
The diffuser helps reduce scattering on the septa.
Uses the same springs and foils as the rest of the frame.
Assembles just like the other foils.
The cathode does not cover over the diffuser foils.
ESS1 has less foils mounted on it than ESS2.
The basic aluminum frame for ESS1 and ESS2 are the same.

## Slide 14: Baffles
The baffles are then installed over the spring assemblies.
Baffles
4 per side
Total of 8
The baffles helps prevent a broken
foil from touching the cathode.
The baffles also retain the retraction
spring on to spring pins.

## Slide 15: Frame Support Rings Installed on to Finished Frame
Only one foil assembly is shown for clarity.
The support rings are installed.
Downstream
Support Ring
Upstream
Support Ring

## Slide 16: Frame assembly with support rings
Small support ring with wheels
Large support ring
Frame assembly
(retraction springs
clearing electrodes
baffles, foils, etc.)
Downstream
End
Upstream
End
Only one foil shown for clarity
Assembly Procedure:
The cathode is placed in the vessel.
Then small support ring end is inserted
into the vacuum vessel till the frame is
completely inserted. The pin at the
top of the large ring clocks the frame
into the correct position. Any thermal
expansion is on the downstream end.
Pin

## Slide 17: Foil assembly with retraction spring
Spring Pin
Retraction
Spring
Frame
Ferrule
Cathode
Foil
Baffle
Clearing
Electrode

## Slide 18: Spec: Foil Plane Effective Thickness & Flatness
All of the following items combine together to make an effective thickness of the foil plane of 50m or better:
  Frame straightness and twist between the rails.
  Foil straightness, twist and cupping.
  The electrostatic force pulling on the foils.

## Slide 19: ESS2 Cathode with re-entrant skirts
The face of the cathode is flat within .25mm.
The measurement is checked by supporting
the cathode at the re-entrant skirts.
Cathode
Re-entrant skirts
Note: ESS1 cathode is shorter with 2 re-entrant skirts

## Slide 20: Cathode with re-entrant skirts and high voltage standoffs
The standoff is adjusted perpendicular
to the cathode by shimming under the
re-entrant skirt if necessary before
assembly into the vacuum vessel.
Standoff
Shim if necessary
Cathode

## Slide 21: Ceramic Standoff Assembly
Leveling
Adjustment
Screws
Gap
Adjustment
Screws
Adapter
Ring
Ceramic Rod
Threaded Cap
The leveling adjustment screws is
used to set the 12mm gap first.
If gap need to be changed, the 4
fasteners in the center can adjust
the gap from 10mm to 25mm.

## Slide 22: Vacuum vessel
Vacuum vessel is made from 6061-T6 Aluminum.
The vacuum flanges sealing surfaces are bonded
with 304 stainless steel to insure good sealing.
Downstream
End
Upstream End
2 Ion Pump Ports
on the Bottom
HV Port
3 Standoff Ports
on the side
Pads for
lifting

## Slide 23: Cathode Installation
Vacuum
Vessel
Cathode
Standoffs
The cathode is placed inside the vacuum vessel then the
standoffs are screwed into the cathode re-entrant skirts
Re-entrant
Skirts

## Slide 24: Spec: Horizontal and vertical position adjustments
The motorized stand will have +/- ½ inch horizontal motion.
The motorized stand will have manual vertical adjustment.
LVDT’s will be used to electronically control the motion.
Because of the precision of the alignment of the septa, the motorized stand will not have to be moved during the quick replacement of the spare septa.
The motorized stands are attached to the very far ends of the vacuum vessel so it pivots at the ends of the frame.

## Slide 25: Section View of Clearing Electrode and Supports
Baffle
Cathode
Frame
Clearing
Electrode
Clearing
Electrode
Support Pin
Ceramic
Insulators
Retaining
Rings

## Slide 26: Section View of High Voltage Standoff Support and Clearing Electrode Feedthru
10kV
SHV
Clearing
Electrode
Connection
Standoff
Support

## Slide 27: Isometric Section View of Standoff

## Slide 28: High Voltage Feedthru
Baseline design is like the electrostatic separator feedthru that uses Fluorinert as a dielectric insulator.
Feedthru design is based on the electrostatic separator.
Fluorinert
Inlet
Fluorinert
Outlet
Feedthru Section View
Feedthru Isometric View

## Slide 29: Spec: Vacuum
Ultra-high vacuum cleaning and handling techniques will be used.
Low E-8 or high E-9 Torr vacuum levels are expected since historically septa of twice this length have achieved this vacuum level with the same differential pumping.
Two 300 l/s ion pumps will be used per septa.
In situ Bake-out’s will not be used to improve vacuum.
Vacuum valves will be located nearby the septa to isolate the area for any operational issues.

## Slide 30: Assembly procedures and alignment
The frame position is not adjustable inside the vacuum vessel.
The cathode is adjusted so it is parallel to the foil plane.
The vacuum vessel mounting hole locations are adjustable. These holes are adjusted so the distance between the foil plane and the motorized stand mount are identical for all the septa. This ensures interchangeability between the septa with no re-survey needed.
How we can do measurements:
  Optical
  CMM (coordinate measuring machine)
  Autocollimator
  Surface plate
  Laser Tracker

## Slide 31: Quick Disconnect Flanges
Quick disconnect flanges are being strongly considered because of radiological concerns.
EVAC ISO Quick Disconnect:
  Takes 1/3 of the time to assemble vs. conflats
  Lighter weight and less parts compared to conflats
  Few technicians have experience with these flanges
  Any scratches on the edge will dictate using a new seal

## Slide 32: Conclusions
Previous design parameters and experience have guided the new design
Questions?