## Slide 1
Collar Pack #2 Disassembly Incident
Summary
Helene Felice
Heng Pan, Dan Cheng, Xiaorong Wang, Soren Prestemon, Maxim Martchevsky,
Ahmet Pekedis, Matt Reynolds, Daryl Horler, Jason Duponte, Tom Lipton, Jordan Taylor

## Slide 2
On 07/07/2015
  During the collar pack #2 disassembly an incident happened:
    The upper coils shifted and collapsed
Preliminary assessment immediately after incident
  No one was injured
  No assembly tooling were damaged
  All collar stacks are intact.

## Slide 3: Context of the incident
Normal setup
During the incident
  The center coil support spud was not in place;
  The technicians were removing the side collar pack, the steel angle block was released
Steel Angle block
Coil support spud
Assembly Table
Assembly Table
Return End
Return End
1- Disassemble the top collar stack
2 -Disassemble the collar stack #2

## Slide 4
Incident sequence
Return end view
Coil 104 fell onto the assembly table,
Coil 3 fell into coil 5
Red circles indicate the edge of the coil impacting other coil or assembly table.
03
104
103
05
03
104
103
05
03
104
103
05
Return end view
Ready to disassemble
Collars removed
Coils fell off
03
104
103
05
103
104
104

## Slide 5: Preliminary Assessment summary details in Heng’s talk
03
05
103
104
Coil 103
No visual damage
All electrical tests ok
Coil 3
Some local scratches (red circle area)
All electrical tests ok
Coil 104
OL splice: epoxy delamination
Damaged wiring of the SG bridges (temp comp), SG are intact
Indents on the coil OD
Bump on the mid-plane
All electrical tests ok
Coil 5
Sectioned wiring from bridges to connector
Kapton GPI damage observed with epoxy damage underneath where coil 104 SG impacted coil 5
All electrical tests ok

## Slide 6: Corrective action already implemented
Modification of the spud
To capture the 4 coils
Modification of the procedure to account for missing disassembly steps
Cause analysis process started at LBNL
Will possibly lead to additional corrective actions
See Patricia Thomas’slides