## Slide 1: Development of Optical Metrology Data Analysis Engine
Ben Sheff

## Slide 2: X-ray Optics
As beamlines get better, need better mirrors
  Residual slope error below 50 nrad
Long trace profiler (LTP) is a high precision metrology tool
  Measures slope of mirror at each point to within 50 nrad
  Extremely accurate for small range of angles, but has problems farther out
  New analysis tools needed to handle this

## Slide 3: Analysis Software
Developed Optical Metrology ENgine (OMEN) in Python
Handles standard analysis
  Easy, dynamic filtering
  Fitting options, with live-updated residue plot
  Region-of-interest selection
Tools to deal with high angles
  Stitching together overlapped, adjacent scans of mirror segments
  Soon will include option to add calibration run

## Slide 4: Goals
Complete a calibration curve for the LTP
  Make working calibration look-up table
  Analyze systematic errors
  Integrate into OMEN
Improve stitching code
  Standard deviation of difference between stitched and unstitched is about equal to standard deviation of either