## Slide 1: Optimization of the DPSS Nd:YLF Amplifier Chain for the 263 nm Drive Laser at the FAST Facility
Julie M. Gillis
Department of Physics
Department of Chemistry and Biochemistry
Duquesne University
Supervisors: James K. Santucci and Jinhao Ruan
FNAL Accelerator Division
Summer Internships in Science and Technology (SIST) Program
Fermi National Accelerator Laboratory
August 4, 2015

## Slide 2: Outline
Research at FAST
Making an Electron Beam
Drive Laser System
Improving the Amplifier Chain
Downstream Effects
Final Remarks

## Slide 3: Research at FAST

## Slide 4: The FAST Facility
Fermilab Accelerator Science and Technology
Testbed for advanced accelerator research and development (AARD)
FAST Facility

## Slide 5: 50 MeV Electron Linac
Superconducting radiofrequency (SRF) linear accelerator coupled to a photoinjector
  2 capture cavities
Dipoles, quadrupoles, transverse profile monitors

## Slide 6: SRF Technology
Nine-cell niobium accelerating cavities with a resonant frequency of 1.3 GHz
TTF/ILC-type cryomodule for 300 MeV electron beam

## Slide 7: IOTA Ring
Integrable Optics Test Accelerator
39 meter circumference
Nonlinear lattice for addressing intensity limitations

## Slide 8: Making an Electron Beam

## Slide 9: Photoelectric Effect
Wave-particle duality of light
Metallic surface bombarded with photons release electrons

## Slide 10: RF Electron Gun
1-1/2 cell PITZ at DESY Zeuthen design
Cs2Te photocathode
  p-type semiconductor
  Band gap = 3.2 eV
High quantum efficiency
  10%-1%
How do we get there?
Incident light must be UV

## Slide 11: Drive Laser System

## Slide 12: Phase-Locked Drive Laser
YLF seed laser
  3 picosecond, 1053 nm (IR) pulses
Amplifier chain (3 pre-amps, 3 single-pass amps, 1 commercial amp)
Fourth harmonic wavelength generation
  Frequency-doubling crystals (1053 nm  526.5 nm  263.25 nm)
Transported to electron gun

## Slide 13: DPSS Amplifiers
Diode-pumped solid state amplifiers
  End-pumped by 808 nm diodes
  Gain medium = Nd:YLF crystal

## Slide 14: Improving the Amplifier Chain

## Slide 15: Preliminary Measurements – SPA3
SPA3 Gain: 3.23
  6.97 μJ per pulse

## Slide 16: Preliminary Measurements – SPAT
50 seed pulses per bunch
Pick-off of seed after SPA1 to Sandbox Table

## Slide 17: Beam Spot Analysis
CCD camera for imaging beam profiles
  1 pixel = 3.45 μm
Gaussian profiles
Measured at crystal distance
SPA3
SPAT
X sigma: 41.9 pixels
144.6 μm
X sigma: 33.4 pixels
115.2 μm
Y sigma: 42.0 pixels
145.9 μm
Y sigma: 32.0 pixels
110.4 μm

## Slide 18: Timing Adjustments
Flat pulse trains for more pulses
Adjust timing of pump diode trigger delays and pulse widths
Delay: 1.097 ms
Width: 1.856 ms
Delay: 1.718 ms
Width: 1.280 ms

## Slide 19: Maximizing SPAT
On sandbox table with 50 seed pulses per train
Photodiode measurements:
Energy meter measurements:
  0 A  10.2 μJ
  90 A  107.9 μJ
Gain: 10.58
Gain: 8.60

## Slide 20: Replacing SPA3
Align through all existing downstream optics
  Northrop Grumman Amplifier (NGA)
  Frequency-doubling crystals and diagnostics
New diode calibration
Maintain flat pulse trains

## Slide 21: Results Comparison
Gain = 4.83
4.83
3.23
Are these improvements actually significant?

## Slide 22: Downstream Effects

## Slide 23: Effects on NGA
500 seed pulses
  2.85 mJ to 32.4 mJ
    64.8 μJ per pulse
Gain: 8.5  11.37

## Slide 24: Effects on UV Pulse Energy
BBO crystals only have ~50% efficiency for transmitting converted light
4.8 μJ per pulse  10.2 μJ per pulse
  15.7% total efficiency

## Slide 25: Final Remarks

## Slide 26: Future Work
Tune up the rest of the amplifier chain
  Replace SPA2 (gain = 1.4) with an improved SPA3
Increase UV pulse energy
  Goal: ~50 μJ per pulse

## Slide 27: Many thanks
Jamie Santucci, Jinhao Ruan, and Chip Edstrom
Laser and Injectors Groups at FAST
FAST/IOTA Group
SIST Committee
Fellow interns of Summer 2015
Fermi National Accelerator Laboratory
Operated by Fermi Research Alliance, LLC under Contract No. De-AC02-07CH11359 with the United States Department of Energy.

## Slide 28: References
K. Carlson, et al., Fermi National Accelerator Laboratory. Design of the Advanced Superconducting Test Accelerator. Beams-doc-4212, 2012.
P.H. Garbincius, et al. Fermi National Accelerator Laboratory. Proposal for an Accelerator R&D User Facility at Fermilab’s Advanced Superconducting Test Accelerator. Fermilab-TM-2568, 2013
J. Ruan. ASTA Injector Laser Lab Standard Operating Procedure, 2015

## Slide 29: Questions?