## Slide 1: MQXFS1 Observations and Feedback from the Assembly Processes
Dan Cheng
8/20/2015

## Slide 2: Outline
Observations and feedback on assembly processes
Summary and Status

## Slide 3: Improved Coil Support Spud
Procedures and tooling were adjusted after the disassembly incident
Redesigned coil support spud was incorporated into the use of coil pack builds #3-5
  Screws positively engage with each coil to prevent relative motion

## Slide 4: MQXFS1 Coil Pack Insertion Rails
Coil pack was inserted into the shell & yoke assembly with the insertion rails

## Slide 5: MQXFS1 Coil Pack Insertion Rails
Rails were removed when the bladders were first cycled

## Slide 6: MQXFS1 Master Keys & Shims
MQXFSD Alignment and load keys required many shims in nominal dimensions
MQXFS1 keys were increased in thickness
  1 mm per each load key half, and 2 mm in alignment key
  This reduced the amount of shim required during bladder operations
Material was changed to bronze instead of mild steel

## Slide 7: MQXFS1 Wire Routing
IL wiring is being routed under the axial end plates via SLA (Accura Bluestone) wire guides

## Slide 8: Threaded holes in Collars
There are still some chips that are being generated by the screwing/unscrewing process of the aluminum collarpacks
  Chips were vacuumed after bolting operations
Long magnet designs plan for Load Pad and Collar stacks to be preassembled, and only load pads would be bolted
  CERN has already tested this option in the short model with promising results

## Slide 9: Summary
Magnet assembly incorporated improvements
  Redesigned coil support spud was used
  Coil pack insertion rails were used successfully
  Increased key thicknesses to reduce required shimming
  Wire guides to protect and route instrumentation wires
Status
  Axial loading should be completed this week
  Electrical QA to follow
  Pizza box fabrication has experienced some delays
  Connector mounts & wiring and magnet support are in fabrication

## Slide 10
Additional Slides