## Slide 1: Sensitivity of Extinction to Optics
An exact analysis will require introducing errors and re-running the simulations, the most important optical features related to optics are:
  Waist in center of vertical non bend plane
    Minimum size at ends
      bcenter = L/2=3m
      bend = L = 6m
    If the beta function is too large, out of time beam in the non-bend plane can scatter in the bend plane, and be driven back into the transmission channel.
      Simulations show 2 need 1.5 cm of clearance, but magnet has a gap of 1.8
      b function at ends can grow by (1.8/1.5)2 = 1.44
  Phase advance between the AC dipole and the collimator will require more current to move the beam clear of the collimator.
    ±25°  10% increase in current