## Slide 1: Delivery Ring Extraction for Mu2e – Optics Design
Steve Werkema
Mu2e Beamline, Controls and Instrumentation Technical Design Review
6 October 2015

## Slide 2: Outline
Delivery Ring Extraction Requirements
Overview – Extraction Equipment layout
Extraction optics and trajectory
Calculation of M4 beamline starting parameters

## Slide 3: Delivery Ring Extraction Section Requirements
Transport resonantly extracted 8.9 GeV/c proton beam from the Delivery Ring electro-static septum extraction channel to the upstream end of the C-magnet downstream of quadrupole D2Q5
Maintain – to the extent possible – the Delivery Ring extraction layout used for extraction of 3.1 GeV/c muons to the g-2 experiment*
Efficiently extract beam to minimize losses such that prompt and residual radiation dose rates are as low as possible –
  MARS tracking models show ~98% efficiency
  Gives acceptable radiation dose rates
* A significant exception to this is noted in a later slide
Notes: Note: #2 is violated by the need to replace the downstream g-2 extraction kicker with the upstream Mu2e electro-static septum module

## Slide 4
Overview of Delivery Ring Extraction
Equipment layout
Resonant extraction overview (not in scope of this review)

## Slide 5: Muon Campus Layout
Proton injection and extraction is located in the D30 straight section
Brian Drendel

## Slide 6: Delivery Ring D30 Straight Section
M4/M5 Beamline
M3 Beamline
D30 Straight Section
Delivery Ring
g-2 Extraction kickers
Shielded Extraction Section

## Slide 7: Delivery Ring Extraction Equipment Layout for Mu2e
Key
ESS1 Electro-static Septum Module 1 (Kick: 0.8 mrad, Horizontal inward)
ESS2 Electro-static Septum Module 2 (Kick: 1.2 mrad, Horizontal inward)
ELAM Extraction Lambertson Magnet (Kick: 40.0 mrad, Vertical upward)
ECMAG Extraction C- Magnet
DsQn nth Delivery Ring Quadrupole in sector s (n = 0 at center of straight)
Starting point of Delivery Ring extraction model is upstream end of ESS1
Starting point of M4 beamline model is the upstream end of ECMAG
Proton Beam
Notes: Notes:
Beam pipe vacuum chamber sections not shown here
D2Q5 is a 8Q24 (24” quad) from BNL. Chosen because of the need for a narrow, wide aperture quad in this location.

## Slide 8: Extraction Section – Plan View
ESS1
ESS2
Q203
Q204
Q205
ELAM
ECMAG
Extraction line
Delivery Ring
Extraction Section

## Slide 9: Compatibility of Mu2e & g-2 Extraction
g-2 kickers
Mu2e ESS
Proton Beam
The downstream g-2 extraction kicker modules must be removed prior to installation of ESS1.
Implications:
Single turn proton extraction at 8 GeV not possible with only one kicker
g-2 3.1 GeV/c operation still possible with one kicker with slightly reduced efficiency
 Must have M4 line commissioned up to diagnostic absorber before installing ESS1
D2Q3
D2Q4
D2Q2
D2Q1

## Slide 10: Implementation of Resonant Extraction in the Delivery Ring
SS 10-60
SS 40-50
SS 20-30
RFKO kicker
Vladimir Nagaslaev
New injection point
Extraction in SS 20-30
Electro-static septa
2 families of harmonic Sextupoles
A family of tune Quadrupoles
Extraction Lambertson
Dynamic orbit control
Abort line
RFKO system
Spill monitoring
Spill regulation
Horizontal 3rd Integer resonance
Qx / Qy=9.650 / 9.735
Notes: SS = Straight Section
RFKO = Radio Frequency Knock Out – horizontal kicker used to heat the beam to control the rate at which beam enters the stop band about the separatrix

## Slide 11: Resonant Extraction Horizontal Phase Space
Horizontal phase space distribution of circulating beam at the upstream end of ESS1
Blue – beginning of spill
Red – early in spill
Yellow – late in spill
Cyan – end of spill
ESS1 Foil Plane
Synergia model
Chong Shik Park
Tune quad ramp drives horizontal tune closer to 3rd order resonance as spill progresses – shrinking area inside separatrix to zero at the end of the spill
Note: x’ at the foil plane changes throughout spill – compensated by DEX bump
Notes: From Synergia tracking model of Mu2e resonant extraction

## Slide 12: Circulating and Extracted Beam at Upstream End of ESS1
Cathode
Foil Plane
Clearing Electrode
40 mm
E
-100 kV
Notes: The electro-static septum is being designed and built under a separate level 3 sub-project (475.05)
Notes:
Proton beam goes into the page
Distribution shown is not expected beam distribution.
  These particles were generated for loss simulations (emphasis on high amplitude particles)
  Relative intensities of extracted and circulated beam have been altered to make the extracted beam visible

## Slide 13: Extraction Lambertson – Upstream End (8.6 m downstream of ESS1)
Extraction Channel
Circulating Beam Channel
54 mm
12.5 mm
Notes: The extraction lambertson is being designed and built on the g-2 project
Notes:
Proton beam goes into the page
Distribution shown is not expected beam distribution.
  These particles were generated for loss simulations (emphasis on high amplitude particles)
  Relative intensities of extracted and circulated beam have been altered to make the extracted beam visible

## Slide 14
Delivery Ring Extraction Model

## Slide 15: Delivery Ring Extraction Models
Several models of Delivery Ring extraction for Mu2e have been constructed
Optics Models
  Original Concept: hand calculation of trajectories (Jim Morgan)
  Original Model in MAD 8 (Carol Johnstone)
  Present Model in MAD X (Steve Werkema)  Focus of next few slides
  Model independently checked in OptiM (Vladimir Nagaslaev)
Resonant extraction studies
  MARS model (Vladimir Nagaslaev)
  Optimize resonant extraction parameters to minimize losses
  Provide beam distributions for tracking models of M4 beamline for extinction and targeting studies
Radiation dose rate/shielding studies
  MARS model that includes shielding (Tony Leveling)
  sky shine, direct dose rate, and residual activation studies
Notes: Note: the trajectories of the present optics model come very close to the original calculations of Jim Morgan

## Slide 16: Delivery Ring Extraction Optics Model
Two pass process:
First Run:
  Model ESS1, ESS2, and ELAM as correction dipoles (doesn’t change survey trajectory)
  Starting survey coordinates = coordinates of circulating beam at upstream end of ESS1
  Starting x and x’ = center of extracted beam at the upstream end of ESS1
  Final coordinates at the upstream end of ECMAG are calculated from the survey coordinates of the circulating beam, and the bearing, pitch, x, x’, y, and y’ of the extracted beam
  Final Dispersion (D and D’) at upstream end of ECMAG is calculated from change in in x and y for a 1% change in Dp/p
Second Run:
  Model ESS1, ESS2, and ELAM as RBENDs
  Starting survey coordinates = coordinates of extracted beam at upstream end of ESS1
  Model kicks from off-center passage through quads by embedding short (10 mm) RBENDs in quads with kicks determined from quad Dx’ and Dy’ from first run.
  bx, ax, by, and ay at upstream end of ECMAG determined by this run

## Slide 17: Extracted Beam Lattice Functions
Chart: Mu2e Extracted Beam: Lattice Functions
| 0 | 0 | 0 | 1.18 | 1.233563 | 1.233563 | 1.233563 | 1.6335630000000001 | 1.6335630000000001 | 1.6335630000000001 | 1.9669380000000001 | 1.9669380000000001 | 2.3003130000000001 | 2.3003130000000001 | 2.3003130000000001 | 2.4527130000000001 | 2.7503129999999998 | 2.7503129999999998 | 2.7503129999999998 | 2.8038759999999998 | 4.5938759999999998 | 4.6474390000000003 | 4.6474390000000003 | 4.6474390000000003 | 6.0602299999999998 | 6.0602299999999998 | 6.0602299999999998 | 6.393605 | 6.393605 | 6.7269800000000002 | 6.7269800000000002 | 6.7269800000000002 | 6.8793800000000003 | 8.6211979999999997 | 8.6211979999999997 | 10.121198 | 10.121198 | 10.521198 | 10.521198 | 10.521198 | 10.825998 | 10.825998 | 11.130798 | 11.130798 | 11.130798 | 11.283198000000001 | 11.730798 | 11.730798 | 11.730798
BETX | 8.756 | 8.756 | 8.756 | 12.1025 | 12.2736 | 12.2736 | 12.2736 | 13.6048 | 13.6048 | 13.6048 | 14.191 | 14.191 | 13.6198 | 13.6198 | 13.6198 | 13.108 | 12.1468 | 12.1468 | 12.1468 | 11.9792 | 7.321 | 7.2099 | 7.2099 | 7.2099 | 4.87 | 4.87 | 4.87 | 4.6787 | 4.6787 | 4.9308 | 4.9308 | 4.9308 | 5.1581 | 8.7746 | 8.7746 | 13.3898 | 13.3898 | 14.8551 | 14.8551 | 14.8551 | 15.4576 | 15.4576 | 14.9247 | 14.9247 | 14.9247 | 14.3872 | 12.8838 | 12.8838 | 12.8838
BETY | 8.15 | 8.15 | 8.15 | 6.0813 | 6.0041 | 6.0041 | 6.0041 | 5.4726 | 5.4726 | 5.4726 | 5.3126 | 5.3126 | 5.6473 | 5.6473 | 5.6473 | 5.9261 | 6.5129 | 6.5129 | 6.5129 | 6.6245 | 11.4017 | 11.576 | 11.576 | 11.576 | 16.831 | 16.831 | 16.831 | 17.5258 | 17.5258 | 16.7935 | 16.7935 | 16.7935 | 16.1497 | 9.8863 | 9.8863 | 6.1046 | 6.1046 | 5.3481 | 5.3481 | 5.3481 | 5.0333 | 5.0333 | 5.1399 | 5.1399 | 5.1399 | 5.3044 | 5.8539 | 5.8539 | 5.8539
DX | 0 | 0 | 0 | -0.003249 | -0.003418 | -0.003418 | -0.003418 | -0.004679 | -0.004679 | -0.004679 | -0.005234 | -0.005234 | -0.004776 | -0.004776 | -0.004776 | -0.004336 | -0.003476 | -0.003476 | -0.003476 | -0.003321 | 0.000765 | 0.000855 | 0.000855 | 0.000855 | 0.003224 | 0.003224 | 0.003224 | 0.003525 | 0.003525 | 0.003305 | 0.003305 | 0.003305 | 0.00308 | 0.00051 | 0.00051 | -0.001702 | -0.001702 | -0.002292 | -0.002292 | -0.002292 | -0.00212 | -0.00212 | -0.00071 | -0.00071 | -0.00071 | 0.000295 | 0.003247 | 0.003247 | 0.003247
DY | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -0.030167 | -0.030167 | -0.046256 | -0.046256 | -0.046256 | -0.060416 | -0.060416 | -0.079102 | -0.079102 | -0.079102 | -0.089779 | -0.12114 | -0.12114 | -0.12114
s = 0 Upstream end ESS1
s = 11.73 m Upstream end ECMAG
D2Q3
D2Q4
D2Q5
ELAM
ESS1
ESS2

## Slide 18: Extracted Beam Horizontal Trajectory: Mu2e and g-2
Chart: Compare g-2 and Mu2e: x
| -1.6335630000000001 | -1.6335630000000001 | -1.6335630000000001 | -0.45356300000000016 | -0.40000000000000013 | -0.40000000000000013 | -0.40000000000000013 | 0 | 0 | 0 | 0.33337499999999998 | 0.33337499999999998 | 0.66674999999999995 | 0.66674999999999995 | 0.66674999999999995 | 0.81915000000000004 | 1.1167499999999997 | 1.1167499999999997 | 1.1167499999999997 | 1.1703129999999997 | 2.9603129999999998 | 3.0138760000000002 | 3.0138760000000002 | 3.0138760000000002 | 4.4266670000000001 | 4.4266670000000001 | 4.4266670000000001 | 4.7600420000000003 | 4.7600420000000003 | 5.0934170000000005 | 5.0934170000000005 | 5.0934170000000005 | 5.2458170000000006 | 6.9876349999999992 | 6.9876349999999992 | 8.4876349999999992 | 8.4876349999999992 | 8.8876349999999995 | 8.8876349999999995 | 8.8876349999999995 | 9.1924349999999997 | 9.1924349999999997 | 9.4972349999999999 | 9.4972349999999999 | 9.4972349999999999 | 9.649635 | 10.097235 | 10.097235 | 10.097235
Mu2e Extracted Beam | 13.687 | 13.687 | 13.687 | 16.918 | 17.086 | 17.086 | 17.086 | 18.34 | 18.34 | 18.34 | 18.996 | 18.996 | 18.857 | 18.857 | 18.857 | 18.612 | 18.134 | 18.134 | 18.134 | 18.048 | 16.251 | 16.23 | 16.23 | 16.23 | 15.663 | 15.663 | 15.663 | 15.855 | 15.855 | 16.711 | 16.711 | 16.711 | 17.257 | 23.507 | 23.507 | 28.888 | 28.888 | 30.323 | 30.323 | 30.323 | 30.842 | 30.842 | 30.205 | 30.205 | 30.205 | 29.6 | 27.824 | 27.824 | 27.824
g-2 Extracted Beam | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.12 | 1.12 | 1.4 | 1.4 | 4.76 | 4.76 | 6.552 | 6.552 | 6.552 | 8.244 | 8.244 | 8.27 | 8.318 | 8.318 | 8.318 | 8.26 | 6.891 | 6.891 | 6.891 | 6.908 | 6.908 | 6.928 | 8.221 | 8.221 | 8.221 | 8.895 | 16.598 | 16.598 | 23.232 | 23.232 | 25.002 | 25.002 | 25.002 | 25.844 | 25.851 | 25.851 | 25.87 | 25.776 | 25.776 | 25.776 | 25.484 | 24.627 | 24.627 | 24.627
g-2 Circulating Beam | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -0.02 | -1.324 | -1.324 | -1.324 | -1.921 | -16.045 | -16.045 | -16.045 | -17.67 | -17.67 | -17.715 | -19.076 | -19.076 | -19.076 | -19.884 | -29.123 | -29.123 | -37.08 | -37.08 | -39.201 | -39.201 | -39.201 | -40.045 | -40.047 | -40.047 | -40.054 | -39.446 | -39.446 | -39.446 | -38.759 | -36.739 | -36.739 | -36.739
s = 0 Upstream end D2Q3
s = 10.10 m Upstream end ECMAG
Mu2e and g-2 extracted beam horizontally within ~3 mm
ELAM
Note: g-2 moves some D30 quads so that the circulating beam is horizontally off-axis by varying amounts. This cause the horizontal position of the circulating beam to differ from zero.

## Slide 19: Extracted Beam Vertical Trajectory: Mu2e and g-2
Chart: Compare g-2 and Mu2e: y
| -1.6335630000000001 | -1.6335630000000001 | -1.6335630000000001 | -0.45356300000000016 | -0.40000000000000013 | -0.40000000000000013 | -0.40000000000000013 | 0 | 0 | 0 | 0.33337499999999998 | 0.33337499999999998 | 0.66674999999999995 | 0.66674999999999995 | 0.66674999999999995 | 0.81915000000000004 | 1.1167499999999997 | 1.1167499999999997 | 1.1167499999999997 | 1.1703129999999997 | 2.9603129999999998 | 3.0138760000000002 | 3.0138760000000002 | 3.0138760000000002 | 4.4266670000000001 | 4.4266670000000001 | 4.4266670000000001 | 4.7600420000000003 | 4.7600420000000003 | 5.0934170000000005 | 5.0934170000000005 | 5.0934170000000005 | 5.2458170000000006 | 6.9876349999999992 | 6.9876349999999992 | 8.4876349999999992 | 8.4876349999999992 | 8.8876349999999995 | 8.8876349999999995 | 8.8876349999999995 | 9.1924349999999997 | 9.1924349999999997 | 9.4972349999999999 | 9.4972349999999999 | 9.4972349999999999 | 9.649635 | 10.097235 | 10.097235 | 10.097235
Mu2e y | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30 | 30 | 46 | 46 | 46 | 59.136 | 59.136 | 74.5 | 74.5 | 74.5 | 82.832 | 107.304 | 107.304 | 107.304
g-2 y | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30.002 | 30.002 | 46.002 | 46.002 | 46.002 | 58.704 | 58.936 | 58.936 | 59.633 | 74.492 | 74.492 | 74.492 | 82.825 | 107.299 | 107.299 | 107.299
s = 0 Upstream end D2Q3
s = 10.10 m Upstream end ECMAG
Vertical extraction is identical for Mu2e and g-2
ELAM

## Slide 20: Possible problem: D2Q5 Field Non-Uniformity
8Q24 Quadrupole: measured normal (bn) and skew (an) harmonic strengths.
Measurements show unusually strong 12- pole (n = 6) and 20-pole (n = 10) components.
2% deviation in gradient at 3” (where we intend to send beam)
There were some measurement problems – an 8Q24 is now on a MTF test stand undergoing a new round of measurements
Chart: Harmonic Number
| 1 | 2 | 3 | 4 | 5 | 6 | 9 | 10 | 12 | 15 | 18 | 20 | 21 | 25 | 27 | 28 | 30
Normal - 2350 A | 1.194e-05 | 1.0002 | 9.7987e-05 | 0.00019926 | 3.7632e-05 | 0.0031349 | 1.1762e-06 | 0.00028866 | 1.9846e-05 | 1.7042e-06 | 5.008e-06 | 6.7935e-07 | 2.6039e-07 | 6.1189e-07 | 1.8084e-07 | 2.6656e-07 | 1.1768e-07
skew - 2350 A | 9.4027e-06 | 0.00021822 | 8.3405e-05 | 0.00015887 | 1.3999e-05 | 5.2578e-05 | 1.2753e-05 | 1.5619e-05 | 3.9891e-06 | 6.5395e-07 | 2.5238e-06 | 2.2303e-07 | 7.4836e-07 | 3.9732e-07 | 8.4576e-08 | 1.4325e-07 | 4.8481e-08
Chart: 8Q24 Dgy(x) / g
Notes: D2Q5 will be replaced by a 8Q24 quadrupole from BNL. 8Q24s are beamline magnets – not known for their high field quality. This magnet is used because it has a large aperture and it is thin.

## Slide 21
M4 Beamline Starting Parameters

## Slide 22: Starting Position and Lattice for M4 line
Quantity | Value | Units | Description
X0 | 30071.579381 | m | Site North
Y0 | 222.112319 | m | Elevation
Z0 | 30446.932635 | m | Site East
q0 | 2.090508 | rad | Bearing
j0 | 0.054674 | rad | Pitch
bx | 12.316 | m | 
ax | 1.877 |  | 
Dx | 0.027 | m | 
Dx’ | 0.004 |  | 
by | 5.600 | m | 
ay | -0.616 |  | 
Dy | -0.119 | m | 
Dy’ | -0.069 |  | 
Starting Coordinates
Starting Lattice Functions

## Slide 23: M4 Starting Phase Space
Horizontal transverse phase space distribution is determined by DR extraction optics
ex = 11 p mm-mrad
Not matched to lattice
* There is a small vertical dispersion (-12 cm) from the vertical bend in ELAM.
Vertical transverse phase space distribution is relatively un-affected* by extraction. Thus, vertical phase space distribution is approximately that coming from the Recycler.
ey = 16 p mm-mrad
Matched to the lattice
Chart: Horizontal Phase Space: Upstream End of ECMAG
Chart: Vertical Phase Space: Upstream End of ECMAG
Notes: From Resonant Extraction MARS tracking model
Ellipses are 95% emittance ellipses.

## Slide 24: Conclusions
The design of the extraction optics for extraction from the Delivery Ring to Mu2e is very nearly complete
The design delivers extracted beam to the same position at the upstream end of ECMAG as g-2 extraction
  Mu2e extraction requires replacement of downstream g-2 extraction kickers with ESS1
Work remaining: incorporate the impact of the D2Q5 gradient non-uniformity into the model

## Slide 25
Backup Slides

## Slide 26: Surface Level Dose Rates at AP30 during Mu2e Beam Operation
Tony Leveling
MARS simulation of direct and sky shine dose rates during Mu2e operation at design beam power.
Assumptions:
Design Beam Power (8kW)
98% Extraction Efficiency
Peak dose rate: 24 mR/hr inside AP30 service building

## Slide 27: Calculation of Coordinates at Upstream End of ESS1

## Slide 28: Emulating kicks from beam offsets in quadrupoles

## Slide 29: MAD Global Coordinates
X 
Y 
Z 
MAD Coordinates:
Axis directions are those of the DUSAF (FSCS:XYZ) system except:
  X is site North (not East)
  Y is Up (not North)
  Z is site East (not Up)
Gives a system where Y is up (as in most accelerator coordinate systems) and X,Y,Z is right handed.

## Slide 30: MAD Global and Local Coordinates