## Slide 1: SRF Crab cavities and their ancillaries for HL-LHC
Peter Ratoff & Graeme Burt Lancaster University & The Cockcroft Institute

## Slide 2: HL-LHC Upgrade IR problem
HL-LHC upgrade during LS3
Complete overhaul of the interaction regions of ATLAS and CMS
Aimed luminosity increase factor of 10, realistically ~4
The HL-LHC upgrade will have a smaller β*
  This will increase the long range effect at the IR unless the crossing angle is increased

## Slide 3: Crab cavities
Increasing the crossing angle decreases the long range effect but decreases geometric overlap
Rotating the bunches with crab cavities before and after collision can reduce this effect

## Slide 4
Crab crossing
4 Rod Crab cavities
IR

## Slide 5
Crab Cavities at KEKB
Full crossing angle = 22 mrad
2 KEKB crab cavities were designed, constructed and installed in KEKB, and operated about 3 years under high current beam.
Peak luminosity Lpeak =21.1 x 1033 /cm2/s attained under crab on operation (peak luminosity world-record 2009).
KEKB operation terminated in June 2010 for the upgrade towards SuperKEKB.
HER
LER
K. Hosoyama @ CC10

## Slide 6
Why do we require compact cavities?
400 MHz elliptical
800 MHz elliptical
400 MHz compact
Using 800 MHz RF causes a S-shaped bunch which reduces luminosity hence a 400 MHz compact cavity is desired
There is limited space for the crab cavities due to the opposing beamline
The cavity must be within a 143 mm radius

## Slide 7
CC Down selection (CC’11)
~4yr of design evolution
Exciting development of new concepts
(BNL, CERN, CI-JLAB, FNAL, KEK, ODU/JLAB, SLAC)
R. Calaga, Chamonix ‘12

## Slide 8: Double l/4 TEM Cavity – BNL
Using two 1/4 wave cavities removes any monopole and quadrupole components from the dipole field.
However it then is only compact in one direction (LHC may need both planes).
Also has another monopole mode nearby.

## Slide 9
l/2 RF Dipole Crab Cavity

## Slide 10: Four rod crab cavity - Lancaster
To make suitable we increased the separation between the rods and made the rods wider.
Very compact in both planes and has a sparse HOM spectrum.
CEBAF separator cavity is:
  499 MHz,
  2-cell, 8 rods
  ~λ long
  0.3 m diameter,
  can produce 600kV deflecting voltage (on crest) with 1.5kW input RF power.
499 MHz CEBAF Separator

## Slide 11
Successful Cold Testings
4 Rod
RF Dipole
Double Quarter Wave
HiLumi-LHC/LARP Crab Cavity System External Review, May 5-6 2014

## Slide 12: DQW
RFD
Dressed cavities
SPS cavities under production by US LARP; Parallel production line launched at CERN – expected 1st bare cavity in one year from now
FPC production ongoing at CERN
HOM production ongoing at CERN
Helium vessel prototype under tests at CERN
Tuning prototype under tests at CERN
Cold magnetic shields under manufacturing by UK

## Slide 13: HOM Couplers
Three HOM in DQW, two for RFD
RF design done by USLARP & UK
Engineering common effort between UK, USLARP and CERN
Bulk Nb antenna, He-cooled
Coaxial lines evacuate 1 kW/HOM
DQW
RFD

## Slide 14: Helium tank prototype
Assembly, welding procedure and main loads under test with a prototype
Deformation of the tank is transferred to the cavity. Estimation (test) of ~1 mm deformation at interface if tank is fully welded.
Design approach: bolted tank with superficial welds for leak tightness
Notes: Dividere la slide in 2

## Slide 15: Tuning System
Crab prototype tuner actuator
First tests 0.5 µm precision

## Slide 16: Cryomodule
Double Quarter Wave
Notes: Design per SPS, lo stesso concetto da tenere per LHC. DQW: vertical kick

## Slide 17: HL-LHC Crab Cryomodule
Design of both cryomodule types well advanced; Review at CERN on 10-11 Nov.
Common effort between CERN, UK and US-LARP
Thermal screen with MLI
Warm magnetic screen
Bare cavity
Tuner
Cold magnetic screen
Cold-warm transitions
He supply
Vacuum tank
FPC
HOM
He vessel
Double Quarter Wave
Notes: Design per SPS, lo stesso concetto da tenere per LHC. DQW: vertical kick

## Slide 18: Magnetic Shielding
Maximum acceptable magnetic field on the cavity: 1 mT
The external screen, in mu-metal, is not enough to shield the cavities
One additional cold screen added per each cavity (Aperam Cryophy)
Magnetic field for external 200 mT
DQW
RFD
Cold magnetic shields design by UK

## Slide 19: Blade stiffners
Blade stiffners were added to the cavity to provide additional structural support and push the lowest microphonic frequency above 20 Hz.

## Slide 20: Thermal shield overview
Work performed by Manchester University undergraduate- Andy May
Ref: Thomas Jones SPICE thermal test design
Flexure mounts arranged such that they create a fixed point at the centre of the shield.
1050 Aluminium shield
Aluminium alloy tubing
Removable side panels (fitted during initial assembly
Thermal shield “Window frame”
Flexures optimised for maximum stiffness at 1W heat leak – 2mm thick x 40mm chosen

## Slide 21: Cryomodules
Double Quarter Wave, Vertical Deflection (ATLAS)
RF Dipole,
Horizontal Deflection (CMS)

## Slide 22: Hardware
RF Dipole
FPC
Tuner
LHe vessel
DQW
B shielding
HOM coupler