## Slide 1: WG3 closing summary
Rob Apsimon
(Tom Kroc, George Coutrakon)

## Slide 2: WG3 agenda
Session 1 (Wednesday 16:00 – 17:30):
ProBE: Proton Boosting Extension for Imaging and Therapy - Rob Apsimon
Proton CT in the US - George Coutrakon
Session 2 (Thursday 09:00 – 10:40):
UK overview of Proton Therapy - Karen Kirkby
US overview of Proton Therapy - Chris Beltran
Proton Therapy - Mark Pankuch
NorthStar Radioisotope Production - James Harvey
Session 3 (Thursday 11:00 – 12:30) – Joint session with WG4:
Laser-driven, high-brightness proton and neutron sources - Ceri Brunner
Solid State Proton Acceleration - Arun Persaud
NORMA FFAG - Sam Tygier
Session 4 (Thursday 13:30 – 15:30) – WG3 Roundtable discussion
Session 5 (Friday 09:00 – 10:40):
Ion Therapy - Tom Kroc
Applications of FETS - Stephen Gibson

## Slide 3: Conclusions from round table discussion
Proton therapy collaboration must have well-defined goals and deliverables
Priorities:
  Proton imaging
  Range verification / diagnostics
  Improved gantry design
  Novel accelerating schemes
Protons vs. ions
  Both are important and need to be developed
  Protons need to be the focus for technology development
Contributions from US + UK
  Funding
  Manpower
  Resources

## Slide 4: Proton imaging
Current proton imaging systems need to be improved
  Significantly slower than conventional CT scans
    ~10-20 minutes
  Detector technology seems to be the bottleneck
    Need 1 proton per bunch to avoid pile-up
    Need ~109 proton tracks to give ~1 mm3 spatial resolution
    Slow detector repetition rate
Detector development essential
  Collaborate with detector experts

## Slide 5: Range verification / diagnostics
Range verification
  Need to determine stopping power of tissue
    Need proton imaging
      Need better detectors!
Diagnostics
  Need to improve diagnostics for low-energy beams
    Improves transmission + energy efficiency
    Reduces patient treatment time

## Slide 6: Improve gantry design
Need to develop smaller, cheaper, lighter gantries
Investigate pros & cons of 360o vs. 180o gantries
Superconducting vs. normal conducting gantries
  Improve cryogenic technology
Establish joint-funded PhD + postdocs to study

## Slide 7: Novel accelerating schemes
Cyclotrons are currently favoured
  Mature technology
  Compact
  Cheap – “off-the-shelf” units
  Maybe not ideal for heavier ions…?
Laser / plasma / dielectric etc…
Should we consider hybrid schemes?
  E.g. cyclinacs (cyclotron – linacs)
Front-end vs. back-end machine size

## Slide 8: Focus on protons vs. ions
Protons
  Simplest problem to solve
  Should try to develop technology for this and then modify for ions
Ions
  Sharper Bragg peak
  More scope for using different isotopes (e.g. C-11)
  ½ the charge-to-mass ratio of protons when fully stripped
    Needs twice as much gradient to accelerate
  Studies should not interfere with proton studies
    Need to develop in tandem
    Multi-ion facilities???

## Slide 9: Contributions from US + UK
Funding
  Need to resolve the US funding “Mexican stand-off”
    Falls between the cracks of DoE + NCI funding
    Work with IARC?
  Joint UK-US funding for R&D?
  Establish international networking grants
Manpower
  Joint PhD students and postdocs
Resources
  Test facilities in US + UK
    In-vivo testing must be performed
Need to be pro-active about establishing long-term collaborative efforts between UK-Fermilab
  Follow-up talks / emails / meetings etc…
  Setup actions, milestones, deliverables

## Slide 10: Reasonably scaled potential collaborative efforts
Proton imaging
  Detector R&D
  Novel imaging techniques
Gantry design
Novel injector schemes?
  Hybrid accelerators

## Slide 11: Should medical applications working group continue?
Simple answer: Yes!
  Lots of people with different skill sets
    Knowledge transfer
  Lots of areas to potentially collaborate on
  UK and US have different areas of focus
    Working together to benefit from individual strengths
However…
  Need to ensure that all communities are well represented
    US / UK
    Clinical
    Manufacturers
    Universities
    National labs