## Slide 1
An overview of Proton Therapy
in the United States
Mark Pankuch PhD
Northwestern Medicine Chicago Proton Center
Proton Accelerators for Science and Innovation : Medical Applications
Fermi National Accelerator Laboratory

## Slide 2: What’s in a name????

## Slide 3: Northwestern Medicine Chicago Proton Center

## Slide 4: The current state of Healthcare in United States
Costs
  For Example: Direct cost of Diabetes in 2012 $176 billion *
    Inconsistent pricing
    Expensive medications
    Over-testing, cautious medicine
    New, more costly technologies
      Robotic Surgery
      Proton Therapy
Reimbursement
  Value based medicine
  Policies for denials of coverage
* American Diabetes Association

## Slide 5: The current state of Proton Therapy in United States
Increasing Interest in Proton Therapy
  2004 : 3 In operation
  2006 : 7 in operation
  2010 : 11 in operation
  2015 : 17 in operation
  At least 9 under construction
Insurance coverage is sometimes difficult
  Often covered after dosimetric comparisons and peer reviews are presented
Many still say “Protons are not a proven technology”
  As of Sept 2015 : 139 clinical protocols for particle therapy*
    Pediatrics /,Head & Neck, Lung, CNS, Breast, GI, GU, Lymphoma, Sarcoma, Eye, Re-treat
  NIH Funded : PCORI Pragmatic Randomized Trial of Proton vs. Photon Therapy for Patients with Stage II or III Breast Cancer : ~$12M 1,700 patients
* Reported to PTCOG from all particle therapy centers, worldwide, including heavy ions

## Slide 6: In the United States

## Slide 7: Indiana University Proton Therapy Center
Will other proton center close??
University’s scientific accelerator adopted into a Treatment Center
Not in the ideal location
Dated technology
High cost for upgrade

## Slide 8: Passive Scattering : Single or Double scattered

## Slide 9: Active Scanning / Uniform Scanning

## Slide 10
Patient Specific Devices
Aperture
Notes: 10

## Slide 11: Universal Nozzle with Aperture and Compensator

## Slide 12: The benefits of a compensator

## Slide 13: Pencil Beam Scanning

## Slide 14: Pencil Beam Delivery
Layers of unique spot patterns delivered over the target volume
Distal AND Proximal conformity
The ability to perform Multi-Field Optimizations

## Slide 15: Advantage of Using a Compensator
No Compensator
With Compensator

## Slide 16: PBS Delivery with Layer Stacking

## Slide 17: Advantages of PBS
With Compensator
PBS

## Slide 18: Different Methods of Optimization
Single Field Uniform Dose Optimization
  Uniform Dose is delivered by each field individually
  Less sparing of critical structures
  Less sensitive to uncertainties
Multi- Field Optimization
  All field spot weights are optimized together
  Better for sparing critical structures
  More sensitive to uncertainties

## Slide 19: Single Field Uniform Dose
OAR
< 100% of Dose
100% of Dose

## Slide 20: Multi-Field Optimized
OAR
< 100% of Dose
100% of Dose

## Slide 21: Spot Scanning in Chicago

## Slide 22: PBS and the Radiation Oncologist

## Slide 23: SFUD with range error
OAR
< 100% of Dose
100% of Dose

## Slide 24: MFO with a range error
OAR
< 100% of Dose
100% of Dose

## Slide 25: Pencil Beam Scanning
Maximum Potential benefits for Protons require the implementation of PBS
  Greatest dose control of dose
  Better Target coverage
  Lower dose to Organs at Risk (OAR)
All new proton centers have PBS capabilities, or have plans to implement in the future
  Some new centers have dedicated to PBS delivery only
Most operating centers have upgraded or plan to upgrade to enable PBS delivery

## Slide 26
+
=

## Slide 27: Head / Neck with PBS
Proton PBS
Photon IMRT

## Slide 28: Lt Sided Breast

## Slide 29: Protons beam

## Slide 30: The future looks bright!
Future development should be focused on Pencil Beam technology
Several things can be improved
  Range uncertainty
  Delivery system
  Pencil Spot size
  Cost
With some more work…….

## Slide 31: Range Uncertainty
Improved Imaging Methods
Patient anatomical changes
  Set-up variances
  Changes in particle path length
    Weight loss / Weight Gain
    Target response to radiation
  Motion
Inaccurate Range calculation
  Errors in the conversion for HU to Stopping Powers
    Trying to use X-ray as a spectrometer
    X-Ray Beam hardening
    Potential for inter-human tissue variability
On treatment Volumetric Imaging
Faster Delivery
Variable Spot Size

## Slide 32: On-Board Imaging / In-room Imaging
2-D Planar Image
3-D Volumetric Image

## Slide 33: On-Board Imaging / In-room Imaging

## Slide 34: Proton Imaging
Using transmission protons to directly reconstruct
  Proton Radiographs (Positioning AND Pre-treatment Range verification)
  Precursor to volumetric Stopping Power maps

## Slide 35: Will Proton tomography required in every room??
Standard CT
Proton CT
Dual Energy CT
Proton radiograph
CT Corrections
Approximation
Truth

## Slide 36: Moving Targets
Temporal dependencies of the PBS delivery system need to be understood when there may be motion
  Lateral Spread
  Longitudinal Spread
  How long each takes

## Slide 37: Moving Target
Geometric miss of target

## Slide 38: Moving Anatomy Altered Path-length
Range Error
Altered
Path length

## Slide 39: Lateral Beam Spread
Depth
Dose
~ 1 second

## Slide 40: Longitudinal Beam Spread
Depth
Dose
2 to 5 seconds

## Slide 41: If our delivery is to a moving target : Interplay
Rietzel and Bert Med. Phys. 7, 2010

## Slide 42: Single /Multiple Fraction and spot size
MGH/PSI Grassberger, et.al Int J of Rad Onc Biol Phy 86, 2013

## Slide 43: The Proton Community's need :
Faster Spot to Spot switching (In a single Layer)
Faster Layer Switching (Layer Stacking)
Variable Spot Size
  Variable Intra- Layer spot size

## Slide 44
IBA Full Gantry

## Slide 45: Hitachi : Mayo Clinic

## Slide 46: The need for lower cost
Smaller Centers ??
Less expensive accelerators
All this functionality

## Slide 48: Mevion

## Slide 49: Are we the best we can be yet???
Probably not…
But we are getting close
  Pencil Beam Scanning
  Faster control systems
  Reduced range uncertainties
  Smaller centers
  All at a lower cost