## Slide 1: LArIAT T-1034 Operational Readiness Review Data Acquisition and Trigger William Badgett Fermilab on behalf of The LArIAT Collaboration

## Slide 2: DAQ Top View
FTBF TDCs 1.2ns
V1751 1nsec
V1740 128nsec
V1740 128ns
WUT 15psec
Tasks:
“Configure, Trigger, Readout, Build and Write”
Five independent asynchronous readout systems

## Slide 3: Beam and DAQ+Trigger Timing
$00 All systems and data fragments synchronized to $00 start of each super cycle
BEAMON and COSMICON are inputs to trigger

## Slide 4
Requirements & Solutions
Have 4.2 second window beam spill + 24 seconds cosmics every 60 second super cycle
Cannot read every sample without custom readout hw $$$
Must have triggered system handle ~ 100 – 200 triggers/spill
TPC Data volume dominates requirements
  ~ 350 μsec max drift time, plus padding = 393 μsec
  Ideally 128 nsec sample time, 256 nsec adequate, 512 ns if needed
  480 wires to readout, no zero suppression, two bytes per channel per sample
Found solution with CAEN V1740 64 channel wave form digitizer
  High density 6U VME, single width – need 8 cards
  Required new “decimation” in firmware to slow 16 nsec to 128 nsec …
  Large buffers can store 64, 128, 256 events, depending on T width

## Slide 5: CAEN V1740 VME Crate
V1740 Crate prior to analog hookup
Note daisy-chained digitizer clock
Chained optical link for configuration and readout
Common trigger and reset $00 inputs from fanouts
V1740s constantly digitizing to circular buffer
On receipt of trigger, copy buffer to memory location
Ready immediately for subsequent trigger

## Slide 6
Beam line and Light Collection
Light collection (ToF, Aerogel, LCS) have much faster time scales
  ~ 10’s of nsec
  2 ✕ CAEN V1751, eight channels each, 1 nsec sampling
  Typical wave form width 28 μsec
  Specially modified for 200 mV scale (single photo-electrons)
  Read via CAEN CONET optical link to A3818 PCI bridge
  For precision ToF hit timing use WUT Wave Union TDC, resolution ~ 15 psec
  Read via VME via PCI bridge
Wire Chambers with max drift ~ μsec
  Use established Hansen readout supported by FTBF staff
  Have 1.17 nsec granularity, independent clock
  Multi-hit TDCs, four chambers, (x,y) (128,128) 1024 channels
  Spill stored entirely in on-board buffers, collated to central controller
  Read at end of spill by main Lariat DAQ over ethernet
TPC contra mundum
  Two very different time scales  fast and slow triggers!
WUT
A3818

## Slide 7: Data Flow Diagram
Details of LArIAT DAQ Readout Data Flow
Several external sources read and collated by single event builder “DAQ PC”

## Slide 8: Online Computing
Demand for online computing modest but critical
One 8 core for configuration, readout, archiving
  Install CAEN A3818 four channel optical bridge (large)
  Locally cache at least one week of data (more in reality)
One 8 core for online data quality monitoring
  Need one minute feedback for beam and detector conditions
  Redundant power, redundant disk (thanks, SLAM group!)
Hot backups for each function
Two thin gateways for access
Strong firewall to access main DAQ, DQM per FNAL and DoE security requirements (unusual for test beam)

## Slide 9: DAQ Software
“KISS” – Keep It Simple, Stupid!
No Quixotic GUI developments, nunca!
Configure system via human readable XML text files
  One per subsystem, store entirety in data stream and LArIAT database every run in structured form
  Easy to include, exclude components and tweak their setting
  Expert access only, shifters do not access
To start a run, simply type “go” at the prompt
  Yes, it’s really that easy!
Display run status in a single easy-to-use web page
  No, it doesn’t really count as a GUI

## Slide 10: LArIAT Run Status
Simple, succinct table indicating all pertinent DAQ and Trigger quantities showing the run is proceeding apace

## Slide 11: DAQ Software, Details
LArIAT Readout Kernel
Configuration and Readout factorized by C++ classes per subsystem, using OO inheritance to simplify coding
  Each subsystem class outputs Lariat specific data fragments
Main LariatReadout class conducts configuration and readout
  Monitors triggers via interrupts and polling
  Watches for spill status in order to cleanup and end and restart
LArIAT kernel wrapped into ArtDaq Boardreader class
  Lariat_generator extends LariatReadout
  Wraps all Lariat specific fragments into one ArtDaq Fragment per spill
  Converts raw binary to Root object readable by Art and LArSoft

## Slide 12: LArIAT Data Fragments
Class names and contents, produced by LariatReadout, defined in shared online and offline package LariatFragments
V1740Fragment
  TPC wires’ wave forms
  Trigger hit timing digital wave form
  Muon Range Stack
V1751Fragment
  ToF, AeroGel, Light Collection (PMTs, SiPMS)
V1495Fragment
  Trigger counters and configuration
TriggerFragment
  Pipeline of all trigger input pattern, including time stamps
WUTFragment
  High precision ToF hit times
TDCFragment
  Beam wire chambers’ hit times
NB: At this level, each fragment is asynchronous to the others and time slicing takes place down stream (see later talk). At readout time, all fragments from one spill are concatenated into one ArtDaq Fragment. See backup slides for synchronization demonstration.

## Slide 13: Data Archiving
DAQ
Collection
Transporter
DAQ
Disk
dCache/
enStore
SAMweb
File
Catalog*
User
Data available signal
DAQ Computer
Request/Get File Names
Request/Get Files by Name
DAQ closes data file and signals archiver to pick up file
dCache/enStore/PNFS: Archiving/file serving process
SAM: Cataloging / description / metadata process
Uses standard Fermilab FTS file transport service
Data files easily retrievable via simple SAM queries
HTTP Transfer
SAM file header
FTP
Data File

## Slide 14: DAQ Hiccups in Run 1
Getting new and existing futures on the CAEN digitizers involved months of iterative debugging and fixes
  Most issues solved prior to Run 1
Remaining issues, CAEN V1740 and V1751 digitizers
  Occasional event counter mismatches, expect BUSY mechanism to help
  Pedestal jumps on V1751s – “ameliorated” by register retries
  Found unexpected V1740 post-trigger dead-time – fixed by CAEN
  Rare readout hang-ups < 0.1%
Wire Chamber TDC readout
  Occasional loss of configuration registers
  Regular failure of basic data sanity checks, data nonsense
  Text based interfaced to TDC controller not reliable – losing bytes

## Slide 15: LArIAT Trigger
Several detectors means several possible trigger sources
With long TPC time scale, fast light time scale:
  Fast Trigger: Readout light, wire chamber, ToF, AeroGel (on V1751s), plus Wire Chambers’ TDCs
  Delayed Trigger: Readout TPC, one readout window later
  Allows time to veto TPC readout in case of pile-up or halo, saves bandwidth
  Also allows intra-drift trigger, e.g. Michel electrons, more info
Need flexible, programmable trigger
  Implement trigger logic and scalers on user-programmable CAEN V1495 VME based FPGA card
  Think CDF Fred or CMS GL1T, unusual for test beam
  Configurable and readable over VME bus
  Serves as final logic for several crates of NIM logic discriminating many detector signals

## Slide 16: Simplified Trigger Logic
32 arbitrary external NIM inputs on the left
Input latch and counters at 100 MHz ✕ 2
16 coïncidence logic units trigger paths
OR of paths indicates fast trigger
Delay, plus NOT VETO indicates delayed trigger
Record triggers + times in FIFO for VME readout

## Slide 17: V1495 Trigger Card
32 Trigger Input, twisted pair ECL (NIM to ECL)
Reset Input on $00
Fast and Delayed Trigger Output
CAEN V1495 Card in situ, prior to cabling
Three 32 bit built-in logic I/O ports
One optional NIM input module
Trigger Counter and Trigger Path Identifier
Send to V1740 for latching on trigger
(synchronization check)

## Slide 18: 16 Typical Trigger Inputs
Input | Source | Input | Source
WC1 | Wire chamber up stream | HALO | Beam halo counters
WC2 | Wire chamber 2 | PULSER | Hardware pulser, testing
WC3 | Wire chamber 3 | COSMICON | Cosmic post-beam gate
WCC * | Wire chamber majority logic | COSMIC | Cosmic paddles
BEAMON | Spill beam gate | LARRY | Cosmic trigger with light
USTOF | Upstream Time of Flight | MICHEL | Michel electron
DSTOF | Downstream Time of Flight | LARSCINT | LAr scintillation light
PUNCH | Punch-through counter | MURS | Muon Range Stack
* WC exceptionally has majority logic, 3 / 4
Above inputs can be specific in up to 16 trigger output paths, required ON or OFF
Delayed trigger VETO uses same input logics with opposite logic
All logic stored in LArIAT database available for offline use

## Slide 19: Typical Trigger Output Paths
Run 6373, near end of LArIAT Run 1 when things were quite stable
With 866 spills, > 14 hour run
Path | Trigger Requirements ON | Required OFF
1 | BEAMON+USTOF+DSTOF+WCC | 
2 | BEAMON+USTOF+DSTOF+WCC+PUNCH+MURS | 
3 | BEAMON+USTOF+DSTOF+WCC+PUNCH | -MURS
4 | BEAMON+USTOF+DSTOF+WCC+MURS | -PUNCH
5 | COSMIC | -BEAMON
6 | LARRY | -BEAMON
The delayed trigger VETO function was not normally required
Run 2 we will use a BUSY function in the VETO logic

## Slide 20: Trigger Running Experience
Generally excellent reliability and functionality
  Firmware code often difficult to understand – most problems related to us not understanding the logic
  Flaws with the PCI to VME bridge had already been worked out by CMS a while back
Implementing upgrades during shutdown
  Adding 16 additional trigger input for a total of 32, since we were over-subscribed at 16
  Adding adjustable software-controllable pulser logic
  Capability to pre-scale one or more trigger paths – useful for background studies with high rate triggers à la colliders

## Slide 21
Backup Slides

## Slide 22: Hardware Spares
VME Crate | Spare | Spare
TPC and μRS+ | Wiener VME64x | One chassis, no power supply
ToF, Light, Trigger | CAEN VME64x | One spare CAEN with power supply
Detector | Digitizer | In System | Spares
TPC | CAEN V1740 | 8 | 0
μ Range Stack + | CAEN V1740 | 1 | 0
Light collection + ToF | CAEN V1751 | 2 | 0
High res ToF | WUT | 1 | 0+
Trigger | CAEN V1495 | 1 | 0
VME Master | CAEN V2718 | 1 | 0
PCI-VME Bridge | CAEN A3818 | 1 | 1
There may be money for spares in FY16

## Slide 23: Cross-Detector Synchronization
Time matching between wire chambers and ToF PMTs
Note offset and slope corrections
Stability improved with time