## Slide 1: Space Charge Losses in Booster at Injection
Alexander Valishev, Valeri Lebedev
November 24, 2015

## Slide 2: Credits and Acknowledgments
Y.Alexahin, J.Amundson, C.Ankenbrandt, W.Chou, A.Drozhdin, X.Huang, N.Kazarinov, J.Lackey, J.MacLachlan, E.Malamud, E.McCrory, L.Michelotti, F.Mills, D.Moehs, K.Y.Ng, S.Ohnuma, F.Ostiguy, M.Popovic, E.Prebys, P.Spentzouris, R.Tomlin, Xi.Yang, R.Zwaska
M.Fitterer, F.Schmidt, D.Shatilov

## Slide 3: Selected References
http://www-bd.fnal.gov/pdriver/booster/
http://frs.home.cern.ch/frs/Source/space_charge/
F.J.Sacherer, Ph.D Thesis, University of. California, Berkeley, UCRL-18454 (1968)
A.Fedotov, I.Hofmann, “Half-integer resonance crossing in high-intensity rings”, PRSTAB 5, 024202 (2002)
E.Prebys et al., “Increasing the intensity of the Fermilab Booster”, PAC’03
W.Chou et al., “Fermilab Booster Modeling and Space Charge Study”, PAC’03, DOE Review
S.Cousineau et al., “Resonant beam behavior studies in the Proton Storage Ring”, PRSTAB 6, 074202 (2003)
J.Amundson P.Spentzouris, “Space Charge Experiments And Simulation In The Fermilab Booster”, PAC’05
Y.Alexahin et al., “Effects of Space Charge and Magnet Nonlinearities on Beam Dynamics in the Fermilab Booster”, PAC’07
S.Bernal et al., “RMS envelope matching of electron beams from ‘‘zero’’ current to extreme space charge in a fixed lattice of short magnets”, PRSTAB 9, 064202 (2006)
X.Huang et al., “Emittance measurement and modeling for the Fermilab Booster”, PRSTAB 9, 014202 (2006)
M.Fitterer et al., “Systematic studies on the effect of linear lattice optics for space-charge limited beams”, PRSTAB (2015)

## Slide 4: Motivation and Outline
Another look at incoherent Space Charge effect in Booster at injection aiming to
  Understand the current limitations.
  Make projections for PIP-II and post-PIP-II era.
  Synergistic with IOTA program
This presentation is about work in progress.
Outline:
  The problem, approach and previous work
  Modeling tools
  Some results
  Questions, proposals and next steps

## Slide 6: Our Study Goals (Back to the Future Part II)
With the help of realistic and useful Booster model (talk by C.Y.Tan)
  It appears many previous studies might have been using incorrect models
Understand the role of Booster lattice on space charge induced loss and emittance blowup
Quantify the requirements on optics control
  Iterate with models
Propose and evaluate possible improvements

## Slide 7: Approach
If one forgets about coherent instabilities (A.Macridin’s talk), the action of direct SC on stability of particle motion is through the time modulation of nonlinear transverse field and consequently, betatron and synchrobetatron resonances.
  Emittance growth and particle losses.
Modeling can be done with following simplifying approximations (frozen SC):
  No self-consistency: Gaussian beam profile.
  Many thin kicks per turn instead of smooth action.
This approach offers quick turnaround time with decent physics
  Can and should be followed by true self consistent modeling

## Slide 8: Previous Work
2003 – W.Chou et al., “Fermilab Booster Modeling and Space Charge Study”
  Effect of doglegs on acceptance
  Modeling chromaticity
2006 – X.Huang et al., “Emittance measurement and modeling for the Fermilab Booster”
  Half-integer resonance not important
  Vertical emittance growth through coupling
2007 – Y.Alexahin et al., “Effects of Space Charge and Magnet Nonlinearities on Beam Dynamics in the Fermilab Booster”
  Half-integer resonance contribution evaluated
  Proposed sc compensation

## Slide 9: Previous Work
Simulations
  ESME
  ORBIT-FNAL
  STRUCT
  MAD/Mathematica
  madx-PTC
  Synergia (the sole survivor)

## Slide 10: Modeling Tools
We were using Lifetrac:
  20 years of development as beam-beam tracking code (many e+e- colliders, Tevatron, LHC, HL-LHC).
  Single-particle tracking, well-parallelized tracking of multiparticle distributions, Frequency Map Analysis, Dynamical Aperture.
Workflow:
  Start with madx lattice file.
  Install thin beam-beam elements (120, 17 per betatron period).
  Produce FMA (quick) and multiparticle distribution evolution (slower).
Limitations:
  Non-adaptive SC (so far, for simplicity).
  Synchrotron modulation not taken into account.
over-estimate
SC

## Slide 11: Booster Parameters in Simulation
Energy | 400 MeV (β=0.713, γ=1.426)
URF | 0.7 MV
Qs | 0.078 (ωs=35 kHz)
Bucket size | 4.2×10-3
Energy spread | 2.1×10-3 (σz=1.26 m) – fully bunched beam
Transverse emittance | 15 mm×mrad (95% normalized)
Aperture | Ax=2.86 cm, Ay=2.08 cm
Np | 0.42×1013 in 84 bunches
SC tuneshift | ΔQx=-0.197, ΔQy=-0.307
Betatron tunes | Qx=6.70, Qy=6.80
Chromaticity | Cx=-20, Cy=-14

## Slide 12: Booster Parameters for “PIP-II mode”
Energy | 400 MeV (β=0.713, γ=1.426)
URF | 0.7 MV
Qs | 0.078 (ωs=35 kHz)
Bucket size | 4.2×10-3
Energy spread | 2.1×10-3 (σz=1.26 m) – fully bunched beam
Transverse emittance | 15 mm×mrad (95% normalized)
Aperture | Ax=2.86 cm, Ay=2.08 cm
Np | 0.66×1013 in 84 bunches
SC tuneshift | ΔQx=-0.31, ΔQy=-0.4
Betatron tunes | Qx=6.70, Qy=6.80
Chromaticity | Cx=-20, Cy=-14

## Slide 13: Lattices Used in Simulation
24-cell fully symetrical FODO (V.Kapin)
24-cell with 10% beta-beat, no coupling
24-cell with 20% beta-beat, no coupling
Actual Booster (C.Y.Tan)
  Chromaticity work in progress

## Slide 14: Results – FMA (a) 0.42×1013

## Slide 15: Results – FMA (a) 0.66×1013

## Slide 16: Results – FMA (a) As=0, 0.42×1013

## Slide 17: Results – FMA (a) As=1*, 0.42×1013
* SC is over estimated for off-momentum particles

## Slide 18: Results – FMA (b) As=0, 0.42×1013

## Slide 19: Results – FMA (c) As=0, 0.42×1013

## Slide 20: Results – FMA (a) As=0, 0.66×1013

## Slide 21: Results – FMA (b) As=0, 0.66×1013

## Slide 22: Results – FMA (c) As=0, 0.66×1013

## Slide 23: Results – Multiparticle Tracking, 0.42×1013

## Slide 24: Results – Multiparticle Tracking, 0.66×1013

## Slide 25: Summary and Next Steps
With known limitations, the method allows for very fast evaluation of options
  Code improvements are in progress
  PIC simulations to follow
The half-integer resonance seems to be the limiting factor
  At intensity of 4×1012 the core particles cross ½
  6.6×1012 is allowed in the ideal 24-fold symmetry lattice
We are studying the possibility of creating lattice with two-fold symmetry
We will work with the optics team to achieve good understanding of the machine model and proper correction of relevant imperfections
  Booster does not have the luxury of large aperture – need to rely on control and precision