## Slide 1: A Fifteen Year Perspective on the Design and Performance of the SNS Accumulator Ring
Sarah Cousineau
on behalf of the SNS Project
Fermilab
11/24/2015

## Slide 2: SNS Accumulator Ring Design Parameters
Circumference: 250 m
Energy: 1 GeV
Intensity: 1.5e14 ppp
# bunches: 1
Bunch length: 700 ns
Accumulation Time: 1 ms
Repetition Rate: 60 Hz
= Beam Power: 1.4 MW
1 GeV H-
1 GeV p
1.4 MW production achieved Friday, November 20.
Design Parameters

## Slide 3: Outline
Performance measures.
What we got right: High pay-off investments
Stuff we worried too much about.
Stuff we should have worried more about.
The power upgrade project.
Attacking our biggest challenge: The H- laser stripping effort

## Slide 4: Ring Performance: Intensity
Production intensity: 1.55e14 ppp
Intensity Limitation: Unknown – not yet found
The SNS accumulator ring has been in operation for 10 years.
It has performed beautifully.
1.56×1014 ppp 1.4 MW

## Slide 5: Ring Performance: Beam Loss
The SNS ring was designed for very low loss.
The result - A very clean ring
Loss level achieved: ~ 2x10-4 of beam at full intensity.
A long list of investments made to ensure this…
...What worked?
collimation
injection
extraction
800
10 - 50
< 5
< 5
< 5
< 5
< 5
< 5
< 5
< 5
< 5
300
< 5
< 5
20
Dosage in mrem/hr @ 30 cm

## Slide 6: Large Aperture: The Highest Payoff Investment We Made
Based on considerations of collective effects, decided to use a very big aperture.
And it works. We use it all.
(Thanks Y.Y. Lee and B. Wang!!)
Element | Diameter (cm) | Acceptance (mm mrad)
Vacuum Pipe | 20 - 30 | 480 pi
Dipole | 23 x 15 | 480 pi
Quadrupole | 21 – 30 | 480 pi
Collimator | 10 – 16 | 300 pi

## Slide 7: Ring Betatron Collimation: High Payoff
We believe that collimation is one of the main reasons we have a clean ring.
Two stage collimator occupies an entire straight section.
Each secondary collimator can absorb:
We do not use the collimator in a two stage fashion. Prioritize aperture.
2 kW continuously, or
2 consecutive 2 MW pulses in failure mode.

## Slide 8: Dual Plane Injection Painting: High Payoff
We paint in both planes with a correlated beam, all the way to collimator aperture.
The injection losses would be intolerable without it.
Painting
No Painting
~ 1 MW Equivalent Beam Profiles
For Two Equal Emittance Beams
Injection Region Beam Loss Monitor Signals
A11c
A11d
A11e
A13
A13b
B01

## Slide 9: e-P Mitigation: Worth the Investment ??
In the area of collective effects, e-p was the biggest concern.
No appr
Trace levels after opening vacuum. No beam loss.
Mitigation Feature | Usage Now
2nd Harmonic RF | Strong knob when e-p present
TiN coating | No way to know if it helps
Clearing solenoids | Not in use
Clearing electrodes | Not in use
Feedback system | Working but not needed
No significant e-p seen during production so far.
< 1 mm oscillation
N. Evans
e-p Activity for 1.4 MW Production Beam

## Slide 10: Two Things We Worried Too Much About
1. Space charge effecst: resonances, halo
Feature | Usage Now
Sextupoles (4 families) | Never used during production
Octupoles (2 families) | Never been used
Sextupole correctors | Never been used
Octupoles correctors | Never been used
2. Extraction loss:
Beam in gap kicker – never installed
Gap smaller, cleaner than expected:
Very good LEBT chopping
Reduced extraction kicker drift

## Slide 11: Injection: We Didn’t Worry Enough
Trajectories not sufficiently modeled.
H0* excited state loss over-constrained the design.
Fallout was many changes once reality struck:
Oversize & thicker primary stripper foil
Thinner, wider secondary stripper foil
Increase septum magnet gap by 2 cm
New C-magnet
New WS, view screen, BPM, NCD (ridicules)
Shift 8 cm beam left
Increased beam pipe aperture

## Slide 12: Menu of Initial Investments and Payoff
Feature | Cost | Payoff So Far
Large Aperture | $$$$ | High
Injection Painting | $$$ | High
Collimation | $$$ | High
TiN coating | $$$ | Unknown
2nd harmonic RF | $$ | Medium
Main sextupoles | $$ | Low
Main octupoles | $$ | None
Sextupole correctors | $ | None
Octupole correctors | $ | None
Clearing solenoids | $ | None
Beam in gap kicker | $ | None
Clearing electrodes | $ | None
We spent the big bucks where it counted most.

## Slide 13: Biggest Challenge: Injection Loss and Foil
Sublimation Range
~1 month @1.3 MW
Nanocrystalline Diamond
~400 ug/cm2 (1 μm thick)
~1500K
We have an aggressive foil development program that has allowed us to get to 1.4MW

## Slide 14: STS and the Beam Power Upgrade
Second target will steal every 10th pulse.
Ring injection region will be carefully redesigned.
We are still worried about e-p.
Parameter | Now | Upgrade
Beam Power | 1.4 MW | 2.0 MW
Beam Energy | 1.0 GeV | 1.3 GeV
Beam Intensity | 1.5e14 ppp | 2.5e14 ppp

## Slide 15: Injection Foils at 2 MW and Beyond
The 2 MW upgrade will used the same foil-based injection scheme, based on:
  No evidence for sublimation right now
  Estimates of 300K temperature increase (not too bad)
  We can take the ~66% increase injection radiation
  We don’t have any other options
We are interested in attacking this problem for the high intensity community.
What if we could inject without the foil?
  Virtually no injection beam loss (no radiation)
  No foil lifetime issues
  Possibility of much higher densities

## Slide 16
?
The Laser Stripping Concept:
A Foil-Free H- Charge Exchange Injection Scheme
H-
p+

UV Laser Beam
H0
H0*
High-field Dipole
High-field Dipole
H-  H0 + e-
H0 (n=1) +   H0* (n=3)
H0*  p + e-

## Slide 17: The Laser Stripping Project
Laser Stripping Project:
Demonstrate laser stripping for longer pulse lengths:
  10 us (2016)
  1 ms (2019?)
Technology aimed at HEP applications.
Funded by DOE HEP grant (DE‐FG0213ER41967) UT, ORNL, Fermilab
Required 10 MW, diverging laser to accommodate excitation frequency spread
Straightforward scaling to 1 ms requires ~600 kW avg UV laser power (too much!)
6 ns
H-
p
2006 Proof of Principal Experiment

## Slide 18: Reducing the Required Laser Power
n
H0
H0*
UV
γ
2. Eliminate resonance transition frequency spread:
POP experiment setup used a diverging laser beam
n
H0
H0*
UV
γ1
γ2
γn
3. Maximize laser ion cross section: Squeeze the beam:
σy ≈ 0.2 mm
σl ≈ 30 ps
Don’t waste the laser power: Temporal matching:
2.5 ns
30 ps
402.5 MHz
H- Beam
402.5 MHz
UV Laser
600 KW
60 W
Average
Laser
Power

## Slide 19: Laser-Ion Beam Temporal Matching
UV peak power achieved: 1.3 - 3.0 MW
Y. Liu, A. Rakhman
Master oscillator power amplification (MOPA) system
Structure | Time | Frequency
Micropulse | 30 – 55 ps | 402.5 MHz
Macropulse | 5 – 10 us | 10 Hz

## Slide 20: Experimental Configuration
Interaction point in the HEBT, laser in the Ring Service Building.
Final optics station and IP
chase
Laser table
Ring Service Building
Ring/HEBT Tunnel
A. Menshov
Laser transport introduces complications (power loss, pointing stability)
Transport Line:
70 m
7 mirrors, 2 windows

## Slide 21
Laser Transport Mock-Ups
Piezoelectric tuner will stabilize laser against > 1 Hz drift.
Mirror losses independently measured to be ≤1%.
Expect ~ 1/3 power loss (Fresnel diffraction, higher order mode loss).
Output Power
From Laser
8 m
6 cycles = ~48m
Conclusion: Remote laser placement is feasible.
Y. Liu, A. Rakhman

## Slide 22
Laser Stripping Efficiency Calculation
All ion and laser beam parameters achieved.
Efficiencies calculated with as-measured parameters, >90% (pyORBIT)
One major concern is that we will break the vessel window
90%
30%
Stripping Efficiency
Laser Power
Tuning here
Final demonstration
only
~1 MW
Experimental Procedure
Final Stripping Efficiency
Concern about power density on window
Courtesy T. Gorlov
Laser radius (mm)
Laser divergence (mrad)

## Slide 23: Installed Experimental Station
Almost finished installation
Experiments schedule for Spring 2016.

## Slide 24: The Next Step: 1 ms Stripping
H- beam
Power recycling cavity relies on CW laser for stable lock.
Amplification of burst mode laser.
50 times power enhancement demonstrated.
Add the recycling cavity to achieve 1 ms laser pulses
Cavity
Burst-mode UV beam
Cavity locking beam

## Slide 25: Summary
The SNS ring is performing extremely well at it’s design parameters.
We struggle with injection foil issues.
We are planning for an upgrade in beam power from 1.4MW to 2MW.
We are working on the development of H- laser assisted stripping.