## Slide 1: Booster alignment and aperture
Kiyomi Seiya
Workshop on Booster Performance and Enhancements
23 November 2015

## Slide 2: Goal: Move magnets to open up apertures

## Slide 3: Outline
Aperture Scan Program
Components in the Booster and Their Aperture
Process of Magnet Realignment
Results of the Magnet Realignment
Status of the Aperture and Orbit
Plan
S. Chaurize
W. Marsh
W. Pellico
K. Seiya
T. Sullivan
K. Triplett
A. Waller

## Slide 4: Booster lattice
Combined function magnets: F, D
FDOODF x 24 periods
Corrector packages at short and long
Corrector package (12 poles) includes
H & V dipoles, quad, skew quad, sextupole, skew sextupole
and H & V BPMs.
F Magnet
D Magnet
Corrector Package

## Slide 5: Aperture scan with B75 application
3bump
5bump
Changes corrector current at injection

## Slide 6: Aperture scan with B75 application #2
Intensity
Int@ext/int@400MeV
Int@inj/Int@400MeV
H Corrector current
BPM position
V Corrector current
I_H [A]
I_V [A]
BPM_H [mm]
BPM_V [mm]

## Slide 7: Offline analysis with Java program

## Slide 8: Booster lattice and beam size
bx @short = 33.7
bx @long = 6.1
by @short = 5.3
by @long = 20.4
H_emittance(95%) = 14p mmmrad
V_emittance(95%) = 16 p mmmrad
+/-21.5 mm
+/-17.9mm
+/-9.12 mm
+/-9.15mm
@ SHORT straight
@ LONG straight
beam size
SHORT straight
LONG straight

## Slide 9: Aperture at Short straight sections
41.66mm
114.3mm
F magnet
4.5 inch beam pipe and corrector
1.64 inch gap

## Slide 10: Aperture restriction at S14

## Slide 11: Aperture at Long straight sections
57.17mm
57.17mm
D magnet
2.25 inch gap

## Slide 12: Components at the Long straight section
RF beam pipe has
smallest diameter.

## Slide 13: Magnet Move at L16
#1
D F F D D F F D
#2
#3
D F F D D F F D
#4
#5
D F F D D F F D
#6
#7
D F F D D F F D
#8
#9
D F F D D F F D
#10
#11
D F F D D F F D
#12
#13
D F F D D F F D
#14
#15
D F F D D F F D
#16
#17
D F F D D F F D
#18
#19
D F F D D F F D
#20
#21
D F F D D F F D
#22
#23
D F F D D F F D
#24
+5mm
-5mm
0
+5mm
-5mm
0
1.3 mm
1.3 mm
Four magnets were realigned on Aug. 6, 2013
15-3 upstream: 0mm 15-3 downstream: +0.6mm 15-4 upstream: +0.7mm 15-4 downstream: +1.3mm 16-1 upstream: -1.3mm 16-1 downstream: -1.3mm 16-2 upstream: -1.3mm 16-2 downstream: -1.3mm

## Slide 14: Orbit difference before and after Magnet Move (simulation)
MAD
Magnet Move program
+/-0.6mm

## Slide 15: Aperture at L16 before and after the Magnet Move
Before Move4
After Move4

## Slide 16: Orbit difference before and after Magnet Move (measurement)
Vertical
Horizontal
+/-0.8mm

## Slide 17: Vertical magnet position after Magnet Move

## Slide 18: Vertical aperture before and after alignments and Magnet Move
Long
Short
Collimators
Collimators

## Slide 19: Smoothing orbits
November, 2015
April, 2012 ($19 operation cycle)
10
0
-10
H [mm]
10
0
-10
V [mm]

## Slide 20: Orbit compared to the central aperture at injection
Orbit has large angle at collimators and absorber.
There was more beam loss at the central aperture.

## Slide 21: 7 break points on the corrector ramp
Break points
#0(2.2msec)
#1(3msec)
#2(6msec)
#3(10msec)
#4(20msec)
#5(32msec)
#6(35msec)
#7(60msec)
Moved 1st break point from 2msec to 2.2msec.
Corrector current is flat during injection.
Notch happens before 2nd break point.
Orbit should be at center after 3msec.
Intensity
Corrector current
#0(2.2msec)
Notch at 2.17 msec
#1(3msec)

## Slide 22: Summary and Plan
Aperture scan was performed with B75.
B75 is operational
Magnets were moved at 5 locations.
Understood how to move magnets based on simulation results.
Vertical aperture was improved.
Plan
Optimizing orbit at collimators and absorber
Smoothing orbits on regular basis
Acknowledgements
Alignment Group
F. Ostiguy

## Slide 23: Aperture scan with 3 bump and 5 bump
F
D
RF
Corrector
+
BPM
Scan @ SHORT
Scan @ LONG

## Slide 25
r_F(design)=75.508566m+0.053inch
r_D(design)=75.434828m-0.040inch
need reference position for each component