## Slide 1: Digital Damper Systems in Booster
Nathan Eddy
Workshop on Booster Performance and Enhancements
Nov. 24rd 2015

## Slide 2: Outline
Digital Transverse Damper
  Motivation
  System Overview
  Tune Measurement
  Diagnostics
Digital Longitudinal Damper
  Motivation
  System Overview
  Commissioning
  Operation

## Slide 3: Transverse Damper - Motivation
Goal to demonstrate a digital bunch by bunch digital feedback system in Booster
  FPGA, ADC, Digital Signal Processing, DAC
  Wideband system
  Flexibility to modify system as needed
Essentially an R&D project so far
  Demonstrate transverse system operation
  Diagnostic capability – tune, studies, etc
  Develop plan for longitudinal system

## Slide 4: Transverse Damper System Overview

## Slide 5: Current Transverse Damper Installation
Input Signals
Sum/Diff Amps
Digital
Damper
Output
Amps
RF Ref
TCLK

## Slide 6: VME Digital Damper Board
Developed in 2006 as R&D Large
Stratix II FPGA handles signal processing & interfaces on multiple clock domains
4 ADC (up to 212MHz) & 4 DAC (up to 636MHz) locked to external RF
Digital I/O – TCLK, MDAT, BSYNC decoders, fanout, diagnostics
Up to 1GB on-board RAM via standard DDR2 SoDimm
VME front-end speaks ACNET via standard Controls front-end

## Slide 7: Transverse Damping
Cable delay to sync RF Ref with beam signals
Sample at 4xRF
  Adjust ADC clock via PLLs in FPGA
  Pseudo I,Q sampling
Programmable Turn Filter
  4 bit coefficients
  3 Turn Horizontal
  5 Turn Vertical

## Slide 8: Transfer Function Measurements with VSA

## Slide 9: Diagnostic Capability
Record bunch by bunch data for entire Booster cycle
  Position, Intensity, Phase
Measure Booster revolution frequency
  1Hz resolution @1ms

## Slide 10: Horizontal Instability Study (2011)
Damper Off
Damper On
Developed when trying to decouple optics after injection
  Demonstrated damper operation on real instability
  Damper showed slow developing Mode 8 coupled bunch
Results presented at IPAC12

## Slide 11: Tune Monitor
Excite Single Bunch & Measure Response
  Minimally invasive
  Can be run on operational cycles
Fully programmable
  Select Bunch
  Excitation
  Up to 32 Measurements per cycle

## Slide 12: Transverse Damper Issues
Horizontal response is not optimal due to pickup & kicker locations
Difficulty exciting beam horizontally after transition
  Chromaticity
  Power
RF Clock Lock
  Causes PLLs for ADC/DAC to relock
  Requires re-phasing

## Slide 13: Transverse Damper Status
Transverse Damper currently is not needed for operation
  Can we lower Chromaticity?
  Do we require more power in the horizontal plane?
Investigate options for moving horizontal pickup & kicker and/or adding additional pickups
  Ideal scenario is two pickups ~90 degrees apart
  Is our current stripline pickup ideal? Use BPMs?
Developing Replacement based upon 1GS/s ADC
  Improve timing/phase stability
  Expect to be able to detect head-tail
  Can we damp it?

## Slide 14: Longitudinal Damper - Motivation
Upgrade the analog damper system
  Critical system
  Requires dedicated hardware for each mode
  Long operational history
Replace difficult to maintain system with digital system
  Limited diagnostics
  Can take days to fix problems

## Slide 15: Digital Longitudinal Damper Test Installation
WCM
Phase Pickup
Mode 1
Digital
Damper
Mode N
Notch
Filter
BP
Filter
Pickup
RF Ref
TCLK
First installation thrown together in back of rack
  WCM input, RF Reference, TCLK, Up to 4 outputs (RF, Cavity)
Eventually will replace existing analog system with clean simple one board solution

## Slide 16: New Digital Feedback Board
Developed for general purpose
  4 250 MS/s ADCs
  4 500 MS/s DACs
  Dedicated PLL based clock distribution chip
  Very good clock jitter, limited to 2Mhz Bandwidth
Locks before transition on every Booster cycle
  Big effort to make this stable
  Looks good so far…

## Slide 17: Longitudinal Damper Block Diagram
Entire design runs locked to RF
16 fully programmable channels (12 – cavity, 2 RF, 2 Reference)
Same NCO generates sin, cos for I,Q mixing
NCO frequency is centered on rev harmonic of interest
Mɸ correspond to programmable magnitude/phase shift
Will also suppress carrier
For output use Weaver Model – preserves sideband structure
25KHz

## Slide 18: Diagnostics -
Raw Data – up to 16M pts
Downconverted Mode signals

## Slide 19: In the Beginning…
Struggled to see expected response
Let’s try to blow things up… Led back to bench
  Discovered bench testing setup was using LSB input…
  Inverting sign set to produce USB output
Should be able to measure Beam Transfer Function…

## Slide 20: Initial Damping
Need to shift phase to account for fixed system delays
  Cables, amplifers, etc.
Initial attempt to set phase on response data not successful…
Traditional Booster “Tuning” employed

## Slide 21: Semi-Operational System
Put into operation in parallel with analog system due to noticeable beam quality improvement
ACNET Application still under development
  Implementing features
  Diagnostics
Can proceed on Backup/Development node while system is “operational”
Next step turn off the analog system…
Remove old system next shutdown

## Slide 22: How about Mode 2?
Beam measurements in the MI-8 line which show amplitude and phase of extracted Booster bunches
With the new digital dampers working – phase errors look excellent and should help reduce loses in downstream machines
Phase error
Bunch Phase
Bunches
Bunches
16
-16

## Slide 23: Summary
Transverse Digital Damper
  Demonstrated ability for digital system to “work” in Booster
  Minimally invasive Tune Monitor & Diagnostics very useful
  Need system upgrades to improve Horizontal response
  Upgraded board under development
Longitudinal Digital Damper
  In operation in parallel with old analog system
    Has made tuning on old system unnecessary
    Improved performance beam quality
    Gaining confidence in stability
  All the benefits of a digital system
    Diagnostics, flexibility, stability
  Would like to implement BTF measurement – VSA again?