## Slide 1: Production Cryomodule Testing
WG-3

## Slide 2: Production Testing Summary - 1
What does Production mean?
  Speed!, but as complete as possible
  Both single cavities and unit
  Not measuring as an ends, but what’s necessary to verify functionality
Acceptance criteria – what’s important
  Total gradient stable gradient (~10 hour minimum to investigate coupler heating)
  Total heat load
  Tuner/cavity frequency
  HOM power
  Radiation/dark current
  BPM
  Magnet
  Heaters
  Thermometry
  Liquid level sensors
  JT valve, CoolDown/Warm up valve
  Vacuum
  Static heat loads: measure as best as we can.
  Endurance test of 10-16 hours, all cavities on.

## Slide 3: Production Testing Summary - 2
When to reject; how long does one troubleshoot before warming up and removing?
  See last bullet with actual range of parameters.
  Troubleshooting time varies case by case.
Usable Eacc (operating vs. breakdown or administrative limit) – Measure each cavity
Q0
  Rate of rise
Onset of FE, magnitude at nominal gradient
  Measure total, then individual cavity to identify the poor ones.
Dark current
  Same as above
What is the Rework plan?
  To be determined on a case-by-case basis
  Options/some forethought about likely failure modes
  Schedule rules!
Coupler condition – warm and cold
Qext range – 1e7 to 6e7
Tuner/piezo range & resolution – Slow 1.3 GHz +/-20 KHz, fast 0-500 Hz
Microphonics/LFDC – measure and evaluate
Soak time: 10 hours based on pCM results
Interlock trip points need to be determined
Magnetic Shielding
Rs_res,Rs_BCS (are R measurements possible on a CM?)

## Slide 4: Production Testing Summary - 3
What needs to be Standardized
  Directional couplers & Eacc calibrations
  Field emission
  Interlock/trip logic
  Q0/DHL measurement