## Slide 1: Overview of TPC Signal Processing
Xin Qian
BNL

## Slide 2: Overview of Signal Processing
time
Number of ionized electrons
Signal on Wire Plane
Field Response
Signal to be digitized by ADC
Electronics Response
High-level tracking …
(Deconvolution)
V. Radeka
TPC signal consists of time and charge information from induction and collection planes
  Same amount charge was seen by all the wire planes
The goal of signal processing is to extract both time and charge information reliably

## Slide 3: What will affect TPC signal?
E-field:
  Electron drift velocity
  Recombination factor
Electron lifetime
  Drift distance  drift time  signal size
Track angle
  Time structure of signal
dE/dx
  Recombination etc.
Diffusion
dE/dx fluctuations
MPV: ~ 1.8 MeV/cm

## Slide 4: Field and Electronics Response
Cold electronics:
4 shaping time (0.5, 1.0, 2.0, 3.0 us)
4 gain (4.7, 7.8, 14, 25 mV/fC)
Leon, SLAC
Charge vs. Time averaged for a single electron
Difference between simulation and data (bigger signal in LongBo arXiv:1504:00398)

## Slide 5: Deconvolution
Fourier transformation
Time domain
Frequency domain
Back to time domain
Anti-Fourier transformation
Time Domain
Frequency Content
Deconvoluted Signals
The goal of deconvolution is to help extract charge and time information from TPC signals
Notes: Explain
1. What is filter like in the frequency domain?
2.Why filter is necessary (e.g. plot results w and w.o. filter )
3. Why we need a zero at zero frequency?

## Slide 6: Deconvolution and Matrix Inversion
We can also write the formula in a discrete manner
If there is no filter function in the deconvolution process , the FFT deconvolution is basically equivalent to the matrix inversion problem
Fourier transformation
Time domain
Frequency domain
Back to time domain
Anti-Fourier transformation

## Slide 7: Matrix Inversion and Chi-square
Matrix inversion can be derived through Chi-square
Now, we recovered the solution in the previous slice
The last equation is in matrix format

## Slide 8: Adding a Penalty in Chi-square
Let’s use the second derivative to penalty
The second derivative can be written as
, in this case

## Slide 9: Continue
The solution is thus
So, we have an additional term of applied to the original solution

## Slide 10: A in Matrix vs. Filter in Deconvolution
A in matrix format is multiplied to the original solution  effective a smearing function
Filter in deconvolution is effective a smearing function
Therefore, we can conclude that they are equivalent!
  Filter is equivalent to a penalty in the chi-square
  Filter is equivalent to a smearing function

## Slide 11: TPC Optimization
The measured signal inside TPC contains both signal and (electronic) noise
  Assuming deconvolution is correctly performed, we recover the signal completely
  Therefore, deconvolution of noise would become uncertainty of charge  smaller the better!
  The relevant factors are noise level and response functions
  Noise level  electronics, wire length …
  Response function  Gap between planes, E-field between planes
  This study does not require high-level reconstruction

## Slide 12: A new Challenge: Induced Charge in Adjacent Wires
V. Radeka Ann. Rev. Nucl. Part. Sci. 38, 217, 1988
v: velocity
Ew: weighting field
qm: charge
Bo Yu for MicroBooNE configuration

## Slide 13: Double Deconvolution
With induced signals, the signal is still linear sum of direct signal and induced signal
  R1 represents the induced signal from i+1th wire signal to ith wire
  Si and Si+1 are not directly related
The inversion of matrix R can again be done with deconvolution through 2-D FFT

## Slide 14
Different curves represent different positions for initial electron
Black  closest to the wire
Green  furthest from the wire
For induction plane, the signal size depends on the position  uncertainty in the charge as we used “average” response function
For collection plane, the signal arrival time depends on the position  uncertainty in the charge
Simulated by Yichen Li (BNL)

## Slide 15: About Wire Pitch
Bigger wire pitch  bigger signal
  With same electronics noise, the noise/signal will be smaller  good
Bigger wire pitch  bigger effect due to position-dependent field response  bigger spread of reconstructed signal  bad
Naively, we expect the signal has a form of
a: position-dependent field response,
b: electronics noise
Figure out a&b with detector parameters

## Slide 16: Angle of TPC
In a neutrino event, because of incident neutrino energy, the entire event is more boosted toward forward region
Due to nucleon response, the lepton tends to going more forward in the center-of-mass frame
TPC with wire readout has more trouble to reconstruct “tracks” which are parallel to the wire plane  charges arrive at various wire-plane at same time  ambiguity to figure out the proper correlation
http://www.phy.bnl.gov/wire-cell/ bee/set/4/event/2/

## Slide 17: Detector Angle
http://www.phy.bnl.gov/wire-cell/bee/set/7515fe16-d163-4df8-ad87-09f7c809dc7e/event/0/
Same events (rotate 0-19 degrees)
  Event 0  0 degrees
  Event 10  10 degrees
  Event 19  19 degrees

## Slide 18
0 degrees
10 degrees
One can click the web-site to look at events in 3D and rotate to get a better understanding.
10 degrees (truth)

## Slide 19
19 degrees
10 degrees
http://www.phy.bnl.gov/wire-cell/bee/set/6/event/8/
MC truth: one electron, one neutral pion, and one positve pion