## Slide 1: Passive Mitigation of Microphonics and LFD in LB and HB 650 Cavities
Timergali Khabiboulline
PIP-II Collaboration Meeting
9-10 November 2015

## Slide 2: Outline
Passive microphonics control
  LFD, reducing cavity frequency shift due to RF pressure
  Reducing sensitivity to bath pressure fluctuations, df/dP
  Cavity mechanical resonances
  Minimizing of acoustics from external forces
  Additional RF power for frequency detuning compensation
Active Microphonics control

## Slide 3: PIP-II requirements for SRF accelerating cavities
Section | Freq MHz | Maximal detune (peak Hz) | Minimal Half Bandwidth (Hz) | Max Required Power (kW)
HWR | 162.5 | 20 | 34 | 4.8
SSR1 | 325 | 20 | 45 | 5.3
SSR2 | 325 | 20 | 27 | 17.0
LB650 | 650 | 20 | 29 | 33.0
HB650 | 650 | 20 | 29 | 48.5
Bandwidth and required power optimized for 2 mA
Pulsed and CW operations
Low beam loading → narrow cavity bandwidth → microphonics
Lorentz Force Detuning (LFD) is an issue in a pulsed mode, and should be analyzed for each cavity type

## Slide 4: HB650 bare cavity LFD simulations
For 2 rings LFD~-0.275 Hz/(MV/m)2
for 1 ring LFD~-0.38 Hz/(MV/m)2.
Because the difference in LFD value for one and two rings options is not essential and the complexity of production of the cavity with two rings is high enough, we decided to use one ring option and redesign the end groups of original Helium vessel.
R1=87.5 mm, R2=120 mm.
R=110 mm.

## Slide 5: LFD for HB650 dressed cavity
Chart: LFD vs. Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
R=100 mm | -5.039 | -2.386 | -1.688 | -1.179 | -0.863 | -0.745 | -0.684 | -0.646
LFD for dressed cavity with R=100 mm stiffening rings

## Slide 6: HB650 dressed cavity df/dP optimizations
Chart: df/dP, Hz/mbar vs Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
0.92 Rend=Rreg=110 | -8.7 | 3.1 | 6.9 | 9.9 | 11.9 | 12.6 | 13 | 13.3
0.92 Rend=110 Rreg=120 | -12.9 | -4.9 | -0.8 | 3.3 | 6.7 | 8.1 | 8.9 | 9.4
Chart: Rreg, mm
| 110 | 115 | 120
 | 5.4 | 6.3 | 8
Stiffness of β=0.92 cavity kN/mm vs. Radius of the Regular stiffening ring
Chart: df/dP, Hz/mbar vs. Tuner Stiffness
| 0 | 10 | 50 | 100
Bellow 115mm | -9 | 6.9 | 12.2 | 13.3
Bellow 135mm | 41 | 22.9 | 16.8 | 15.7
Bellow 165mm | 180 | 50.9 | 24.5 | 22

## Slide 7: HB650 dressed cavity df/dP optimizations
df/dP for stiffening ring R = 90 mm vs. 100 mm
Bellows radius of OD=125 mm
Chart: df/dP vs. Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
R= 90 mm | 28.539 | 17.723 | 15.198 | 13.435 | 12.366 | 11.976 | 11.773 | 11.65
R=100 mm | 10.787 | 10.771 | 10.767 | 10.765 | 10.763 | 10.762 | 10.762 | 10.722

## Slide 8: HB650 cavity stiffness
R=100 mm, ΔL ~ 334 μm
Stiffness ~ 3.0 kN/mm
Cavity Stiffness vs stiffening ring diameter

## Slide 9: HB650 dressed cavity stress analysis
2 bar pressure + Gravity Load, RT, Tuner = 80 kN/mm
σ ~ 90.6 MPa
Maximum allowable Stress is 88.7MPa
σ ~ 76.4 MPa
R=2.5mm
t=300μm
R
t

## Slide 10: Mechanical resonances of HB650 dressed cavity

## Slide 11: Summary
LB650 dressed cavity design is in progress
HB650 dressed cavity optimization done
  Stiffening ring position R=100 mm and bellow radius R=125 mm accepted
  LFD Coefficients for tuner stiffness 80 kN/mm -0.69 Hz/(MV/m)^2
  dF/dP for tuner stiffness 20 - 80 kN/mm is less than 12 Hz/mbar.
  Cavity stiffness is ~ 3.0 kN/mm and tuning sensitivity is ~ 160 kHz/mm.
  Modal analysis has been done. Lowest longitudinal mode ~ 100 Hz with 20-80 kHz/mm tuner stiffness.
  Stresses analysis has been done for internal pressure of 2 bar + gravity load at RT
    Stresses in cavity are acceptable
    Stresses in bellow are allowable for 5 mm pitch