## Slide 1: Booster modification for 20 Hz operation
Kiyomi Seiya
PIP-II Collaboration Meeting
9-10 November 2011

## Slide 2: Outline
Resonance circuit modifications
Injection energy stabilization
Cogging

## Slide 3: Booster FDOODF lattice
Combined function magnets: F, D
FDOODF x 24 periods
Corrector packages at short and long
Corrector package (12 poles) includes
H & V dipoles, quad, skew quad, sextupole, skew sextupole
and H & V BPMs.
F Magnet
D Magnet
Corrector Package

## Slide 4: GMPS(Gradient Magnet Power Supply System)
PS1
PS2
PS3
PS4

## Slide 5: F Magnet and D Magnet on a Girder
F-Magnet
D-Magnet
Choke
Resonant Capacitor
F-Magnet
D-Magnet
Resonant Capacitor
Choke
Coil
Magnet pole
Current on Magnets
@ Injection  @ Extraction
103A 966 A
11/9/2015

## Slide 6: Loss measurements at 20 Hz
Frequency [Hz]
Losses [W]
Losses [W]
Losses @ 75 A (rms)
with Magnet, Cable and Capacitors
Losses @ 30 A (rms)
with Choke, Cable and Capacitors
0
10
20
30
40
50
Frequency [Hz]
0
5
10
15
20
25
30
V
I

## Slide 7: Requirement for 20 Hz operation on GMPS
Require about 3.9% more power.
Capacitor voltage will increase by about 32%
Resonant capacitor at each “Girder” must decrease from ~8.33 mF to 4.69 mF.
RMS current per µF will also increase as well.
Require same measurements at high current ~500A(rms)

## Slide 8: Injection field error on present operation
I_err ~ 0.04A
T_err_max ~ 40 msec
dR ~ 1.2mm
Current on Main dipole magnet
Orbit difference

## Slide 9: GMPS regulation
Reference
Magnet
Transductor
GO TO
4 PSs
DAC OUT
VXI card
NIM

## Slide 10: GMPS feedback
Vout = G * coeff * (Vave + Vpeak * cos(output_phase))
VXI card: I_MIN, I_MAX and period
NIM module: Set gain according to the operation time line
(Booster and MI are using same substation)
B
MI field
Booster Int.
Booster Loss

## Slide 11: Plan for GMPS regulation
I_err < +/- 0.02 [A], T_err < 20 msec
Both feedback on a new VXI board
15Hz operation
PIP-II 20Hz operation
~ 40 msec
~ 600 msec

## Slide 12: Notch and Cogging
Gap
for the extraction kicker
MI/RR revolution
1st Booster batch
2nd Booster batch
Time
h=588
h=84
Notch(extraction kicker gap) – Booster extraction kicker – MI/RR injection kicker
Main Injector / Recycler
81 bunches + 3 empty buckets

## Slide 13: Beam at injection and extraction without Cogging
Notch
Notch
 81 bunches + 3 empty buckets
Adiabatic capture with 37MHz RF
 84 bunches
Time
1 Booster revolution
Injection from LINAC @ 400MeV
1st Booster batch
2nd
Lost 3 bunches
every Booster
extraction.
at extraction
at MI/RR injection
Intensity
Beam loss at extraction
at injection

## Slide 14: Total bucket count during Booster cycle
Booster:
15 Hz resonant circuit
RF frequency: 37.7 – 52.8MHz
Total rf bucket count = const.
Total rf bucket count = const. -- Notch is at same position at extraction

## Slide 15: Cogging using 48 new dipole corrector magnets
Fixed with RPOS feedback
Changed by dipole corrector
Dipole corrector: 0.009[T-m] @ 24.4[A]
B field error ~1% can be compensated.
(Assuming 10[A] change )
Keeps beam on central orbit and save aperture.
Creates notch anytime after injection( even LINAC notch)
 reduce beam power loss by 40%.

## Slide 16: Block diagram of Cogging feedback
Integrated diff. bucket count has to be ‘0’ at the end of cycle.
BRF
Bdot
11 msec (MI/RR RF x 588)

## Slide 17: Field error and integration of difference of rf counts
Simulation
Measurement
B_main dipole field
Booster: 15Hz resonant circuit synchrotron synchronized to the 60Hz power line.
Number of MI/RR revolution

## Slide 18: Simulation for the feedback and measurements
Integrated error w/o feedback (simulation)
With feedback (simulation)
With feedback (MEASUREMENTS)

## Slide 19: Orbit changes during Cogging operation
Corrector current
Orbit difference
Corrector current : +/- 1A
Orbit change < 1mm
2A
+/- 10 mm

## Slide 20: Cogging at 20Hz
+/- 4mm
Required corrector current
for Cogging at 20 Hz operation: < 4A
Integrated error with feedback (simulation)
Measured orbit change
with 4A offset < +/- 1mm

## Slide 21: Summary
Resonance circuit modifications
 Estimated losses, power and required capacitors
 Need measurements at high current
Injection energy stabilization
 Developing new GMPS regulator for present 15 Hz operation
 It should work for 20Hz
Cogging
 Current system should work for 20Hz