## Slide 1: Low-b and High-b 650 MHz Cavity Cryomodules
Tom Nicol - Fermilab
PIP-II Collaboration Meeting
9-10 November 2015

## Slide 2: Linac map

## Slide 3: General cryomodule parameters

## Slide 4: Low-b cryomodule general requirements
General |  | 
 | Physical beam aperture, mm | 83
 | Overall length (flange-to-flange), m | 3.9
 | Overall width, m | ≤1.6
 | Beamline height from the floor, m | 1.3
 | Cryomodule height (from floor), m | ≤2.00
 | Ceiling height in the tunnel, m | 3.20
 | Max allowed heat load to 70 K, W | 100
 | Max allowed heat load to 5 K, W | 15
 | Max allowed heat load to 2 K, W | 100
 | Maximum number of lifetime thermal cycles | 50
 | Intermediate thermal shield temperature, K | 45-80
 | Thermal intercept temperatures, K | 5 and 45-80
 | Cryo-system pressure stability at 2 K (RMS), mbar | ~0.1
 | Environmental contribution to internal field | <0.1 mG
 | Transverse cavity alignment error, mm RMS | <0.5
 | Angular cavity alignment error, mrad RMS | ≤5
Cavities |  | 
 | Number, total per cryomodule | 3
 | Frequency, MHz | 650
 | b geometric | 0.61
 | Operating temperature, K | 2
 | Operating mode | CW and pulsed (0-100%)
 | Operating energy gain, MV/m | 17.7
 | Coupler power rating (TW, full reflection), kW | 120
Table from FRS
(subject to change)

## Slide 5: High-b cryomodule general requirements
General |  | 
 | Physical beam aperture, mm | 118
 | Overall length (flange-to-flange), m | 9.5
 | Overall width, m | ≤1.6
 | Beamline height from the floor, m | 1.3
 | Cryomodule height (from floor), m | ≤2.00
 | Ceiling height in the tunnel, m | 3.20
 | Max allowed heat load to 70 K, W | 300
 | Max allowed heat load to 5 K, W | 25
 | Max allowed heat load to 2 K, W | 220
 | Maximum number of lifetime thermal cycles | 50
 | Intermediate thermal shield temperature, K | 45-80
 | Thermal intercept temperatures, K | 5 and 45-80
 | Cryo system pressure stability at 2 K (RMS), mbar | ≤0.1
 | Environmental contribution to internal field | 10 mG
 | Transverse cavity alignment error, mm RMS | <0.5
 | Angular cavity alignment error, mrad RMS | ≤1
Cavities |  | 
 | Number, total per cryomodule | 6
 | Frequency, MHz | 650
 | b geometric | 0.92
 | Operating temperature, K | 2
 | Operating mode | Pulsed and CW
 | Operating energy gain, MV/m | 17.7
 | Maximum cavity heat load to 2 K, W (each) | 30
Table from FRS
(subject to change)

## Slide 6: Pressure system requirements
System | Warm MAWP (bar) | Cold MAWP (bar)
2 K, low pressure | 2 | 4
2 K, positive pressure piping | 20 | 20
5 K piping | 20 | 20
45-80 K piping | 20 | 20
Insulating vacuum | 1 atm external, vacuum inside | Na
Cavity vacuum | 2 bar external, vacuum inside | 4 bar external, vacuum inside
Beam pipe outside cavities, includes warm to cold transitions | 1 atm external, vacuum inside | 1 atm external, vacuum inside
Table from FRS
(subject to change)

## Slide 7: Cryomodule heat loads in CW

## Slide 8: Maximum allowed heat load per cryomodule

## Slide 9: SSR1 cryomodule (SSR2 will probably be similar)
First LB 650 cryomodule must connect to this end of the last SSR2

## Slide 10: Configuration options
XFEL, ILC, LCLS-II style
  Cavity string supported from gas helium return
Atlas, FRIB, etc.
  Cavity string support from top plate of rectangular vessel
SNS, ESS, etc.
  Cavity string supported using tension elements, with and without space frame
SPL
  Cavities supported by the input coupler
Superconducting magnet inspired supports, e.g. SSC or LHC

## Slide 11: Configurations – XFEL, ILC, LCLS-II

## Slide 12: Configurations – XFEL, ILC, LCLS-II

## Slide 13: Configurations – Atlas, FRIB, etc.

## Slide 14: Configurations – Atlas, FRIB, etc.

## Slide 15: Configurations – SNS, ESS, etc.

## Slide 16: Configurations – SNS, ESS, etc.

## Slide 17: Configurations – SNS, ESS, etc.

## Slide 18: Configurations – SPL

## Slide 19: Configurations – Superconducting magnet inspired

## Slide 20: Configurations – Superconducting magnet inspired

## Slide 21: Configurations – Superconducting magnet inspired

## Slide 22: Configurations – Superconducting magnet inspired

## Slide 23: Configurations – SSR1 cryomodule

## Slide 24: Configurations – Spoke test cryostat

## Slide 25: Configurations
Concept 1
  Vacuum vessel closed at both ends
  Room temperature strongback – cavities supported from bottom
  Strongback is inside the vacuum vessel, outside the thermal shield
  Support post(s) for each cavity
Concept 2
  Vacuum vessel closed at both ends
  Cavity support similar to XFEL – cavities hanging from return pipe
  Support posts attached to return pipe not cavities

## Slide 26: Low-b cryomodule configuration
11 total cryomodules
3 cavities each (650 MHz, 5-cell)
33 total cavities
No magnets internal to the cryomodule
Approximate length = 3.9 m

## Slide 27: High-b cryomodule configuration
4 total cryomodules
6 cavities each (650 MHz, 5-cell)
24 total cavities
No magnets internal to the cryomodule
Approximate length = 9.5 m

## Slide 28: Low and High-b cryomodule general configuration
Beam pipe
Bayonets connections,
cryogenic valves, etc.
Ports to access tuner
motors
Power couplers
Heat exchanger

## Slide 29: Concept 1
Strongback
Support post
Heat exchanger enclosure
Vacuum vessel extension for bayonets, cryo valves, etc.
Thermal shield

## Slide 30: Concept 1
650 Cavity with 2-phase pipe
Warm up cool
down pipe
He reservoir
with level sensor
4K circuit for intercepts
Thermal shield
Strong back with
supports
Illustration only – not representative of actual cavity string

## Slide 31: Concept 2
Coupler ports
Cold mass supports:
Fix
Sliding
Heat exchanger
Beam pipe
Illustration only – not representative of actual cavity string

## Slide 32: Concept 2
Heat exchanger
Vacuum vessel
He 2-phase pipe
Bayonets, cryo valves, etc.
300 mm pipe
650 MHz cavity
Thermal shield
Coupler port

## Slide 33: Concept 2
He reservoir with level sensor
Warm up cool down pipe
Illustration only – not representative of actual cavity string

## Slide 34: Cryomodule design concepts - Pros and cons
Concept 1 (room temperature strongback)
  Many design features common with the current SSR1 cryomodule design
  Coupler port locations are fixed with respect to the vacuum vessel
  Support system not subject to thermal distortions during cooldown
  To date, unproven
Concept 2 (XFEL-like design)
  Design concepts are direct descendants of the XFEL design
  Could possibly use tooling common to XFEL-like cryomodules
  Coupler positions change during cooldown
  Support pipe can distort during cooldown

## Slide 35: High-b cryomodule
Heat exchanger
Check valve
Gate valve
Tuner access ports

## Slide 36: High-b cryomodule
Strongback
Support posts
2-phase manifold

## Slide 37: High-b cryomodule

## Slide 38: Lab 2 renovation

## Slide 39: Summary and status
Four 5-cell b=0.9 cavities manufactured by AES are in-house, five more expected from PAVAC.
Low-b cavity design being developed at VECC.
High-b cavity design will be provided to RRCAT for manufacture.
Common tuner design being developed by engineers from RRCAT.
Input coupler for all 650 MHz cavities will be developed at Fermilab.
Low-b cryomodule design will be developed at VECC, hopefully with features common to high-b design.
High-b cryomodule design will be a joint effort between Fermilab and RRCAT.
Significant progress is being made on the high-b cryomodule design. The most urgent need is for assembly tooling that could be common for both SSR1 and 650 MHz cryomodules.
Current plan is to put four US-made b=0.9 cavities and two India-made b=0.92 cavities in the prototype high-b cryomodule.
Significant progress is being made in Lab 2 for cryomodule assembly.