## Slide 1: 3.9 GHz components design
Nikolay Solyak (from behalf of LCLS-II design team)
Dressed cavity Review, FNAL, Nov. 20, 2015
Speaker:

## Slide 2: Outline
3.9 GHz system functionality
Requirements (Elvin)
Cavity design
HOM heating issues and cables
Wakefields
Coupler design
BPM; Gat Valve; HOM absorber
Conclusion

## Slide 3: Overview, why?
Space charge effects limit the maximum obtainable charge density from the photocathode and thus the minimum bunch length.
300 pC bunch has a length of approximately 1 mm at the exit on the injector. Sinusoidal variation in the RF voltage over this distance leads to a correlated energy variation, or “chirp,” in the uncompressed bunch and, after bunch compression, to an asymmetric bunch profile
Applying a voltage at a harmonic ω1=3ω0 of the fundamental RF frequency ω0 results in an integrated voltage that is approximately linear over the bunch length, removing the curvature of the beam distribution in longitudinal phase space, and facilitating more efficient bunch compression and controlled bunch charge distribution
3.9 GHz cryomodules are installed just before the first bunch compressor BC1

## Slide 4: FLASH - ACC39 performance
4
ACC39 routinely operates at 18.9 to 19.7 MV/m
  Capable of operation at 22 MV/m
    - Limitation set by thermal interlocks – concern about compromising HOM’s on cavities 3 & 5 (trimmed 2-post style)
Amplitude stability ≤ 2x10-5 pulse-to-pulse
Phase stability ≤ 0.003° pulse-to-pulse

## Slide 5: 4.8
750
Comparison
3.9 GHz vs. 1.3 GHz:
Iris Aperture: 30mm vs. 70mm (ratio 2.34)
Ep/Eacc ; 2.26 vs. 2.0 (13% higher)
Hp/Eacc(mT/MV/m) 4.86 vs. 4.26 (14% higher)
R/Q (Ohm) 750 vs. 1000
BCS resistance ratio (f2) (9 times higher)
FLASH

## Slide 6
Field asymmetry and RF Analysis for 3.9GHz cavity
Upstream HOM Coupler
Downstream HOM Coupler
 | 106 Vx/Vz |  | 106 Vy/Vz | 
 | Direct | P/W | Direct | P/W
Upstream | -73.8 + 250i | - | -19.4 + 147i | -
Downstream | -609 – 25.9i | - | 25.1 + 136i | -
Full | -682 + 227i | -683 + 230i | 5.5 + 282i | 5.6 + 281i
3.9 GHz Accelerating Structure
Magnetic Fields
Transverse Electric Fields

## Slide 7
FLASH-like Cryomodule Layout:
XFEL/LCLS2 Cryomodule Layout:
3.9 GHz Cryomodule Options
1.3GHz like Cryomodule Layout:
ey
ex
Dex (%) ~ 6.0 %
Dey (%) ~ 24.0 %
 | 1.3GHz-like | XFEL
Δεx (%) | 6 .0 | 0.09
Δεy (%) | 24.4 | 0.15

## Slide 8
Wake development in the 3.9GHz cavity
Electric field snap-shot of 2mm rms bunch
Cubic mesh (σ/h = 6)
Wake potential convergence
Qext ~ 1e7
A.Lunin/T.Khabiboulline

## Slide 9
Wake Potentials in the 3.9GHz cavity
dx= 0mm; dy= 0mm
dx= 0mm; dy= 0mm
dx= 0mm; dy= 0mm
dx= 0mm; dy= 1mm

## Slide 10
Wake Loss and Kick Factors in the 3.9GHz cavity
Couplers wake Kick
Structure Kick, dx= 0mm, dy = 1mm
Conclusions
Transverse wake kicks produced by couplers in the 3.9GHz cavity is about 0.02 V/pC and weakly depends on a bunch length.
Couplers wake kick is comparable with kick produced by the structure itself for beam shifted by 0.1mm of axis.

## Slide 11: LCLS-II requirements: (PRD and FRD)
Two CMs; 8 cavity / each
Coupler orientation as per XFEL
Electropolishing instead of BCP
~150 W heat load/cryomodule (2K)
BPM at downstream end (1.3GHz type)
No magnet
Table 3. Tuning/stability requirements

## Slide 12: Cavity gradient and Q0 requirements (recent data from XFEL cavity production)
Recent XFEL production cavities (INFN-Zenon);
At 2K the all cavities have Qo in range ~(2-3)·109
No field slope up-to ~17 MV/m; Quench at 20-23 MV/m, VTS
No Q degradation after welding to HV
P.Perini, INFN
Risk: LCLS-II cavity (cw) requirements more stringent than XFEL (pulse) !!!
 Require Prototyping and Testing
Chart: 
| 2.1144564467938403 | 2.1847542151507953 | 2.1993784365288072 | 2.2227591205605215 | 2.2800495662949194 | 2.2862823061630215 | 2.3074993729621265 | 2.3291139240506324 | 2.4268003165391714 | 2.489851150202977 | 2.5129745971046158 | 2.5463603653473568 | 2.5648173961527734 | 2.5806451612903225 | 2.6062322946175636 | 2.6195899772209565 | 2.6436781609195399 | 2.6674398376340966 | 2.7291604865025212 | 2.7955028866605893 | 2.9677419354838706 | 3.0986864264061973 | 3.1539252656839216 | 3.2033426183844012 | 3.3022254127781765 | 3.3333333333333335 | 3.3798677443056575 | 3.4716981132075468 | 3.5127911416571207 | 3.6234738085860569 | 3.6726546906187623 | 3.7581699346405228 | 3.8032244729226949 | 3.8365304420350288 | 3.8884192730346574 | 4.1856232939035483 | 4.2553191489361701 | 4.3233082706766908 | 4.4465925567907201 | 4.6300956215400095
before 150C | 5602.9128 | 5279.183 | 5097.917 | 5142.0548 | 4053.9735 | 3599.4363 | 3545.7134 | 4516.4016 | 3881.7419 | 3290.3387 | 3299.4759 | 2775.2601 | 2469.4622 | 2216.0659 | 2275.4991 | 2203.7301 | 2419.166 | 2284.251 | 2072.9665 | 1900.4954 | 1219.5161 | 942.705 | 942.7047 | 776.8382 | 834.749 | 725.8391 | 719.8831 | 761.4148 | 588.0233 | 463.9871 | 405.3948 | 339.3732 | 388.172 | 358.8539 | 331.7895 | 209.4896 | 162.9363 | 145.743 | 120.4671 | 109.982
after 150C | 3869.2307 | 3869.2307 | 3807.2258 | 3093.3668 | 2855.4136 | 2743.3073 | 2549.0371 | 2424.1863 | 2320.0204 | 2113.6129 | 2037.4783 | 1940.9312 | 1797.0497 | 1654.3859 | 1381.2192 | 1131.2836 | 899.8842 | 797.2129 | 742.404 | 652.6629 | 562.9604 | 514.219 | 464.0023 | 398.04 | 378.1082 | 296.8642 | 314.2448 | 299.2054 | 276.2431 | 218.756 | 154.2655 | 120.8387 | 114.2158 | 109.9856 | 83.066 | 77.6369 | 70.2866 | 64.2078 | 54.9928 | 47.1367 | 42.8825

## Slide 13: Chimney Power Limit
Chart: Chimney diameter, mm
| 55 | 60 | 76.199999999999989 | 101.6
Scaling from ILC cav (HTS) | 25 | 29.7521 | 47.9871 | 85.3104
HZB (ILC) | 30
JLAB-12GeV upgrade cav | 54
LCLS2-1.3GHz;19MV/m; Q=2e10 | 19.37
LCLS2-3.9GHz;18MV/m; Q=2e9 | 25.8
LCLS2-3.9GHz; 16.5MV/m; Q=2e9 | 21.7285
LCLS2; 3.9GHz;13.4MV/m;Q2e9 | 14.3308
Cryoload at 2K
 | Nominal parameters | Max or Min | VTS/HTS param
Eacc (MV/m) | 13.4 | 16.5 | 18
Q0 | 2.e9 | 2.e9 | 2.e9
P/cav (W) | 17.4 | 21.7 | 25.9
LCLS2-1.3 GHz
LCLS2-3.9 GHz

## Slide 14: Cavity design issues and proposed modifications for LCLS-II CW operation
Cavity
HOM coupler
Main Power Coupler
Blade-Tuner with piezo (Y.Pischalnikov talk)

## Slide 15
Cavity drawings: LCLS-II vs. XFEL and FLASH
FNAL/FLASH
design
INFN
modification
(adopted for LCLS2 as a starting point)
Additional modifications are needed to meet LCLS2 reqs.

## Slide 16
INFN modified FNAL design of the cavity for XFEL project. Mostly modifications done to simplify/improve production (Zenon) and tuning. Drawings and 3D models are available (thanks INFN team)
CW operation in LCLS-II is more severe regime for the cavity. Some minor modifications are needed to reduce risks and eliminate tuning and heating problems.
Proposed modifications in cavity RF design.
Issue #1: Frequency of lowest dipole mode trapped in coupler end of the cavity is too close to operating mode frequency, 3.9 GHz. As a result the tuning of notch frequency is difficult and 3.9 GHz frequency power leak is significant.
    Solution: Move away frequency of this mode. Few options:
        Reduce radius of pullouts for main and HOM couplers.
        Reduce beam pipe and bellow diameter from 40 to 38mm.
Issue #2 : Overheating of the HOM antenna (quench ~20MV/m at cw/VTS)
  Solution: HOM F-part modification possibilities in order to reduce heating
    Reduce penetration to beam pipe
    Increase length of bump
LCLS-II 3.9 GHz cavity design

## Slide 17
Reduce beam pipe diameter from 40mm to 38mm.
FLASH: Lowest Dipole HOMs. Beam Pipe Ø 40 mm and Bellows Ø 42 mm.
F = 3.992 GHz, QE = 3.6e4
F = 4.047 GHz, QE = 8.0e4
LCLS2: Lowest Dipole HOMs. Beam Pipe Ø 38 mm and Bellows Ø 38 mm.
5mm
Ø38 mm
F = 4.092 GHz, QE = 2.7e4
F = 4.188 GHz, QE = 7.4e3
Lowest dipole mode frequency shifted by 100 MHz up away from operating mode frequency.
No modification of cavity cells.
Add small conical transition between beam pipe and end cell.
  A. Lunin/T.Khabiboulline

## Slide 18
Effect of pullouts radius change (main coupler).
In current design lowest mode are closer (min ~10-20 MHz vs. 100MHz in simul.)
The FPC pull out radius of 3mm shifts the nearest HOM by 25 MHz, changing the beam pipe aperture to 38 mm allows to detune the HOM by ~ 100 MHz up.
FLASH design
Coupler Pullouts R=3mm
Beam pipe Ø38mm
Ø40
R=6
lowest dipole modes

## Slide 19
Pbellow_Cu_RT = 2*ω*W/Qbellow_Cu = 2*6.28*3.9e9*1.57/3.3E12 ≈ 0.023 W
Conservative approach: Copper RRR = 15
RF Losses in the Bellow due to the Operating Mode Fringing Field
Pbellow_Cu_5K ≈ 0.006 W
Accelerating gradient: 15.5 MV/m
Stored energy: 1.57 J
Qbellow_Cu : 3.3e12
Copper at RT (σCu = 5.8e7 s/m)
80 mm
105 mm
Magnetic Field
Smaller for 38mm pipe

## Slide 20: Modification of HOM coupler
Reduce penetration of antenna inside HOM to reduce heating  F-part modification
Increase wall thickness on the top of HOM can to prevent cracks and vacuum leak
To modify length of HOM feedthrough
(choice of feedthrough design: Fermilab vs. XFEL)

## Slide 21
HOM F-part modification to reduce antenna heating
G = 3.2e8 
G = 1.74e9 
  Current design HOM antenna quenches at ~20 MV/m in VTS. Expected that quench limit will even lower in CW regime at HTS and CM.
RF power dissipation on HOM antenna reduced by factor of 5.4 after modification
  A. Lunin/khabiboulline
Reduce penetration to beam pipe. Increase length of bump in F-part
Current design
Modified design

## Slide 22
HOM can thickness increase from 1.0 mm to 1.3 mm.
  Thickness of hat is a concern. Was broken when h=1mm.
  XFEL design already has thickness of 1.15 mm  one prototype cavity has a leak. Proposal to have 1.3mm.
1.15mm

## Slide 23
Von Misses stresses distribution of HOM cup at yield level (non-linear analysis)
1.3 mm vs. 1.5 mm wall thickness
Knob pulled up by 0.1 mm
Wall=1.3 mm
Wall=1.5 mm
Conclusion: 1.3mm is acceptable thickness of can wall
/ T.Khabiboulline

## Slide 24: Notch filter tuning requirements
Tuning accuracy ±2MHz  P < 0.1 W
For 1.3 GHz HOM accuracy for notch filter frequency ~0.5MHz

## Slide 25: HOM feedthrough:
XFEL design (used for 1.3GHz and 3.9 GHz)
Antenna modified for 3.9GHz
FNAL design for 3.9 GHz (FLASH)
XFEL design: no resonances up to 3.5GHz, no data for 3.5-10GHz range (test under preparation)
FNAL design: good up to 10GHz (goal of design)
T.Khabiboulline design

## Slide 26: Analysis of HOM Spectrum in the 3.9GHz LCLS-II cavity
Matched TEM Impedance Boundary
Matched Dipole HOMs
Impedance Boundary
> 1000 modes in 4- 10 GHz frequency band
Recent HOM modeling in modified cavity
Modified cavities with random mechanical errors (± 0.1mm). Compare with INFN.
All cavities tuned to frequency and flatness (>90%)
Copper plated bellows in between cavities
Statistics: 10…20 cavities
A.Lunin/T.Khabiboulline

## Slide 27
HOMs Resonant Losses in the 3.9GHz LCLS-II cavity (run #1)

## Slide 28
HOMs Transverse Kick (1mm offset) in the 3.9GHz LCLS-II cavity (Ø38mm)

## Slide 29
3.9 GHz: Power removed by HOM coupler
A. Sukhanov
Simulation model includes copper plated bellows between cavities
HOM frequencies have random distribution ~ 1MHz rms
Max values of R/Q for each mode is used (vs. cavity to cavity distance)
QHOM < 106 for most dangerous modes
R/Q of monopole modes in cavity chain

## Slide 30: HOM antenna heating issues
Expected maximum power flux to HOM coupler up to 4W:
~0.5 W – leakage from operation mode
Part of this will be dissipated in cable (0.6dB/m) and will heat HOM antenna
Heat removal from feedthrough (2K) and from the cable intercepts (5K and 50K) is essential part of design.
Choice of cable and specs is part of current activity

## Slide 31
Wide cooling leads
(45mm x 2.5x10 mm2)
Narrow cooling leads
(45mm x 2.5x2.5 mm2)
Thermal simulation for HOM cable (TFlex401) Pantenna= 9uW (140mT with modified design, 63 mT with original design)
Cable is OK up to 9 W input power flow
(80°C cable limit).
zoom
M.Hasan/T.Khabiboulline

## Slide 32: Lead Intercepted Power (3.9 GHz)
Power Flow [W] | 2K | 5K | 50K | 300K
0 | 6.30 | 189.88 | 287.86 | -484.04
1 | 18.06 | 217.86 | 358.44 | -394.68
2 | 29.84 | 246.19 | 435.51 | -298.46
3 | 41.63 | 274.95 | 520.27 | -194.23
4 | 53.49 | 304.20 | 614.21 | -80.58
5 | 65.44 | 334.01 | 719.21 | 44.26
6 | 77.43 | 364.58 | 837.66 | 182.56
7 | 89.46 | 396.08 | 972.68 | 337.22
8 | 101.50 | 428.79 | 1128.35 | 512.10
9 | 113.61 | 462.98 | 1310.21 | 712.38
10 | 125.80 | 499.07 | 1525.91 | 945.19
Narrow Leads
Power Flow[W] | 2K [mW] | 5K [mW] | 50K [mW] | 300K [mw]
0 | 9.27 | 164.76 | 242.83 | -416.87
1 | 21.91 | 193.01 | 313.60 | -326.02
2 | 34.61 | 221.87 | 393.03 | -226.41
3 | 47.43 | 251.44 | 483.14 | -116.22
4 | 60.39 | 281.94 | 586.51 | 6.86
5 | 73.47 | 313.74 | 706.51 | 145.86
6 | 86.67 | 347.22 | 847.86 | 304.90
7 | 100.05 | 383.02 | 1017.10 | 489.75
8 | 113.67 | 422.00 | 1223.63 | 708.57
9 | 127.78 | 465.89 | 1481.52 | 973.22
10 | 142.70 | 517.64 | 1812.94 | 1301.92
Wide Leads

## Slide 33
Vendor | Times Microwave |  |  | Huber+Suhner |  |  |  | Gore Type 42
Cable Type | TFlex-401 | TFlex-401t | SFT-304 | 32022 | 32039 | SF229 | 3288LM (SF329) | Gore Type 42
Inner Cond OD [in] | 0.0641 | 0.062 | 0.062 | 0.0359 | 0.06 | ? | ? | 0.089
Outer Cond ID [in] | 0.208 | 0.185 | 0.185 | 0.106 | 0.191 | ? | ? | 0.196
Outer Cond OD [in] | 0.249 | 0.227 | 0.227 | 0.109 | 0.20 | ? | ? | 0.225
Cable OD [in] | 0.27 | 0.250 | 0.250 | 0.144 | 0.250 | 0.20 | 0.20 | 0.29
Material of Conductor | CuAg | CuAg | CuAg | CuAg | CuAg | CuAg | AlCuAg | CuAg
Dielectric | PTFE (εr=2.04) | ePTFE | ePTFE | Microporous PTFE | Extruded TFE | Low density PTFE | Microporous PTFE | ePTFE (εr=1.4)
Velocity % | 69.5 | 69.5 | 76 | 76.3 | 70.3 | 82 | 82 | 
Attenuation [dB/m] at 1 GHz | 0.26 | 0.22 | 0.22 | 17dB/100ft at 2GHz | 12dB/100ft at 2GHz | 0.18 | 0.18 | 0.3
Outer Braid | CuAg | CuAg | CuAg+ Polymide/Al+CuAg | CuAg+ Polymide/Al+SS | CuAg+ Polymide/Al+SS | Polymide/Al+CuAg | Polymide/Al+AlCuAg | CuAg+ Mechanical Shield
Jacket Material | FEP | TEFZEL 750 | FEP | FEP | FEP | FEP | ECTFE | TEFZEL
Temperature Rating [C] | -65 to +125 | -55 to +200 | -55 to +200 | -55 to +200 | -55 to +200 | -55 to +125 | -65 to +165 | -100 to 150
Shielding | >100 dB | >100 dB | >110 dB | >110 dB | >110 dB | >90 dB | >90 dB | >110 dB
Radiation Resistance [Rad] | 1e5 | 3e7 | 1e5 | 1e5 | 1e5 | 1e5 | 2e8 | 1e8
Material of Connectors | Brass | Brass | Brass | Brass | Brass | Brass | Brass | Be Cu
Price of 3m long assemblies(min is 250) | $147 | $175 | $157 | $146 | $192 | $266 | $341 | $756

## Slide 34
TFlex 401 cable after 500 MRad γ-radiation in Sandia (7 days)
Modification: FEPTefzel for outer conductor
New antenna design has better thermal performance
Preliminary analysis shows that the TFlex-401t/Huber-SF329 cable used for the 1.3GHz cryo-module will work for up to 8W power flow out of the HOM ports for the 3.9GHz cryo-module
Wide Leads are critically needed
Conclusion
Y.Pischalnikov/T.Khabiboulline/M.Hasan

## Slide 35: Proposed modification of 3.9 GHz power coupler for LCLS-II CW operation
Coupler was designed for pulse operation (P=50kW, DF=2%).
LCLS-II requirements: Pmax=2kW cw; quasi – TW regime:
    Without modification coupler inner conductor of warm part will be overheated up to ~1000 K.
Proposed modifications:
    Shorter antenna (QL~2.5e7 vs. 1.5e6)
    Increase thickness of copper plating in inner conductor from 30 microns to 150 microns
    Reduce length of 2 inner bellows in inner conductor from 20 convolutions to 10-15 convolutions.
    Increase thickness of ceramics in cold window to move parasitic mode away.
    Look alternatives

## Slide 36
Solid Model of Power Coupler of 3rd harmonic cavity
Fix coupling; Q=2.5e7 (2.9e7)
Cylindrical cold window (same as 1.3GHz)
Waveguide warm window

## Slide 37: Main Coupler Design
Input Coupler Modifications
Cold part (upper picture)
Dimensions of ceramic window
Length of antenna (cut at the last stage of production)
Warm outer part (middle in picture)
  No changes
In inner conductor of warm section (bottom picture)
  Cu plating increased from 30 to 150 um.
  Alternative solutions:
    reduce number convolution in both inner conductor bellows (15 vs 20)
    Replace SS tube to solid copper
Cold part
Warm part (outer conductor)
Warm part (inner conductor) and Waveguide with warm window

## Slide 38
Thermal simulations (COMSOL)
  FLASH/XFEL coupler with 20 convolution (inner) 30 µm Cu plating. Max. T ~658-1000 K
RF Power=2kW TW
I.Gonin

## Slide 39
SS Inner Conductor + bellows plating | T max, K | Losses, 80K | Losses, 4K
30 microns plating | ~1000 | 9.2 | 0.8
100 microns plating | 507 | 9.3 | 0.8
150 microns plating | 427 | 9.4 | 0.8
T=150K
T=10K
T=320K
SS inner conductor and bellows, all copper plated
Pin=2kW TW,
10μm on outer,
RRR=50; ASE,
10% roughness
ε=9.8, tan=3e-4,

## Slide 40
Alternatives: Copper inner conductor; SS bellows (30,50,100 um Cu plated)
Cu inner conductor + bellows plating | T max, K | Losses 50K | Losses 5K
30 µm | 591 | 7.75 | 0.8
50 µm | 461 | 7.65 | 0.8
60 µm | 403 | 7.7 | 0.8
100 µm | 346 | 8.0 | 0.8
Pin=2kW TW,
10μm on outer,
RRR=50; ASE,
10% roughness
ε=9.8, tan=3e-4,
Cu inner conductor + bellows plating | T max, K | Losses 50K | Losses 5K
30 µm | 591 | 2.08 | 0.465
50 µm | 461 | 2.4 | 0.47
100 µm | 346 | 3.45 | 0.485
Static losses ( boundaries: 10K/50K/320K)
Dynamic losses ( boundaries: 10K/150K/320K)

## Slide 41
150 μm 20 convolutions of SS bellow Cu plated
0.58mm
0.275mm
150 mm plating
Positive experience with 1.3GHz coupler at CPI
Concern: smaller size of bellow OD=12mm vs. 25mm (see picture)
 need prototyping and coupler tests (DV program)

## Slide 42
Main coupler antenna configuration
Beam Pipe Ø40 mm
 | Qext | Ant. depth [mm]
Original coupler, 40 mm | 2.5E7 | 11
Modified coupler, 38 mm | 2.5E7 | 9.5
11 mm
9.5 mm
  A. Lunin
Coupler tip length should be longer by 1.5 mm
Beam PipeØ38 mm
Beam Pipe Ø40 mm
Beam Pipe Ø38 mm

## Slide 43
Dipole mode
TE 110
Geometry
Monopole mode TM010
Computer simulations:
#1: ε = 10, F = 3.1062 GHz,
#2: ε = 10, F = 3.0860 GHz
Measurements:
#1: F1/F2Fav = 3.09956 / 3.10782 / 3.1037 GHz
#2: F1/F2Fav = 3.07873 / 3.086977 /3.0829 GHz
Computer simulations:
#1: ε= 10; F = 4.07725 GHz
#2: ε= 10; F = 4.02229 GHz
Measurements:
#1: F = 4.07875 GHz, Q = 2585
#2: F = 4.02507 GHz, Q = 2387
Sample #1:
ID = 35.03 mm; OD = 46.99 mm
L = 23.09 mm – 23.85 mm
ε ≈ 10.0; tanδ≈ 1.03E-3 (@4 GHz)
Cu tube: ID = 50.16 mm
Length ~ 600 mm
Sample #2:
ID = 35.00 mm; OD = 46.99 mm
L = 24.99 mm – 25.4 mm
ε ≈ 10.0; tanδ≈ 1.03E-3 (@4 GHz)
Measurements of WESGO ceramic samples (CPI)
S. Kazakov
Preliminary results
Measurements at 1.3 GHz ongoing
Cross-check with independent measurements

## Slide 44: BPM and HOM absorber
Concept: Use 1.3GHz beam line components (ID=78mm) in transition between cavity string:
BPM,
Spool piece,
Gate-valve,
Beamline HOM absorber
Optimize length and shape of transition from ø38mm to ø78mm for minimum wakefield.
Short ~25mm in flange (XFEL)
Long >300mm in spool-piece (upstream)

## Slide 45: Conclusion
General Design and Technology exist (based on XFEL/INFN)
To meet LCLS-II requirements cavity, coupler, HV, tuner designs should be modified to reduce risks and improve performance at cw operation.
Simulations and studies for the dressed cavity are done to prove proposed modifications and predict performance in LCLS-II cryostat.
Auxiliary components (Tuner, main coupler, magnetic shielding, feedthroughs,…) require more work and prototyping before major procurement starts.
Some work require for understanding 3.9GHz cryomodule (wakefields, HOM absorber performance, heating and heat removal issues/design, ….). All these questions will be addressed in the followings reviews.

## Slide 46
Thanks:
T.Khabiboulline, I.Gonin, A.Lunin, S.Kazakov, R.Stanek, C.Ginzburg, E.Harms, H.Edwards, C.Grimm, M.Foley, Y.Pischalnikov, T.Arkan, A.Rowe, A.Grassellino, G.Wu, O.Prokofiev, J.Ozelis, A.Saini, J.Kaluzny, S.Yakovlev, M.Hasan, T.Peterson, Y.Orlov, Y.He, E. Borissov, …

## Slide 47: Back-up slides

## Slide 48
Transverse deformations, for original (upper) and modified (lower) couplers
Longitudinal deformations, for original (upper) and modified (lower) couplers
Stresses, MPa/mm | 20 conv. | 10 conv.
Inner conductor, transverse | 26 | 45
Outer conductor, transverse | 44 | 44
Inner conductor, longitudinal | 150 | 290
Outer conductor, longitudinal | 96 | 96

## Slide 49: LCLS-II 3.9GHz Cryomodule, (F10014857 in Team Center)
XFEL cavity orientation (z-rotation:180 deg)
8 - 3.9GHz cavities
Power couplers from both sides
2-coldmass supports
Interconnection sliding bellow
38” OD vacuum vessel pipe
One thermo shields:50K
5K intercept

## Slide 50: LCLS-II. 3.9GHz Cavity String (F10014812)
3.9 cavity Style-A
3.9 cavity Style-B
Gate Valve
Blade tuner
Spool piece
Spool piece
and BPM