## Slide 1: Step IV Operational Proposal
S. Feher
FNAL
December 3rd, 2015

## Slide 2: Outline
Status of SS electrical circuits
Powering and Magnet circuit protection operational requirements
Recommended Magnet protection scheme and operation of the PSs
Conclusions

## Slide 3: Status of SS Electrical Circuit
SSD
Known Damage:
  LTS lead between the HTS lead and the M1 coil is open
  Internal diode pack connection is open for M1
  At one side of the M1 LTS lead is shorted to ground
  The two LTS leads for M1 are connected to each other; finite resistance
  M2 coil is connected to M1 coil therefore connected to ground with ~ 2 kΩ resistance
Possible future degradations:
  M2 ground connection becomes more solid; less resistance
  Leak occurs at M1/M2 feedthrough (between the cold mass and insulating vacuum)
SSU
Known Issues:
  Center Voltage tap of the ECE coils is open
  One of the voltage taps across the M2 coil is open

## Slide 4: Status of SSU Electrical Circuit
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
Cold Mass Shell
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
M1
M2

## Slide 5: Operational requirements
By design:
Powering
  Current measurement accuracy 2x10-4 (new transductors being installed)
  Fail safe powering; no harm to equipment (Magnet, leads, PS itself) and personnel
Magnet circuit protection
  Coils are self protected; if the coil quenches sufficient to turn off the PS
  HTS and LTS leads during quench: keep the hot spot temperature below 300 K
  Coils hot spot temperature during quench less then 80 K
  Magnet peak voltage relative to ground below 1600 V; for ECE circuit internal diode pack needed to fulfill this requirement
Practical reasons:
HV withstand to ground less than 150 V (cold HiPot value)
HTS lead voltage less than 3 mV (threshold value is at 1 mV)
LTS lead voltages during quench as low as possible (no clear understanding how it was built, what are the lead dimensions and/or cooling conditions; quench integral value limit is not known)

## Slide 6: Protection issues
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
Direct protection of LTSa and LTSb segments with V-taps;
LTSd is only protected with the magnet; low threshold settings required to lower the hot spot temperature
LTS/N easily can be overheated
Internal diode/resistor pack does not extract enough energy

## Slide 7: Proposed Operational Configuration
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
Carefully selected External diode pack, and R2
Contactor for the External diode pack is open; not to interfere with PS operation

## Slide 8: Different quench and failure scenarios
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
Magnet quench
HTS lead quench
LTSa or LTSb quench
LTSd quench
Ground fault
PS malfunction

## Slide 9: Magnet quench
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
Magnet quench is detected
  PS Contactors open for all circuits: M1 (for SSD M1 is floating), M2, ECE)
  External diode pack contactors close
  Diode Pack is sized to keep the internal diode pack closed (M1 and M2 ~ 5 V, for ECE ~ 10 V); current is circulated through the external diode pack
During magnet quench HTS or LTSa or LTSb quench occurs
  External diode pack contactor opens for the particular circuit
  R2 resistor is sized to keep the max voltage below 150 V in a case LTSc or LTS/N opens
Ground fault occur during quench
  No additional action – the maximum external voltage will be limited to 5 V

## Slide 10: HTS or LTSa or LTSb quenches
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
HTS or LTSa or LTSb quench is detected
  PS Contactors open for all circuits: M1 (for SSD M1 is floating), M2, ECE)
  External diode pack contactor remain open for the quenching circuit the rest of them will be closed – this requires major modifications of the QPS; more channels needed
  R2 resistor is sized to keep the max voltage below 150 V in case LTSc or LTS/N opens
During HTS or LTSa or LTSb quench the magnet also quenches
  No additional action – the current decay will be faster
Ground fault occur during quench
  No additional action – the maximum external voltage will be limited to 5 V

## Slide 11: LTSd quenches
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
LTSd quench is detected
  This quench can not be separated from a magnet quench – very low quench detection threshold is required; dI/dt based quench detection system for M1 & M2 and significantly lower threshold for the ECE half coil based detection system (more filtering) are needed
  PS Contactors open for all circuits: M1 (for SSD M1 is floating), M2, ECE)
  External diode pack contactor remain open for the quenching circuit the rest of them will be closed – R2 resistor is sized to keep the max voltage below 150 V in case LTSc or LTS/N opens
During LTSd quench the magnet also quenches
  No additional action – the current decay will be faster
Ground fault occur during quench
  No additional action – the maximum external voltage will be limited to 5 V

## Slide 12: Ground fault or PS malfunction
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
Ground fault or PS malefuntion
  PS Contactors open for all circuits: M1 (for SSD M1 is floating), M2, ECE)
  External diode pack contactors close
  Diode Pack is sized to keep the internal diode pack closed (M1 and M2 ~ 5 V, for ECE ~ 10 V); current is circulated through the external diode pack
During ground fault or PS malfunction HTS or LTSa or LTSb or LTSd quench occurs
  External diode pack contactor opens for the particular circuit
  R2 resistor is sized to keep the max voltage below 150 V in a case LTSc or LTS/N opens

## Slide 13: Conclusions
The proposed PS and QPS configuration will minimize the risk of loosing the magnet circuits
Requires major modifications of the QPS

## Slide 15: Proposed Operation Configuration
Cold Mass Shell
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs

## Slide 16: Status of SSU Electrical Circuit
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
Cold Mass Shell
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Vacuum Shell
Internal Diode
Pack
External Diode
Pack
PSU
Energy Absorber
HTS
HTS
LTSa
LTSa
LTSc
LTSb
LTSc
LTSb
LTSd
LTSd
LTS/N
LTS/N
R2
R1
R1
Feedthroughs
M1
M2