## Slide 1
Status of ICARUS
C. Montanari – CERN / INFN-PV

## Slide 2: Foreword
In 2013 ICARUS concluded a very successful, long duration run with the T600 detector at the LNGS underground laboratory taking data both with the CNGS neutrino beam and with cosmic rays. Several relevant physics and technical results were achieved.
It is mainly thanks to the continuing efforts of the ICARUS Collaboration and to the support of INFN, that the LAr TPC technology has been taken to full maturity. The T600, with about 500 ton of sensitive mass, is the largest LAr TPC ever constructed.
The T600 detector is now at CERN for a significant overhauling in view of the short baseline neutrino experiment on the FNAL Booster and NUMI beams. The experiment is expected to start data taking by end 2017.

## Slide 3: ICARUS-T600 detector at LNGS
Two identical modules (T300)
  3.6x3.9x19.6 = 275 m3 each
  Liquid Ar active mass: ~476 t
  Drift length = 1.5 m (1 ms)
  HV = -75 kV; E = 0.5 kV/cm
  drift velocity = 1.55 mm/μs
  Sampling time 0.4 μs (sub-mm resolution in drift direction)
4 wire chambers
  2 chambers per module
  3 “non-distructive” readout wire planes per chamber wires at 0, ±60° (ind1, ind2, coll view)
  ~ 54000 wires, 3 mm pitch and plane spacing
  Charge measurement on collection plane
20+54 8” PMTs for scintillation light detection
  VUV sensitive (128nm) with TPB wave shifter
LN2 vessels
readout electronics
T300
T300
cryogenics
(behind)
cathode
readout wire arrays
E
E
1.5m

## Slide 4: T600 overhauling activities in progress
  The following main activities are being developed to setup the ICARUS T600 detector for the SBN run at Fermilab:
    New PMTs system deployment;
    Cathode substitution/”planarization”;
    Detector re-cabling;
    New readout electronics;
    New cold vessels construction;
    New thermal insulation;
    Maintenance and partial replacement of cryogenics and purification systems;
    Construction of the Cosmic Rays Tagger.

## Slide 5: General schedule
NOW

## Slide 6: New PMTs system deployment
    The mechanical design of the new scintillation light collection system has been completed for the chosen configuration. All the components have been delivered to CERN.
    The PMTs are being produced by Hamamatsu. The 20 pre-series samples arrived at CERN at the end of September. All units have been tested and certified both at room temperature and in LAr.
    The first production batch of 80 PMTs has been delivered and is presently under test (room temperature and LAr). The second production batch of 100 PMTs is being delivered.
    Design of a second version of new bases has been completed. The full production has been ordered and a pre-series has been delivered.
    The setup for testing and pre-assembling of the PMTs is operational: two locations, B182 for cold tests and Ideasquare for warm tests and pre-assembly.
    The TPB evaporator is installed in B169. Evaporation protocol was established after several tests. Production is ongoing (4 evaporations/day).
    See G.L. Raselli presentation in the breakuot session for additional details.

## Slide 7: New PMTs system deployment and mechanics
90 PMTs per wires chamber – 360 PMTs in total

## Slide 8: Cathode substitution/”planarization”
    The intervention on the cathode panels of the first T300 module by personnel of the CERN Main Workshop was successful: the residual non-planarity is within few mm.
    The “flattening” operation was completed at the end of September. The panels were taken to an external company for cleaning and electro-polishing. All the pales have been re-installed in the first T300 module. Survey of the present planarity is ongoing.
Cathode panels after flattening and electro-polishing

## Slide 9: Detector re-cabling
The design of the decoupling boards is complete and the components selection for the biasing chain is also complete.
Prototypes have been installed in the TPC to check for mechanical interferences and to fix the details of the mechanical supports.
Pre-series have been delivered; a second batch was also produced and delivered.
New cables have been selected and tested in LAr. Order for the cables procurement and assembly was done. Production of the cable bundles is ongoing.
V1
V2
V3

## Slide 10: Detector re-cabling
Decoupling boards (pre-series)
First cables bundle

## Slide 11: The need for an electronics upgrade
ICARUS-T600 electronics consists of analogue boards (VME-like) with 32 low noise amplifiers, and a tree of 8 analog multiplexers, 4 10-bit ADCs, 2 digital multiplexers, resulting in a 2.5 MHz AD conversion (400ns sampling). Each analogue board is connected (serial link) to a digital VME module that provides storage, data compression, read-out through VME bus.
Limitations of ICARUS-T600 electronics is due to the technology available when electronics was first conceived (1998). Spare part are difficult to find.
Improvements concern:
  adoption of serial synchronous ADCs, one per channel;
  housing and integration of electronics on detector flanges;
  adoption of a modern serial bus architecture with optical links for faster transmission rate (Gbit/s) to sustain higher data rates.
The procurement of the new electronics (≈ 55000 channels) has been granted by INFN. For fiscal year 2016 INFN has granted 530k€. The total cost is about 1930k€.
The readout electronics for the PMTs is not yet fully defined, although it is budgeted within the existing CERN – INFN MoU.
See S. Centro presentation for details.

## Slide 12: New simplified analogue/digital integration
Block diagram of the classical old Icarus multiplexed ADC architecture, compared with the new parallel serial ADC feeding directly the digital part housed in a single high performance FPGA.
Present ICARUS Analogue board
Upgraded scheme integrating Analogue and Digital board into one single board

## Slide 13: The flange as electronics backplane
A new flange, that uses the same INFN proprietary design, used for T600, has been developed.
The connectors on the external side allow for direct insertion of 9 electronics boards where both analogue and digital electronics are housed.
The design will allow for reusing the original T600 cabling modularity and same number of signal feed-through.

## Slide 14: Some examples at FNAL (MC) – ev.150 (0.7GeV)
Old Ind: >~20 MIP wires
New Ind (filtered signal). Hits are resolved even very close to the vertex

## Slide 15: New cold vessels construction
  First extrusions produced and delivered to CERN for first tests on welding.
  Order for the panels pre-assemblies was sent out to the company, first delivery before end of 2015 (the roof pre-assemblies)
  Order for end-caps also done.
  The final assembly strategy has been defined; the required tools have been delivered.
  CERN Main Workshop is proceeding with the assembly of the stiffening frames. All the angular profiles of the stiffening frames have been delivered at CERN, as well as 10 “I” profiles.
  Welding procedures have been defined according to maximum quality (level B of Eurocodes).
  See M. Nessi presentation in the breakout session for additional details.

## Slide 16: New cold vessels

## Slide 17: Assembly Tool in B156

## Slide 18: New Thermal Insulation
Slide 18
Purely passive insulation chosen for the installation at CERN, coupled to our standard cooling shield with boiling Nitrogen.
Technique developed for 50 years and widely used for large industrial storage vessels and ships for liquefied natural gas.
Expected heat loss through the insulation:
T600 ≈ 6.6 kW
Preliminary design done by GTT in Jan 2013
No internal membrane is required for our case

## Slide 19: Cryogenics and purification systems
    Maintenance of cryogenic pumps and valves from the Gran Sasso installation was started.
    Tests of the new cold shield have been done. Measurements confirm the numerical model. A complete report is being elaborated.
    Tests of the new copper filters are under way at B182 with the 50 liters prototype. First results, with purification in the gas phase, show that the purity limit is compatible with our needs (> 10 ms, above the sensitivity of the 50 lt chamber). Results on the adsorption capacity are somehow contradictory. Further tests are ongoing. Tests of purification in the liquid phase are being prepared in collaboration with WA105 Collaboration.

## Slide 20: T600 Warm Vessel
Preliminary design is complete
Procurement and production in 2016

## Slide 21: Far Detector Building at FNAL – July 24, 2015
Dear Carlo and Sandro,
On Wednesday July 22nd, Fermilab issued the formal notice to the construction contractor for the SBN far detector building that they may begin work on the project. We expect that the contractor will start on site within the next couple of weeks.
Included in the notice are the construction milestones agreed to by Fermilab and the contractor. Below is a summary of some key dates. As you can see we are on target for being ready for the T600 installation start.
We will make sure to keep you informed regularly as the construction proceeds.
Regards, Peter
SBN Far Detetor Building Milestones
0 Calendar Days - Notice to Proceed Issued (22JUL15)
183 Calendar Days – Concrete Work Complete (21JAN16)
319 Calendar Days – Building Envelope Work Complete (05JUN16)
440 Calendar Days – Substantial Completion (04OCT16)
-----
Peter Wilson - Short Baseline Neutrino Program

## Slide 22: Understanding the Cosmic Rays induced backgrounds
  The planned activities at FNAL to settle the LSND / MiniBooNE / reactors hints for the possible existence of a new sterile neutrino pose several challenges.
  The unambiguous identification of CC electron neutrino events to within the overwhelming background from cosmic rays, neutral currents and CC muon neutrinos is a must for the successful completion of such an ambitious program.
  Although the superior characteristics of the LAr TPC technology allow us to identify and reject most of the backgrounds, we are all well aware that additional tools are needed to cope with the ones coming from cosmic rays.
  The intrinsic complexity of the cosmic rays induced events, makes Montecarlo estimates largely uncertain.

## Slide 23: Understanding the Cosmic Rays induced backgrounds
  A direct measurement of cosmic rays induced background before the start of operation on the Booster neutrino beam, in our view, can and must be done in order to assess:
    the correct thickness of the overburden;
    the correct performance of the Cosmic Rays Tagger;
    the validity of the reconstruction and event selection algorithms.
  This measurement can be performed, at CERN, using already existing cryogenic and purification equipment. The existing equipment has to be complemented with a TPC (≈10 m3 active volume), an adequate shielding using existing concrete blocks and and Cosmic Rays Tagger.
  The direct availability of data from other detectors like MicroBooNE, MiniBooNE, ... is also crucial for a correct comparison of data and Montecarlos.

## Slide 24: Former WArP Cryostat
Internal vessel diameter | 2900 mm
External vessel diameter | 3200 mm
Max ext vessel diameter | 3440 mm
Internal vessel thickness | 6/7 mm
External vessel thickness | 6/10 mm
Max internal height | 4996 mm
Max external height | 5090 mm
Cylindrical useful part height | 3755 mm
Cooling worm-pipe diameter | 22x1.5 mm
LAr recirculation flange from cap flange 170 mm dim. | 2630 mm
Internal vessel volume | 29 m3
Vacuum insulation volume | 6 m3
Cryostat mass (empty) | 8800 kg
LAr level from cap flange | 500 mm
Max LAr level from bottom | 3693 mm
LAr volume | 22.8 m3
LAr mass | 32000 kg

## Slide 25: Former WArP Cryostat
Internal vessel diameter | 2900 mm
External vessel diameter | 3200 mm
Max ext vessel diameter | 3440 mm
Internal vessel thickness | 6/7 mm
External vessel thickness | 6/10 mm
Max internal height | 4996 mm
Max external height | 5090 mm
Cylindrical useful part height | 3755 mm
Cooling worm-pipe diameter | 22x1.5 mm
LAr recirculation flange from cap flange 170 mm dim. | 2630 mm
Internal vessel volume | 29 m3
Vacuum insulation volume | 6 m3
Cryostat mass (empty) | 8800 kg
LAr level from cap flange | 500 mm
Max LAr level from bottom | 3693 mm
LAr volume | 22.8 m3
LAr mass | 32000 kg

## Slide 26: Cosmic Rays Tagger – Conceptual design
Largest possible coverage (> 98%)
Timing to recognize particles coming from outside the detector from those coming from the inside.
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Total surface
≈ 1250 m2
Access to the detector
Scintillator + WLF fiber + SiPMs
Two configurations considered
  X-T – single layer
  X-Y double layer
Physics performance vs. cost
More details in breakout session

## Slide 27: Conclusions
    The overhauling of the T600 is proceeding according to schedule and in line with the budget, with the only exception of the Cosmic Rays Tagger.
    The first T300 module will be ready in the first months of 2016. The second one will take advantage of all the preparatory work of the first one and will require only six months to be completed. Both modules will be ready for transport in second half 2016.
    Aim of the Collaboration is to start data taking with the BNB during 2017.
    Preparation for installation and run at FNAL requires some actions:
      Formal agreements between INFN and FNAL and between CERN and FNAL;
      Exact definition of the onsite work to be done by the Collaboration prior to transportation;
      Identification of the missing resources.
      The active involvement of US teams is essential.

## Slide 28
Schedules and future activities
28
ICARUS Referee Meeting, September 15, 2015

## Slide 29: First Cold Vessel
NOW

## Slide 30: Second Cold Vessel
NOW

## Slide 31: First TPC
NOW

## Slide 32: Second TPC
NOW

## Slide 33: Cryogenics
NOW

## Slide 34: Warm Vessel
NOW

## Slide 35: Cosmic Tagger
NOW

## Slide 36: Transport to FNAL
NOW

## Slide 37: Assembly at FNAL & Commissioning
NOW

## Slide 38: All in One
NOW

## Slide 39
BACKUP SLIDES

## Slide 40: PMTs mechanics
Shielding grid
Basic Unit
(36 / T300 module)

## Slide 41: PMTs mechanics
Shielding grid

## Slide 42: Preparation of the dark room for PMT testing (I)
Dark room
Electronics Lab
Dark room
Electronics Lab
Ideasquare Lab
Test Area
Control Area

## Slide 43: Preparation of the dark room for PMT testing (II)
Equipped for simultaneous testing of 16 PMTs
items | status
Furniture | Installed
Cabling | Installed
Feedthroughs electronics lab to dark room | Installed
Access and environmental monitoring | Being implemented

## Slide 44: TPB Evaporation – B169
The evaporator is installed in B169.
Protocols for PMTs cleaning and evaporation have been established after several tests.
Production is ongoing.

## Slide 45: New cold vessels construction – Materials I

## Slide 46: New cold vessels construction – Materials II

## Slide 47: U-frames Assembly tooling
Design of a specific tooling
  To ensure an appropriate positioning and clamping of the parts in order to achieve the thigh tolerances required
  To allow the welding in flat position which is mandatory to achieve the quality level required
Delivered: end October

## Slide 48: U-frames - Assembly tooling Assembled and aligned in B156

## Slide 49: Assembly strategy - 1

## Slide 50: Assembly strategy - 2

## Slide 51: Assembly strategy - 3
Start from the roof
Vessel assembled “on a side”
As many final welds during installation as possible.
Rotation of the whole vessel, in the end, to complete welding.
1
2

## Slide 52: Assembly strategy – Tool for cold vessels rotation

## Slide 53: Test of copper-based filter

## Slide 54
Drawing to be replaced with the new design by D. Smargianaki and D. Warner

## Slide 58: Installation area
Second T300 module in transport vessel.
Clean room with first T300 module
First cold vessel assembled in B156. Second cold vessel assembled in B185. This allows to recover about 2 months in the construction procedure.

## Slide 59: T600 Warm Vessel and Cryogenics envelope
Longitudinal view
Warm Vessel
Cryo
and purification
Drawing to be replaced with the new design by D. Smargianaki

## Slide 60: T600 Warm Vessel and Cryogenics envelope
Detector supports (I beams)
Drawing to be replaced with the new design by D. Smargianaki

## Slide 61: Existing cryogenic plant
Main purifier
GAr Fiters
GAr re-condenser
LAr recirculation pump

## Slide 62: Existing cryogenic plant (Top part)

## Slide 63: Detector conceptual layout
Wire Chambers (3 planes 0, ± 60°)
Central cathode plane
Cryogenic 3” PMTs (existing)
≈2m
≈1 m drift
≈1 m drift
3.2 m
≈ 10 m3 active volume

## Slide 64: New T600 layout
Warm vessel cage
External skin
Insulation panels
T600 modules

## Slide 65: New T600 layout
Insulation top
Top flanges (final layout)

## Slide 66
Cosmic Rays Tagger – US contribution
See Bob Wilson presentation in the breakout session for additional details