## Slide 1
Discussion slides
Dual-Phase ProtoDune
26/2/2016

## Slide 2
Offline (downstream the online computing farm) and computing model:
MC production and code management actually centralized at CCIN2P3 in Lyon
Massive MC production expected at CCIN2P3 and possible other centers
6x6x6 data production at CERN and Fermilab
Software based on QSCAN (simulation/reconstruction); fast execution and easily adaptable for detector performance analysis, online monitoring and analysis :
Framework dealing with all the aspects of the detector simulation and reconstruction going from: geometry description, interface to MC transport codes like Geant3 and 4 via VMC, events generators like Genie, detector response and electronics simulation for both single and dual-phase, simulated and real events reconstruction and event display. Interface to the raw and simulated data formats for various detector setups going from several R&D prototypes to WA105 3x1x1 and 6x6x6 and the 20 and 50 kton detectors considered in the LAGUNA-LBNO design study. Allowing to understand the performance of the detectors under construction like the 3x1X1 and 6x6x6 by also comparing to the result obtained in the last 10 years with different prototypes.
3x1x1 simulation analysis and monitoring with QSCAN (September 2016)
Developing QSCAN for 6x6x6; needed for detector optimization analysis and online analysis/monitoring

## Slide 3
WA105 TDR: 175 M triggers, to be refined once the beam simulation will be available
If totally stored in non-zero-skipped, lossless compression format
(assuming Huffman, factor 10 compression: 15MB/event)  2.4 PB
(+ cosmic runs and technical tests)
Following discussions we had with the IT people at CERN this total data volume of 2.4 PB does not present any technical problem on the CERN and Fermilab storage facilities scale
Requested link from online-storage to CERN computing division at 20 Gbps, compatible with 100 Hz non-zero-skipped, Huffman compressed (factor 10) data flow
Existing fast link between CERN and FNAL
Total data volume