## Slide 1
ESS Target Cryogenic System Cryogenic Operations Workshop
Fermilab
John Jurns (ESS) Lead Engineer TMCP
Philipp Arnold (ESS) Cryogenics Section Head
Jesper Ringnér (ESS) Lead Engineer CMS
Yannick Beßler (FZJ) In-kind Project Leader
Marcel Klaus (TUD) CMS Design Engineer
26 October 2016

## Slide 2: Target cryogenic system collaboration
European Spallation Source
Participants –
Host countries Sweden and Denmark
17 other European countries contributing
Target cryogenic systems contributed by in-kind partners from Germany

## Slide 3: Neutron production at ESS

## Slide 4: ESS Target Cryogenic Systems Overview
Pure Helium
Gas Storage 1
Standalone Helium Purifier
Helium Recovery System
Pure Helium
Gas Storage 2
Accelerator
Cryoplant
Test & Instrument Cryoplant
5 m3
LHe Tank
Target Moderator
Cryoplant
LHe Mobile Dewars
Test Stand Cryodistribution System
Instruments & Experiments
LN2 Storage Tanks
LN2 Mobile Dewars
Cryodistribution System for Elliptical Linac
Elliptical
Cryomodules
Test Stand Lund 2
Target Cryodistribution System
Hydrogen Circulation Box
Hydrogen Moderator
Cryodistribution System for
Spoke Linac
Spoke
Cryomodules
20 m3 LHe Tank
  Target Moderator Cryoplant (TMCP) – Provides cooling to the H2/He heat exchanger to remove heat from the hydrogen circuit. He circuit operates at approximately 15 K and 2.1 MPa.
  Cryogenic Moderator System (CMS) – Cryogenic hydrogen system that circulates sub cooled liquid hydrogen to cold moderators, and removes heat through a heat exchanger to a cold helium circuit
  Cold Moderators – Cryogenic hydrogen moderators use sub cooled liquid hydrogen at 17 K and 1.1 MPa to reduce the energy of the neutrons
Cryogenic
Transfer
Line

## Slide 5: Comparison to other neutron spallation sources
 | J-Parc | SNS | ESS
He cryoplant capacity | 6.45 kW @ 16.5K | 7.5 kW @ 16.5K | 30.3 kW @ 15K
H2 mass flow rate | ~ 180 g/s | ~ 150 g/s | ~ 1000 g/s
He mass flow rate | 307 g/s | ~ 275 g/s | 1125 g/s
Number of expansion turbines | 1 | 1 | 2(2)
Number H2 circulators(1) | 2 (parallel) | 3 (parallel) | 2 (series)
SNS hydrogen has separate circulation loop for each moderator, ESS & J-Parc have a single hydrogen circulation loop to the moderators
ESS TMCP has 3rd bypass turbine at 90K level. ESS specified 2 parallel cold end turbines to provide redundancy and turn-down capacity

## Slide 6
6
CMS
Moderator Reflector
He transfer lines
H2 transfer lines
Cold box
Compressors
TMCP
Integrated TMCP/CMS/MR system
Buffer
tanks

## Slide 7
ESS
moderator
& reflector
system
design
LH2 Transfer Lines
LH2 Cryostat
Moderator & Reflector Plug
Rotation Unit
Spallation Target
Proton beam

## Slide 8
Thermal moderator (water)
Cold Butterfly moderator (LH2)
ESS moderator & reflector unit design
Be-Reflector/
-vessel
LH2 pipework
Vacuum chamber (extruded profile include 2 cooling chambers for thermal moderator water

## Slide 9
ESS cold Moderator performance
Source: ESS neutronic group
Butterfly cold moderator provides significant increase in neutron brightness compared to ESS TDR design
ESS TDR design
2013
Current Butterfly design
2015

## Slide 10: CMS Specification
Main task for the Cryogenic Moderator System.
The Target Station shall use para-H2 material as cold moderator coolant such that the neutronic performance will sustain the required brightness while the technical risk will be residual thanks to the available experience using this material.
Expected Heat load neutronic: 19.0kW incl. Contingency margin
Expected Heat load static: 9.8kW
Hydrogen content in system: 22kg liquid hydrogen
Working Temperature: 17-20.5K
Working pressure: 1.1MPa
Design pressure: 1.7MPa
Pressure drop: ~0.2MPa
Expected mass flow: 1000 g/s
Ortho-Para catalyst: Oxisorb placed in a by-pass line
O-P ratio: >99.5%
In line measurement: Raman spectroscopy ahead and after moderator
Pressure control: Active buffer, expansion vessel.

## Slide 11: CMS Schematic

## Slide 12: CMS Overview
Cryostat
Weight 3700kg
Ø: 1800mm
H: 2000mm
Pipes and components insulated with MLI
H2 Pump
O-P Catalyst
Heat exchanger 1
H2 Pump
Heat exchanger 2
Buffer
He return
He supply
H2 supply
H2 return

## Slide 13: CMS Overview, buffer vessel
Small mean temperature variations can cause severe pressure fluctuations
H2 at < 20 K almost incompressible
H2 at > 35 K becomes compressible
-> buffer mitigates pressure variations
Pressure Control System – Buffer Vessel
A vertical buffer vessel with an axial temperature and density gradient will store/release hydrogen mass of the main loop in case of beam increase/decrease.

## Slide 14: CMS Overview, heat exchanger 1 & 2
Helium Outlet
Helium Inlet
Hydrogen Inlet
Hydrogen Outlet
Housing
Copper Spiral
Heat exchanger 1:
Aluminum plate fin exchanger
Used to liquefy the hydrogen during fill and maintain temperature during operation
Heat exchanger 2:
Fin tube exchanger
To liquify GH2 from buffer and main fill line during operation.

## Slide 15: CMS Overview, hydrogen pumps
Equipment spec pumps | 
Flow rate | Qmax: 1000g/s @17K
Working Temperature media | 17-300K
Working pressure | 1.1MPa
Set up | Serial connection, Both pumps at full flow, shared pressure drop
Fail mode | 1 pump, 100% flow
Pressure drop estimated | ΔP: 0.1/0.2MPa
Media | Gaseous, supercritical and liquid H₂
Control | Frequency Controlled motor
Hydrogen Pumps
Serial setup with 2 pumps
Each pump provides full mass flow but shares the pressure drop
If one pump fails the second pump will step up and compensate for the full pressure drop.

## Slide 16: CMS Overview connections to moderator plug
Jumper connections with bayonet couplings inside the monolith.
Vent line for hydrogen
Connected to safety relief valves and manual release valves
Purged with He/N2
Manifold includes valves, instruments and raman probes.

## Slide 17: TMCP Design Drivers
Unique attributes of the TMCP
High maximum heat load: 30 kW at 15 K
Wide range of dynamic heat loads: 5-30 kW
6 years from 1st protons on target to full power operation
Multiple operating modes
  Steady state – 15-100% of capacity
  Transient – Cool down and warm up
  Switching – Short term fast changes
CMS requires narrow temperature range: 17-21 K
High heat load and narrow temperature range means high helium mass flow rate
Long cryogenic transfer lines results in high helium inventory - ˜490 kg total

## Slide 18: TMCP Design Drivers
Closed loop modified Brayton cycle
1
2
3
Narrow operating range for LH2
H2/He heat exchanger
Helium
18.8 K Average
3.5 K max delta T
20.5 K
17 K
20 K
15 K
Hydrogen
5 K max delta T
Large variation in heat load

## Slide 19: TMCP Process Design Description
300 K
60-90 K
24 K
20 K
15K
90-220 K
Helium buffers with “low” and “high” pressure region
2 screw compressors
Turbine for HXs
Intermediate “heating” of feed flow upstream turbines
2 expansion turbines
Multi-purpose ambient heater

## Slide 20: TMCP Process Design Description
Operating modes
Nominal design
Low Power
Beam trip
Temperature
Entropy
expansion
CMS heat
compression
21.5 bar
313 K
1.1 kg/s
21.2 bar
15 K
20.6 bar
20 K
5.4 bar
14 K
5.2 bar
309 K
0.1 kg/s
T-S diagram, nominal design

## Slide 21: Highlights
Butterfly design successfully modeled, manufacturing process proven
Butterfly design promises significant improvement in neutron brightness
CMS Critical Design Review passed, detailed design on-going
CMS buffer unique robust design, proof of concept testing planned
CMS long lead items (pumps, heat exchanger) procurement cycle started
TMCP contract award made to Linde Kryotechnik May 2016
TMCP Preliminary Design Review held with LKT September 2016
Project on schedule
  TMCP commissioning complete 4Q18
  CMS installation complete 1Q19
  Integrated testing 1-2Q19

## Slide 22: ESS Target Cryogenic Systems
Finis