## Slide 1: SENSE Kick-Off Meeting

## Slide 2: What Problem(s) are We Solving
Multi-domain network service automation
  Mix of manual provisioning and automation today
  No service consistency across domains
  No service visibility across domains
  Expression and application of individual domain policies
  Narrower focus: Science DMZ to Science DMZ
Ability for science workflows to drive service provisioning
  Networks don’t provide application consumable interfaces
  Programming APIs usually not intuitive and require detailed network knowledge, some not pre-known
  Three science application use-cases

## Slide 3: What Problem(s) are We Solving
Multi-domain information exchange for service provisioning and troubleshooting
  Data APIs across domains for applications, users, network administrators
  Performance, service statistics, topology, capability etc.
  Exchange of ‘scoped’ and authorized information
Aligned with security policies @ the end-site

## Slide 4: Core idea
End-to-end, multi-domain provisioning automation and resource orchestration

## Slide 5: SENSE scoped definitions
End-to-End (network point of view)
  DTN NIC to DTN NIC, across Science DMZ, WAN(s), Open exchange points (ideally)
Multi-domain
  Multiple administrative domains, independent policies and AUP
  Different users?
Provisioning automation
  Bring-up and management of services without interrupt-driven human involvement
  Does not have any implications on duration of service
Resource orchestration
  Allocation and reservation of resources including compute, storage and network
  Network resources may include bandwidth, path, VLAN, QoS etc.

## Slide 6: Current State of SDN - Gaps
Inter-domain SDN undefined, and not focus of open-source or commercial efforts
  No organized R&E efforts either, though on many roadmaps
Describing resources are not done in a standard, consistent manner
  Minimal ethernet topology discovery by controllers, represented in proprietary JSON formats
Multi-domain admission control and Authz
  No clear way to specify AA, policies, and enforce them across domains
A ‘usable’ multi-domain testbed

## Slide 7: SENSE SDN Control Plane Architecture for End-to-End Orchestration
Defines Service Perimeter/Boundary
Orchestrator Role
Resource Manager Role

## Slide 8: SENSE Requirements for an SDN OS
Communication and coordination between the control planes at different sites, as well as the wide area network(s) connecting them.
Security mechanisms to protect the integrity and availability of network, compute, and storage resources. These mechanisms need to protect against both accidental and deliberate forms of misbehavior.
Abstractions of resource state and metadata that may have different representations (or, to a certain extent, different data models) across the various domains.
An easy way of expressing local resource control policies and running them within the network.

## Slide 9: SENSE OS (SENOS) Architecture
Resource Topology Service
API
Resource Computation Service
API
Policy Service
API
Monitoring Service
API
NE Driver (OpenFlow)
Service
API
SENOS Intelligent Service Functions
SENOS Core Functions
Multi-Point VPN Service
Intent API
Persistent State
SSHD
Python
Messages
Roles
Users
Resources
ACL
Thread
Generic API
System Services
ScienceDMZ Driver
Service
API
Big Science Service
Intent API
User Services (Application Containers)
Separation of kernel (privileged) and multi-user (unprivileged) execution space
Supports the concept of resources and allows the owners of resources to specify how those resources may be used, via access control lists.
A set of generic object definitions for commonly-used objects in SDN programs, such as network nodes, ports, and links.
An inter-process message-passing facility for communication between SENOS instances.
Service functions provide the intelligence to interpret or render a user’s intent, enforce policies, and coordinate workflows.
Service functions are hierarchical in nature, with atomic services being a discrete set of services that can be composed to build a more complex, custom service.
Core
Functions
Service
Functions

## Slide 10: SENOS Intelligent Service Functions (1/2)
Resource Information Service (RIS)
  Harvest and normalizes resource topology
  Enforces policy views of topology
Resource Computation Service (RCS)
  Multi-Constrain Multi Resource computation (from RAINS)
  Add support for SENSE requirements
    Next-Generation Science DMZ and site resources
    Flow management, flow termination, and site services integration functions
    Interaction with SENOS Policy Service

## Slide 11: SENOS Intelligent Service Functions (2/2)
Intent and Rendering
  Intent APIs expose very high-level service abstractions that focuses on the ‘what’ the application wants to accomplish and not on the ‘how’
  Renderer implements the business logic for the service
    Authorization
    Policy enforcement
    Computation to determine a next set of tasks
    Creation of subordinate (lower-layer) intents, if any
    Directly performing a set of actions
    Returning request status
  Multi-Point VPN Service will be the first network service prototyped for the SENSE project

## Slide 12: End-Site Orchestration
Two main ideas
  Flow management @ Science DMZ
  DTN Autoconfig
Flow management
  Route to right flows to the right DTNs, vlan or mor granular flow identification using OF
  Support multi-science Science DMZ, with resource allocation and traffic steering
  Allow addition of NFV services like Caching, and flow service chaining

## Slide 13: End-Site Orchestration (contd.)
DTN Autoconfig
  Systems configuration to ensure data transfer application can connect @ Layer 3 and/or Layer 2
    Includes, VLAN configuration on the NIC
    Private or public IP address configuration of L2 or L3 VPNs
    Other configuration like TCP window size, might be a stretch
  Creating VMs or containers with right data-movement software for multi-science DTNs
More ideas?
  OVS configuration and QoS configuration
  Flow steering and ACLs to connect to the internal file system over different NICs

## Slide 14: WAN / Regional / Exchange Network Orchestration
Leverage past experience with dynamic point-to-point circuit services to develop multi-point offering
Network Element (NE) Control
  SENOS NE Driver for southbound communication (i.e. OpenFlow, NetConf/YANG, P4, CLI, etc)

## Slide 15: SENSE End-to-End Orchestration
Three Science Use-cases
  LHC CMS use-case
  NERSC Burst Buffer use-case
  Superfacility use-case

## Slide 16: Instrumentation / Monitoring / Measurements
Feedback to the user / application is critical, but must be in the context of the request, e.g. feedback for a service request should in terms of the service parameters and not low level technology specifics (unless they are part of the service parameters)
Exchange of information between (service) domains for operational support needs to be investigated to understand the level of abstraction (or lack thereof) needed to maintain a domain’s information exchange policy, but still provide useful data
Data mined will be used for system modeling and machine learning to perform capacity predictions and develop strategies for negotiating resources
  This task will collaboratively lead by the SDN NGenIA project

## Slide 17: End-to-End SENSE Testbed
Network,
Storage
Network,
Compute
Network,
Compute,
Storage
Network,
Compute,
Storage
Network,
Storage

## Slide 18: SENSE Deliverables Year 1 (1/2)
3.1.2.1 Resource Information Service
Develop SENOS Resource Information Service module that is compatible with MRML [ESnet – 2Q2016 Final]
3.1.2.2 Resource Computation Service
RCS Architecture and design document [UMD – 2Q2016 Final]
Base RCS SENOS (Resource Computation) Service module implementation [UMD – 4Q2016 Final]
3.1.2.3.1 Multi-Point VPN Service
SENOS Layer 2 (Multi-Domain) Multi-Point Service design document [ESnet – 2Q2016 Final]
SENOS Layer 2 (Multi-Domain) Multi-Point Service module implementation [ESnet – 4Q2016 Update]
3.2.3.1 DTN Auto Configuration
End-System / DTN Auto Configuration Agent requirements and design document [NERSC – 2Q2016 Final]
End-System / DTN Auto Configuration Agent implementation and SENOS-RM integration [CalTech – 4Q2016 Update]
3.2.4 Next Generation Science DMZ
NGScience DMZ architecture and design document [FNAL – 4Q2016 Final]
NGScience DMZ SENOS-RM Base Implementation which provides resource representation to higher level SENOS-O [UMD – 4Q2016 Update]

## Slide 19: SENSE Deliverables Year 1 (2/2)
3.3.1 Network Intent API and Rendering
SENOS OpenFlow NE Driver Service module design document [ESnet – 3Q2016 Final]
SENOS OpenFlow NE Driver Service module implementation [ESnet – 4Q2016 Final]
3.4.1 Global Resource Modeling
Document describing service level abstraction for each resource domain [ESnet – 3Q2016 Final]
Resource modeling exercise for each SENOS- RM domain and SENOS-O instance [All– 4Q2016 Final]
3.4.2 Science Workflow Intent Rendering
LHC CMS workflow use case and requirements document [FNAL– 2Q2016 Final]
Superfacility workflow use case and requirements document [ANL– 2Q2016 Final]
KBase workflow use case and requirements document [NERSC– 3Q2016 Final]
SENOS Big Science Workflow Service module design document [ESnet – 4Q2016 Final]
SENOS Big Science Workflow Service module implementation [ESnet – 4Q2016 Initial]
3.5.1 Feedback across the Intent Based Interface
Requirements document for coherent end-to-end monitoring, measurement, and management of SENOS services [CalTech – 3Q2016 Final]
Architecture and design document for coherent end-to-end monitoring, measurement, and management of SENOS services [CalTech – 4Q2016 Initial]

## Slide 20: Management Plan discussion
Monthly PI meetings: Chin
  Progress, issues
  ½ hr
Quarterly Progress reports in bullets
  Internal, but can be shared to DOE program manager

## Slide 21: Areas of research, and leads
Roles and responsibility
  Software:
    Processes, release mechanism, etc.
  Deployment:
    Deployment of SDN testbed, architecture, timeline
  Science Use-cases & demos:
    Coordination of science use-cases, demos etc.
  Multi-domain orchestration:
    Resource models, design, AA, etc.
  Policies and End-Site Orchestration:
  Site policies, ScienceDMZ automation, end-host automation requirements
  Overall Project Management:
    Work with Thomas, deliverables tracking, reports etc.