## Slide 1: End-Site Orchestration
With Open vSwitch (OVS)
R. Voicu, A. Mughal, J. Balcas, H. Newman for the Caltech Team

## Slide 2: Site Orchestration: Prerequisites
The Caltech team’s earlier work, in OLIMPS and the DYNES and ANSE NSF projects with dynamic circuits, integrated with the CMS PhEDEx and ASO applications used a so-called “FDTAgent” to couple the data transfer nodes (DTNs) at the end-sites running Caltech’s FDT as the high throughput data transfer application
The agent (1) requests the circuit, (2) waits for an answer, (3) configures both end-hosts if the circuit provisioning succeeds, and (4) modifies the local end-host routing including creating VLAN interfaces to use the new circuit. Integrated with PhEDEx
We generalized this to multiple circuits and paths with an OF controller in 2013-15
We clearly needed to move to standard methods of site/regional/wide area integration

## Slide 3
Caltech from ANSE to SDN-NGenIA: Dynamic Circuits with Software-defined path building and load balancing
Dynamic circuits used to create network paths with reserved bandwidth
OF Flow-matching is done on specific subnets to route only the desired data packets to the circuits
Caltech’s controller is used to select paths for the circuits, based on available capacity, load-balancing, etc.
Controller also can be used to load-balance and/or moderate flows over multiple non-circuit paths
In SDN-NGenIA we need to generalize this, and move to production ready tools

## Slide 4: Site Orchestration: Prerequisites
In seeking standard methods of site orchestration, including solving the campus QoS problem in a generally applicable, transfer-protocol independent way, we decided to use Open vSwitch (OVS)
OVS is designed to enable network automation via programmatic interfaces, especially for virtualized environments. It supports standard, well-established protocols for internal management: Security, monitoring, automated control
Huge performance improvements in recent versions (2.x+) made OVS appealing.
  Caltech’s tests showed ~no penalty in performance compared with bare metal
No special requirements: OVS is Included in the standard Linux releases.
Seamless migration: OVS can run on part of a cluster The deployment path can thus be gradual, with no impact on production
  IP reachability and per-formance are the same with or without OVS
www.openvswitch.org

## Slide 5: OVS Benefits: Managing Site Interactions Locally, with Regional and Wide Area Networks
Provides SDN-orchestrated configuration for data flows all the way to end-host, which can be orchestrated from the local/campus SDN controller or brought down from the Regional/WAN controller
Provides QoS and traffic shaping right at the end-point of a data transfer
  QoS via OVS is protocol agnostic: one can use TCP (GridFTP, FDT) or UDP
  Under the hood, OVS uses the TC (Traffic control) part of iproute2 to configure and control the Linux kernel network scheduler
  Helps to achieve better throughput by moderating and stabilizing data flows; e.g. in cases where the upstream switches have limited buffer memory
Monitoring is done with standard sFlow and/or NetFlow protocols
Traffic mirroring: Taps and/or mirroring are required at some sites

## Slide 6: OVS Benefits (2)
SDN-based configuration of the end-host
  OVS is SDN Controller agnostic: will work with any SDN controller which supports OpenFlow and/or OVSDB
      The Open vSwitch Database Management Protocol: RFC 7047
  OVS extends SDN capabilities all the way to the end-host: provides a unified configuration based on the same SDN approach for both the network infrastructure and the end-host
Highly dynamic and flexible security policies
  Makes it possible to replace the standard (iptables) end-host firewall configuration with a more dynamic, flexible approach via the local controller.
  Security control may be unified inside a “centralized” SDN controller where needed

## Slide 7: OVS Open vSwitch Performance Tests
We compared the performance of hardware “bare metal” versus OVS in two cases:
  A bridged network: The physical interface becomes a port in the OVS switch
  Dynamic bandwidth adjustment Through policy at the site egress

## Slide 8: 10GE Performance Tests
Two SandyBridge machines
10GE Mellanox cards (“back-to-back”)
Stock SLC 6.x kernel – Mid2015
Connected via a Dell Z9000

## Slide 9: OVS Dynamic bandwidth adjustment Egress rate-limit 10GE LAN tests
500Mbps
5Gbps
1Gbps
2.5Gbps
7Gbps
10Gbps
NO policy
7.5Gbps
9Gbps
10Gbps
policy
11Gbps
policy
0.5 Gbps
10Gbps
NO policy
4Gbps
Smooth Stable Flows at any rate up to line rate

## Slide 10: OVS 10G LAN tests CPU Utilization
5 Gbps
2.5 Gbps
10 Gbps
NO policy
7.5 Gbps
10 Gbps
policy
11 Gbps
policy
10 Gbps
NO policy
4 Gbps
  Almost the same CPU Usage
  With and without an egress limiting policy in place
Available CPU

## Slide 11: 10G WAN Tests: Over an NSI Circuit
OVS 2.4 with stock kernel Centos6
10G NSI circuit from Caltech to Umich (~60 ms RTT)
Very stable up to 7.5 Gbps
Shaping still good ( 2%) above 8 Gbps

## Slide 12: 100GE Performance Tests (Feb. 2016)
100GE Mellanox NICs; Haswell Machines; Z9100 Switch
Kernel 4.x(4.4.1) EPEL CentOS 7 (Feb 2016) Up to date kernel needed for > 35 Gbps
OVS 2.4 (also via standard EPEL)

## Slide 13: OVS Dynamic bandwidth adjustment Egress rate-limit 100G tests
1 Gbps
40 Gbps
80 Gbps
75 Gbps
10 Gbps
110 Gbps
policy
100 Gbps
NO policy
50 Gbps
90 Gbps
100 Gbps
NO policy
60 Gbps
Smooth Stable Flows at any rate up to line rate

## Slide 14: 100GE OVS Performance Tests CPU Utilization
1Gbps
40Gbps
10Gbps
110Gbps
policy
100Gbps
NO policy
50Gbps
90Gbps
100Gbps
NO policy
80Gbps
CPU Usage:
Penalty for using policy 1% or less
Available CPU
CPU Used: System

## Slide 15: Notes on 100GE Performance Tests
The default kernel and iproute packages in Centos 7 are not suitable for 100GE rates
      Although they work fine up to nearly 40GE rates
Both the kernel and user-space utilities in older kernels suffer from the use of 32-bit rate limit counters, which gives a maximum rate limit of ~35 Gbps (34.360 Gbits/s)
Newer kernels are required (>=3.13): these are available via the “standard” EPEL repositories
Newer `tc` (Traffic Control) utility is also needed
  This is part of the `iproute2` package

## Slide 16: End-Site Orchestration – Site example Northbound interaction with SDN OS
End-hosts automatic discovery: the SDN controlling infrastructure becomes a distributed LS (Lookup Service)
Automatic identification of data flows between pairs of hosts (IPs) which helps with flow steering
The HL services/applications manage the OVS instances via “standard” RESTful NB APIs. The SB protocols + drivers: handled by the SDN controller
Fast prototyping using scripts and/or Python as NB clients

## Slide 17
ODL Controller
OVSDB + OpenFlow
End-Site Orchestration – Site example Southbound interaction with SDN OS
OVSDB – Open vSwitch Database Management (RFC7047)
Used to create the virtual bridges
Virtual bridges can use standard OF to speak with the controller
Normal routing if the controller is down
OVSDB
OpenFlow

## Slide 18: End-Site Orchestration Inter-Site Example Multiple Host Groups, Paths, Policies

## Slide 19: A Few Notes on OVS
As soon as OVS starts (e.g. during OS boot) it will connect to the configured end-site controller
Both major SDN controllers ONOS and ODL support OVSDB
The SDN controller can “speak” both OVSDB and OpenFlow to the OVS instance
OVS offers the means to identify different data flows in a standard approach for SDN since OVS uses OpenFlow
Both sFlow/NetFlow and OF can be used for data flow monitoring
OVS also helps in cases where the network infrastructure at the end-site only partly supports, or does not support OF
OVS can also be used to extend VLANs all the way to the end-host if data flows over VLAN-based “circuits”

## Slide 20: Argonne Mira/Cooley Moving Towards LCFs as a Grid Resource
Mira @ Argonne:
  48 racks PowerPC 1600Mhz
  786,432 processors, and 768 terabytes, 1GByte/core
  Torus network – each node connected with 9 neighbors
Cooley @ Argonne:
  Two 2.4 GHz Intel Haswell E5-2620 v3 processors per node (6 cores per CPU, 12 cores total)
  126 compute nodes
  GPUs: One NVIDIA Tesla K80 (with two GPUs) per node
  384GB RAM per node, 24 GB GPU RAM per node (12 GB per GPU)

## Slide 21: Argonne Mira/Cooley Data Flow Moving Towards Data Intensive LCFs
Supports GridFTP doors, which can be accessed from any GridFTP-enabled end-point – e.g. LHC site
The DTN nodes mount the shared file system (GPFS)
The FS is seen by both Mira and Cooley
FDT can be installed in user space
Overarching requirement in the system design is to make Mira/Cooley appear as a Grid resource (Opportunistic site)
An added field of development for site orchestration using OVS and SDN, targeting the GridFTP doors, then state of the art DTNs